## Slide 1: In situ estimation of effective rock elastic moduli by seismic ambient vibrations Bohemian Cretaceous Basin, Czech Republic
Jozef Müller (jozef.mueller@uni-jena.de)
Jan Burjánek, PhD
(burjanek@ig.cas.cz)

## Slide 2
Goals
Non-invasive ambient noise investigation of rock structures
  In situ estimate of elastic moduli (E, G)
    Competent sandstones at the Konice site
    Ambient noise array measurement
  Study of behaviour and local response of a rock tower
    Kapelník rock tower
    On-site noise measurements and beam theory (using the E, G)

## Slide 3
Study area
Bohemian Cretaceous Basin
  C oniacian sandstones
  Turonian claystones
Subhorizontal strata
  ≈ 1-D model
Red dots: investigated sites
Blue crosses: boreholes

## Slide 4
1) Konice Array Measurement
[Right] Array geometry
Seismometers in shallow pits
Station positions measured with a DGPS
Two hours of 3C ambient noise recordings

## Slide 5
1) Dispersion Curves
Frequency-wavenumber array analysis
  Wathelet et al. (2020)*
[Left] Rayleigh wave dispersion curve
[Right] Love wave dispersion curve
Both represent fundamental modes
*Wathelet, M., Chatelain, J.-L., Cornou, C., Di Giulio, G., Guillier, B., Ohrnberger, M., Savvaidis, A., 2020.
Geopsy: A user-friendly open-source tool set for ambient vibration processing. Seism. Res. Lett. 91, 1878-1889

## Slide 6
1) Inverted Velocity Profiles
[Left] Depth profile of P-wave velocities
[Right] Depth profile of S-wave velocities
P-wave velocities were determined thanks to low Poisson’s ratio and consideration of the Rayleigh wave ellipticity
Expected sandstone-claystone interface in depth of around 80 m
Poor resolution
Poor resolution

## Slide 7
1) Elastic Moduli
Histograms of elastic moduli of the sandstone formation at Konice (15 m to 75 m)
Mean: 1.53 GPa
Mean: 0.59 GPa
Shear modulus
Young’s modulus

## Slide 8
outfanatic.com
Below: result of a particle motion polarisation analysis from recording at the top of the tower
outfanatic.com
2) Kapelník
Kapelník rock tower

## Slide 9
2) Model Eigenfrequencies
Euler-Bernoulli formula for bending of a cantilever beam with a rectangular cross-section
  Young’s modulus
  Density
  Mode coefficient (fund., 1st, 2nd, etc.)
  I, A, H Geometrical parameters of the beam
Why? Investigated rock tower is similar to the beam
Rectangular cross-section yields two eigenfrequencies for each
The eigenfrequencies represent oscillations in two horizontal directions

## Slide 10
2) On-site vs. Calculated Data
[Right] Oscillation frequencies and directions of the Kapelník rock tower and its possible heights based on the frequencies
  Joint results of the on-site data
  (dash-dotted lines)
  Euler-Bernoulli beam formula
  (solid curves)
Frequencies from model and on-site data for match at height of around 36 m
Overground tower height is 32 m
Notes:   Euler-Bernoulli beam formula
  (solid curves)
    The same for 𝐸∗σ𝐸 and 𝐸/σ𝐸 (dotted envelopes)

## Slide 11
Conclusion
Konice
  Non-invasive estimate of effective E and G of competent sandstone strata
Kapelník rock tower
  Successful combination of on-site and model data
  Determination of eigenfrequencies and directionalities of oscillations
  Proof of concept for possible monitoring of other rock structures
Submitted as Müller, J., Burjánek, J., 202X. In situ estimation of effective rock elastic moduli by seismic ambient vibrations (under review)

## Slide 12
Thank You For Your Attention