## Slide 1: Nitrate and Water Isotopes as Tools to Resolve Nitrate Travel Times in a Mixed Land Use Catchment
Christina F. Radtke1, Stefanie R. Lutz², Christin Müller1, Jarno Rouhiainen1, Ralf Merz1, Xiaoqiang Yang3,
Rohini Kumar4, Paolo Benettin5, Kay Knöller1
1 Helmholtz-Centre for Environmental Research UFZ, Department of Catchment Hydrology, Germany
2 Copernicus Institute of Sustainable Development, Utrecht University, the Netherlands
3 Helmholtz-Centre for Environmental Research UFZ, Department of Aquatic Ecosystem Analysis and Management, Germany 4 Helmholtz-Centre for Environmental Research UFZ, Department of Computational Hydrosystems, Germany
5 École Polytechnique Fédérale de Lausanne EPFL, Lausanne, Switzerland

## Slide 2: Background Information
Good
Bad
Problem:
  High nitrate concentrations
  Legacys and time lag
Gain more information about nitrate and flow paths:
  Usage of stable isotopic signatures: δ18O-H2O, δ2H-H2O & δ18O-NO3, δ15N-NO3
Hypotheses:
  Transit times of water and nitrate vary during changing hydrological conditions
  Decoupling of nitrate transit times and water transit times
    Nitrate is younger than water
Chemical state of groundwater bodies in Germany

## Slide 3: Methods
Mesoscale Hydrological Model Nitrate1
  Water fluxes (ET,P,Q,Leaching)
  Nitrate concentrations (in Leaching, Q)
Modified tran-SAS2
  Based on isotopic signatures: δ18O
  To simulate transit times and age
  Modifications:
    Second storage for biogeochemical processes
    Processes: nitrification, denitrification
Meisdorfer Sauerbach (11.5 km²)
  Isotope data
    Precipitation: Stream: 2013-2017 monthly, 2017-2019 biweekly, 2017-2020 daily 2019-2020 daily
1 Yang, X., & Rode, M. (2020). A Fully Distributed Catchment Nitrate Model - mHM-Nitrate v2.0. Zenodo. doi:10.5281/zenodo.3891629
2 Benettin, P., & Bertuzzo, E. (2018). tran-SAS v1.0: a numerical model to compute catchment-scale hydrologic transport using StorAge Selection functions. Geoscientific Model Development, pp. 1627-1639.

## Slide 4: Methods: laboratory
Water isotopes
Water sample filtration (0.45 µm)
Picarro L1120-I analyser based on laser spectroscopy
standard deviation of ± 0,6 ‰VSMOW for δ2H and ± 0,2 ‰VSMOW for δ18O
Nitrate isotopes and nitrate concentration
Water sample filtration (0.45 µm)
denitrifier method with bacteria strains of Pseudomonas chlororaphis was used for the measurement of isotopic composition of dissolved nitrate
Nitrate isotope analysis with mass spectrometer DELTA V Plus in combination with a GasBench II from Thermo Scientific
the analytical precision for nitrogen and oxygen isotope measurements of nitrate are 0.4 and 1.6 ‰, respectively, international standards (USGS32, USGS34, USGS35 and IAEA NO3) were applied for calibration
nitrate concentration was measured by ion chromatography with a Dionex ICS-2000 combined with AS50

## Slide 5: Conceptual model tran-SAS-nitrate
5
ET
Infiltration layer
Routing storage
P
SAS : StorAge Selection Functions
P : Precipitation [mm] &
ET : actual Evapotranspiration
L : Leaching [mm], Nitrate concentration[mg/l] &
Q : Discharge [mm] &
ONO3 : Oxygen fractions (16O and 18O)
pNO3 : Age distribution of nitrate
e(-k) : Denitrification with denitrification rate k; k16O > k18O
L H2O & NO3
SAS
ET
Q H2O & NO3
Water
Water & Nitrate
SAS
SAS
SAS

## Slide 6: Model description
Assumptions:
  no interflow from infiltration layer
  Nitrate from microbial activity is formed by entering the routing storage (Age 1) with isotopic signature
  δ18O-O2 is defined with 23.5 ‰ (Kendall et al. 1998)
  Denitrification happens only in routing storage
  No intermediates during biogeochemical processes are considered
  No more interaction with surrounding oxygen
Isotope fractionation during denitrification is considered
Description:
  Water fluxes (in this case modelled by mHM-nitrate) with it‘s isotopic signatures are inputs for the model as well as nitrate concentration (modelled by mHM-nitrate)
  Isotopic signature δ18O is used as fingerprint for dating
  With storage selection functions (SAS) the release of water isotopes and nitrate isotopes is controlled
  The model is calibrated against measured isotopic signatures of water in stream
  The model could also be set up with measured data if available, but in our case we didn‘t had all necessary measurements

## Slide 7: Data

## Slide 8: Water isotopes: Age distribution in stream Meisdorfer Sauerbach KGEδ18O =0.33

## Slide 9: Water isotopes: Age distribution in stream Meisdorfer Sauerbach
Comparing discharge since 2013 with discharge in 2018 and the following years we can see that discharge peaks are lowered by more than 50 %, therfore we are talking about dry conditions already since 2018
In 2018 the proportion of old water from groundwater bodies is higher than the proportion of old water during discharge peaks in 2019 and 2020
The fraction of young water, either event water (<7days) or water up to 2 months old is higher during dry conditions compared to wetter periods until 2018
We assume it may be that there is a lowered connectivity between surface water and groundwater due to prolonged dry conditions
 | water age contribution [%] |  |  |  | 
Year | > 7 days | > 14 days | > 28 days | > 60 days | > 180 days
2017 | 0.187 | 0.253 | 0.309 | 0.375 | 0.486
2018 | 0.061 | 0.088 | 0.129 | 0.208 | 0.388
2019 | 0.143 | 0.201 | 0.260 | 0.329 | 0.447
2020 | 0.144 | 0.208 | 0.266 | 0.337 | 0.450

## Slide 10: Nitrate isotopes in stream
Range of values for denitrification rate as well as fractionation factor are gained from literature (Granger & Wankel, 2016)
A fixed value over time is set for denitrification rate k of δ16O, with a fix fractionation factor α over time the k of δ18O is achieved; both values are visually compared to measured isotopic signature of δ18O-NO3 in stream
The grey interval shows all possible combinations of the whole range of denitrification rates and fractionation factors, while the black line shows the average matching observed isotopic signatures
The intensity of denitrification is controlled by transit times in the routing storage at the release of water and nitrate to the stream

## Slide 11: Water and nitrate isotopes Transit times
Water TT
Nitrate TT
Nitrate is ∅ 41 days younger than water in the Meisdorfer Sauerbach catchment
Difference higher during spring an summer: younger nitrate in spring and summer caused by higher microbial activity and nitrification due to higher temperatures, older water due to drier climate conditions
Autumn lowest: caused by water availability which is higher during autumn and newly applied fertilizer (in Germany there are periods during summer where it‘s not allowed to apply fertilizer)

## Slide 12: Discussion
Transit times of water are higher compared to transit times of nirate
  Decoupling: Flow paths of water, that does not transport nitrate (e.g. forested area)
More young water fractions during dry years – Why?
  Precipitation falls on fast responding areas (e.g. drainage dominated areas) in catchment → Bypass of old water
  Domininant surface runoff due to soil which was drying out
Highfrequency data is necessary compared to monthly/biweekly data
Complex regional and geological characteristics in Meisdorfer Sauerbach catchment
Plan: Apply model to other catchments

## Slide 13: Thank you for your attention!
Thank you for your attention!
Contact: christina.radtke@ufz.de