## Slide 1
Shi Huang, Yongqiang Yuan, Keke Zhang, and Xingxing Li
2022.5.26
Geocenter motions derived from BDS
School of Geodesy and Geomatics, Wuhan University

## Slide 2
Overview
We focus on the solar radiation pressure (SRP) models of BDS satellites to improve the BDS-derived geocenter coordinates (GCC).
The impact of SRP modeling on GCC
The contribution of IGSO satellites in GCC estimation
The correlations between GCC-Z and SRP parameters
The comparison to the external GNSS and SLR solutions
Method
Background
Result
Summary
Navigation: Click buttons for more information

## Slide 3
Background
Determination of Geocenter coordinates (GCC)
Fig. 1 Definition of GCC.
The GCC is defined as the vector offset of CM relative to CF
Precise determination of the instantaneous GCC is one of tasks of geodesy, and is important for the geophysical interpretation of geodetic measurements
Z
X
Y
ITRF
GCC
CF
CM

## Slide 4
BDS constellation:
7 Geostationary Earth Orbit
(GEO) satellites
10 Inclined Geosynchronous Orbit
(IGSO) satellites
27 Medium Earth Orbit
(MEO) satellites
Background
Fig. 2 Schematic diagram of BDS constellation.
http://www.csno-tarc.cn
BeiDou Navigation Satellite System (BDS)
BDS-3 has been completed in June 2020.
As a member of GNSS, BDS has the ability to determine the GCC independently

## Slide 5
Method
Fig. 3 The distribution of stations, and the color of the dot indicates the station’s priority
Strategy
SRP models used in this study:
The Empirical CODE Orbit Model (ECOM) with 5 parameters
The extended ECOM (ECOM2) with 9 parameters
Adjustable box-wing model (ABW)
A maximum of 130 globally homogenous IGS/iGMAS stations during the period 2019-2021 were selected as shown in Fig. 3:
The geocenter coordinates (GCC) are determined together with the satellite orbits, station coordinates, troposphere parameters and Earth rotation parameters

## Slide 6
Time series of GCC-Z derived from BDS
Results
ECOM case
In MEO solution, the annual signal with an amplitude of 84.6 mm takes great domination
The inclusion of IGSO reduced the amplitude of annual signal by 27.8%
Fig. 5 Time series (left) and spectrum analysis (right) of GCC-Zs derived separately from MEO, IGSO+MEO satellites of BDS with respect to the SLR-based solution provided by ILRS.

## Slide 7
Time series of GCC-Z derived from BDS
Results
ECOM2 case
In MEO-only solutions, the switch from ECOM to ECOM2 model reduces the amplitude of the annual signal by a factor of 2.5 (from 84.6 mm to 33.5 mm).
After the inclusion of IGSO, the signals of 1, 2, 3 cpy (cycle per year) have decreased by a factor of 1.5, 7.8, 2.5 respectively.
Fig. 5 Time series (left) and spectrum analysis (right) of GCC-Zs derived separately from MEO, IGSO+MEO satellites of BDS with respect to the SLR-based solution provided by ILRS.

## Slide 8
Time series of GCC-Z derived from BDS
Results
ABW case
In the MEO-only solutions, the ABW model appears to reduce the amplitude of annual signal by factors of 5.4 and 2.1 with respect to ECOM and ECOM2 models.
The inclusion of IGSO largely reduces the annual signal by a factor of 2.8 (from 15.6 mm to 5.5 mm). Also, the dominant 3 cpy signal is significantly improved, dumping from 29.3 mm to 16.1 mm.
Fig. 5 Time series (left) and spectrum analysis (right) of GCC-Zs derived separately from MEO, IGSO+MEO satellites of BDS with respect to the SLR-based solution provided by ILRS.

## Slide 9
Analysis of formal errors
Results
Fig. 6 Time series of formal error of the GCC-Z in mm.
The time series of formal errors of GCC-Z shows a tendency towards lower due to the increasing number of observations of BDS during this time period
The inclusion of IGSOs decreases the averages of formal errors by 16.5%, 22.0% and 13.4%, the STDs are also reduced by 38.2%, 36.2% and 28.6% for the ECOM, ECOM2 and ABW solutions respectively.

## Slide 10
Correlations between GCC-Z and SRP parameters
Results
Fig. 8 Correlations between the GCC-Z estimate and the SRPs in July 1, 2020. The correlations of satellites in the same orbital plane is averaged.
For the ECOM and ECOM2 cases,
the GCC-Z is correlated with
Fig. 9 Time series of GCC-Z separately obtained by estimation and reconstruction using the formula above, and the grey lines represent the absolute difference between them.

## Slide 11
Correlations between GCC-Z and SRP parameters
Results
Fig. 8 Correlations between the GCC-Z estimate and the SRPs in July 1, 2020. The correlations of satellites in the same orbital plane is averaged.
For the ABW case,
the GCC-Z is correlated with
and are similar to and in ECOM/ECOM2 model, for both of them might bring an non-zero out-of-plane acceleration which will disturb the GCC-Z estimation
The physical model with prior optical information helps de-correlating the SRP parameters and the GCC-Z

## Slide 12
Comparison to external solutions
Results
Fig. 9 Amplitudes and phases of the annual signals
Fig. 10 Time series of three components of GCC estimates derived from IGSO+MEO of BDS.
Difference of SRP modeling and inclusion of IGSO satellites have little impact on the annual signals of X and Y components of GCC.
IGSO+MEO solution using ABW model is in the best agreement with CODE and ILRS solutions.

## Slide 13
Summary
Compared to ECOM and ECOM2 models, the ABW model is more suitable for BDS to determine the GCC;
The inclusion of IGSO satellites can reduce the MEO-specific signal and the annual signal of GCC-Z series;
The time series of GCC derived from MEO and IGSO satellites of BDS using ABW model is in the best agreement with CODE and ILRS solutions.

## Slide 14
Thanks！