## Slide 1: Topographic analysis of debris flow gullies affected by tectonic activities on the edge of Qinghai-Tibet Plateau
Institution: Institute of Mountain Hazards and Environment,CAS
Reporter: Xinyue Liang
Time: 2022.05.26
EGU22-6857

## Slide 2
1.Background
2.Method
3.Result
4.Conclusion
Yang J, Kaus B, Li Y, Leloup P, Popov A, Lu G, Wang K, Zhao L*. Lower crustal rheology controls the development of large offset strike-slip faults during the Himalayan-Tibetan orogeny [J]. Geophysical Research Letters, 2020, 47: e2020GL089435.
Earthquake activity is frequent
Large number of Holocene faults
Extrusion deformation on surrounding region
Tectonic features of the Qinghai-Tibetan Plateau
（Yang, et al）

## Slide 3
1.Background
2.Method
3.Result
4.Conclusion
Mainly concentrated on the edge of the Qinghai-Tibet Plateau
Zonality, relative concentration and group-occurring
It is distributed around strong earthquakes
There is a linear distribution along the fault
Sanyanyu Gully
Jiangjia gully
Guxiang gully
Cutou gully
Spatial characteristics of Debris flow
Debris flow on the active fault belt
Destructive
Sudden
Rapid
Characteristics

## Slide 4
Bibili gully
Tianmo gully
1.Background
2.Method
3.Result
4.Conclusion
Internal and External Dynamics of Debris Flow Formation
Jiangjia gully
Source area
sedimentary area
circulation area
The development of debris flow is affected by geology, geomorphology and climate.
Identify debris flow types and explore formation mechanisms
The process of surface runoff and the supply of material sources
Susceptibility of debris flow
Debris flow classification
Formation conditions
Gully morphology
Material composition
Hazard level
……
Material, water
hillslope, valley
Viscous, diluted, transitional
Scale volume, economic loss
……

## Slide 5
Study area
Landform
Deposition
Barrage lake
sediment thickness measurement
Vegetation biodiversity survey
UAV measuring terrain
Underwater terrain survey
Yarlung zangbo river
Nu River
Xiao River
…
Field investigation
1.Background
2.Method
3.Result
4.Conclusion

## Slide 6
1.Background
2.Method
3.Result
4.Conclusion
Parameter | Formula | Interpretation
Area (A) | \ | The larger area, the greater possibility of providing loose material.
Slope (S) |  | H is the vertical height, the horizontal length, S is the average slope of gully.
Length of main river (L) | \ | The longer main gully, the more loose debris is accepted and transported.
Gradient（G） |  | is the elevation change， is the length change. Gradient reflects the hydrodynamic conditions and material transport capacity of debris flow.
Relative altitude (RA) |  | is the highest and lowest elevation in gully. RA indicates river incision and surface denudation.
Ratio of form (Rf) |  | Rf reflects the hydrodynamic conditions of the gully.
Hypsometric curve (HI) |  | is average elevation. HI Reflects the stage of gully evolution.
Shape of the longitudinal profile of gully (N) |  | N reflects the developmental topographic conditions and can be divided into young, prime and old age.
gully density (GD) |  | The greater density of gullies, the more unstable surfaces and the weaker the slope stability.
fractional vegetation cover (FVC) |  | Usually the vegetation cover higher, the more stable the slope.
Parameter | Formula | Interpretation
Area (A) | \ | The larger area, the greater possibility of providing loose material.
Slope (S) |  | 
Length of main river (L) | \ | The longer main gully, the more loose debris is accepted and transported.
Gradient（G） |  | 
Relative altitude (RA) |  | 
Ratio of form (Rf) |  | Rf reflects the hydrodynamic conditions of the gully.
Hypsometric curve (HI) |  | 
Shape of the longitudinal profile of gully (N) |  | N reflects the developmental topographic conditions and can be divided into young, prime and old age.
gully density (GD) |  | The greater density of gullies, the more unstable surfaces and the weaker the slope stability.
fractional vegetation cover (FVC) |  | Usually the vegetation cover higher, the more stable the slope.
Stream length-gradient index
Hack, 1973
Reflecting tectonic activities differences of local sections in medium-small scale
Main factors of debris flow
Hydraulic characteristic
Stream power index(SPI)：
Topographic wetness index (TWI)：

## Slide 7
𝐸_𝑖 indicates that the greater the degree of variation in the value of the indicator, the greater the amount of information provided
1.Background
2.Method
3.Result
4.Conclusion
Nonmetric multidimensional scaling(NMDS)
Calculation of dissimilarity δij between debris flow gullies by Euclidean distance
Nonparametric tests
Infer whether the median or distribution pattern of samples from multiple aggregates is differentially significant.
Significance tests of geomorphic factors for different types of debris flow gullies.
weight
where ,
Entropy weight
Fuzzy Mathematics
Fuzzy mathematics is a method of evaluation based on multiple variables, and is a way to delineate fuzzy boundaries between things in terms of affiliation.
，， is boundary values of each level.
The entropy method is an objective assignment method that uses information entropy to calculate the entropy weight of each index, and the weight of each index is corrected by the entropy weight
Unconstrained sorting
reduction dimension
classification
Threat strength coefficient is used to measure the goodness of two-dimensional sorting points fitting the original entity :
Fuzzy Mathematics
Information entropy
𝐸𝑖 shows that the greater the variability of indicators, the more information they provide
Notes: 由于NMDS是一种非约束排序的分类方法，利用数据的相似性将多维简化到低维进行定位和归类。泥石流受到多种因素的影响，复杂的非线性结构，因此NMDS可用来划分泥石流类型。非参数检验可用于判断泥石流类型是否存在显著的差异性，熵权法与模糊数学结合可用于对泥石流的易发性进行评价。
泥石流因子与泥石流规模量还未确切地量化关系
使用胁强系数来衡量二维排序点拟合原始实体的优度：
Calculation of debris flow gully using euclidean distance in two - dimensional space
推断样本来自多个总体的中位数或者分布是否存在差异性显著。
用于不同类型泥石流沟地貌因子显著性检验。
𝑠_1，𝑠_2，𝑠_3为每个等级的节点
模糊数学是根据多变量对事物进行评价的一种方法，是以隶属度划分事物之间的模糊界限。
𝐸_𝑖表明指标值得变异程度越大，提供的信息量越多
熵值法是一种客观赋权的方法，利用信息熵计算出各指标的熵权，通过熵权对各指标的权重进行修正

## Slide 8
1.Background
2.Method
3.Result
4.Conclusion
Impact of tectonic activities on debris flow group
Debris flow group is mainly distributed in the largest gradient of main river
Significant differences of tectonic activity between upstream and downstream within the seven basins
Debris flow group is distributed in the strongest tectonic uplift in main river

## Slide 9
1.Background
2.Method
3.Result
4.Conclusion
Debris flow is divided into three types by NDMS
Type I: rainstorms in exposed bedrock areas.
TypeII : glaciers in exposed bedrock areas.
Type III: rainstorms in depositional areas.
Debris flow gully classification
Type I
Type II
Type III
Three types of debris flow topography have obvious indigenous differences

## Slide 10
1.Background
2.Method
3.Result
4.Conclusion
Characteristics of the three types of debris flow fans
Morphological characteristics of debris flow fan
Characteristics of particle size distribution on debris flow fan
Type I and II hydraulic capacity is large, and its carrying particles are large
Type III debris flow have weak erosion force and carry small particles

## Slide 11
1.Background
2.Method
3.Result
4.Conclusion
Evaluation of debris flow scale
Scale：
Factor Weight of Three Types of Debris Flow
Entropy Weight Method - Fuzzy Mathematics
Type1: middle scale
Type2: large scale
Type3: low scale
Spatial distribution of debris flow scale evaluation
weight

## Slide 12
1.Background
2.Method
3.Result
4.Conclusion
Seven typical basins on the edge of the Qinghai-Tibetan Plateau were classified into three categories: rainstorms in exposed bedrock areas (Type I ), glaciers in exposed bedrock areas (Type II ), rainstorms in depositional areas (Type III).
The difference between type II and type III is greater than that between type I and type II.
Type I is mainly small and middle-scale debris flow, Type III is small-scale debris flow, and Type II has a greater possibility of large-scale debris flow.

## Slide 13: Thank you for your attention