## Slide 1: Spatiotemporal Analysis of the Causes and Effects of Wildfire by Satellite Imagery and in situ Data: Case studies of Taiwan and California, USA
Date: 2022/05/24
Yu-Jen Tung1 and Christina W. Tsai2
1 Research Assistant, Department of Civil Engineering, National Taiwan University, Taiwan
2 Distinguished Professor, Department of Civil Engineering, National Taiwan University, Taiwan
E-mail: r09521307@ntu.edu.tw, cwstsai@ntu.edu

## Slide 2: Table of Contents Introduction 01 Results and Discussions 03 Methodology 02 Conclusions and Ongoing Works 04
Study Areas
Objectives
Framework
Data Acquisition
Time Frequency analysis
Multi-dimensional Complementary Ensemble Empirical Mode Decomposition (MCEEMD)

## Slide 3: 01 Introduction
Study Areas, Objectives, Framework, Data Acquisition

## Slide 4: Study Area
California, USA
(Vegetation classification and mapping)
Taiwan
Northeast monsoon
(winter)
Southwest monsoon
(summer)
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works
Focus on 4 regions
Investigate the whole Taiwan.
Little research on wildfire issues.
Diverse topography
2 Monsoons affect rainfall seasons.

## Slide 5: Study Area
 | California, USA | Taiwan
Area | 423,970 km2 | 36,197 km2
Climate Types | (Coastal) warm-summer Mediterranean climate (Southwestern) subtropical semi-arid or steppe climate (Southeastern) hot arid climate | Tropical Climate
Precipitation | 350~2500 mm | 2500 mm
Wind | Santa Ana winds | seasonal monsoon typhoons (tropical cyclones)
Forest Coverage | 30.84% (USA) | 60.71%
Nature-Caused Wildfire | 10-15% | 2%
Anthropogenic activities | Firearms and explosives use | Burning paper money
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works

## Slide 6: Objectives
To investigate the trend and the variability of wildfire occurrences time series, by using a time-frequency tool, Complementary Ensemble Empirical Mode Decomposition (CEEMD).
To identify the wildfire influence on forest vegetation distribution, detected by satellite image time-series data, through multi-dimensional Complementary Ensemble Empirical Mode Decomposition (MCEEMD). To compare the variation of the wildfire occurrences trend and influence in Taiwan and California, USA.
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works

## Slide 7: Framework
causes
consequences
Dry weather
Soil moisture
Air pollution
Wildfire occurrences
High temperature
Forest recovery
Forest burnt
Official records
MCEEMD/ CEEMD
TDIC
IMFs
Trends/ Variability
Satellite image time series (SITS)
Study area:
Taiwan
Study area:
California, USA
Comparison
Spatiotemporal Analysis
Health impacts
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works

## Slide 8
 | Variables | Sources | Data Duration | Frequency | Resolution/ Scale | Indices | Analysis Methods | Objective
Wildfire Occurrences | Occurrence Time series | MTBS (US), Forestry Bureau (TW) | 1984~2020 (US), 2010~2021 (TW) | daily | - | Times, Burnt area | CEEMD | -
Burnt Area | Vegetation Cover | Landsat series MODIS | 1984~2021 2000.03~2021 | Yearly Monthly | 30 m 0.1 degrees | NDVI | MCEEMD | Forest Recovery
Anthropogenic Activity | Religious activities (Taoism) | National Religion Information Network | 2010~2021 (TW) | daily | - | - | CEEMD | Occurrence
Meteorological Variables | temperature | Climatology Lab (US), TCCIP (TW) | 1979~2021 (US), 1960~2020 (TW) | daily | ~4-km, 1 km | - | MCEEMD | Occurrence
 | precipitation | Climatology Lab (US), TCCIP (TW) | 1979~2021 (US), 1960~2020 (TW) | daily | ~4-km, 1 km | Rainfall intensity, SPI | MCEEMD | Occurrence
 | Humidity | Climatology Lab (US), TCCIP (TW) | 1979~2021 (US), 1980~2020 (TW) | daily | ~4-km, 2 km | Relative humidity | CEEMD/ MCEEMD | Occurrence
 | Soil Moisture | Climate Data Store | 2006~2020 (US) | monthly | 0.25 degrees | - | CEEMD/ MCEEMD | Occurrence
 | El Niño | BOM (au), NOAA | 1984~2021 | monthly | - | SOI, ONI | CEEMD | Occurrence
Air pollution | PM2.5, PM10 | EPA (US), EPA (TW) | 2000~2020 (US), 2010~2021 (TW) | daily | - | - | CEEMD | Impact area/ Health impacts
Health Impacts | ED contact/ Hospitalizations | Ministry of Health and Welfare (TW) | 2000~2018 (TW) | - | - | - | CEEMD | Health impacts
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works

## Slide 9: 02 Methodology
Multi-dimensional Complementary Ensemble EMD

## Slide 10: Empirical mode decomposition (EMD)
A data-driven technique: the basis functions are derived from the signal itself
Analyzing data from nonstationary and nonlinear processes
A local and adaptive method
Instantaneous frequency
Intrinsic mode functions (IMFs)
Multi-dimensional EEMD
Wu and Huang
EMD
Huang et al.
Complementary Ensemble EMD
Yeh et al.
2009
2010
1998
Ensemble EMD
Wu and Huang
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works

## Slide 11: Empirical mode decomposition (EMD)
Empirical mode decomposition
Multi-dimensional Complementary Ensemble Empirical Mode Decomposition (MCEEMD)
Huang et al. (1998)
Lin (2020)
Trend : extrema <=1
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works
IMFs
Sifting process of EMD

## Slide 12: 03 Results and Discussions
Time Frequency analysis:
California, USA
Taiwan

## Slide 13: California, USA
Wildfire severity
Causes:
  Precipitation
  Relative Humidity
  Temperature
Effects:
  Vegetation Cover
  Soil Moisture
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works

## Slide 14: Time Frequency analysis of Wildfires in California
IMF | (days) | (yrs)
1 | 5.7 | 0
2 | 12.5 | 0
3 | 31.3 | 0
4 | 87.8 | 0
5 | 183.6 | 1
6 | 363.8 | 1
7 | 861.9 | 2
8 | 1975.4 | 5
9 | 4004.1 | 11
10 | 11566.9 | 32
Wildfire Severity 1984~2020 (daily)
Severity (ha/day) burnt area/ day
Characteristic timescale The timescale of high energy IMFs
Distribution of wildfire in California
IMFs/ characteristic timescale of wildfire time series in California
Energy concentration
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works

## Slide 15: Time Frequency analysis of Wildfires in California
IMF | Sierran |  | North Coast |  | Central Coast |  | South Coast | 
 | (days) | (yrs) | (days) | (yrs) | (days) | (yrs) | (days) | (yrs)
1 | 6.0 | 0 | 7.1 | 0 | 6.2 | 0 | 6.5 | 0
2 | 14.1 | 0 | 14.9 | 0 | 16.2 | 0 | 18.0 | 0
3 | 34.4 | 0 | 35.9 | 0 | 38.6 | 0 | 43.3 | 0
4 | 82.8 | 0 | 95.2 | 0 | 97.2 | 0 | 88.7 | 0
5 | 175.5 | 0 | 206.1 | 1 | 206.5 | 1 | 189.5 | 1
6 | 365.3 | 1 | 405.0 | 1 | 423.7 | 1 | 416.0 | 1
7 | 936.7 | 3 | 882.1 | 2 | 1023.9 | 3 | 1092.2 | 3
8 | 1838.4 | 5 | 2006.8 | 5 | 2207.0 | 6 | 2470.8 | 7
9 | 4714.2 | 13 | 3999.0 | 11 | 5317.0 | 15 | 5332.3 | 15
10 | 9064.2 | 25 | 11636.6 | 32 | 10228.0 | 28 | 10131.8 | 28
Wildfire Severity 1984~2020 (daily) (i.e., burnt area)
Trend of wildfire in 4 selected California regions
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works

## Slide 16: Time Frequency analysis of Wildfires in California-Causes
mean
Standard
Deviation
2019
Precipitation(mm) 1979~2021 (daily)
Evolution of the variable
TrendCEEMD = Rn(2019) – Rn(1979)
Evolution of precipitation
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works
More precipitation
Higher variability
decrease

## Slide 17: Time Frequency analysis of Wildfires in California-Causes
Standard
Deviation
mean
Mean Relative Humidity (%) 1979~2021 (daily)
Evolution of the variable
TrendCEEMD = Rn(2019) – Rn(1979)
Evolution of Humidity
2019
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works
Higher
Stable
Unstable
decrease

## Slide 18: Time Frequency analysis of Wildfires in California-Causes
2019
Standard
Deviation
mean
Mean Temperature (oC) 1979~2021 (daily)
Evolution of the variable
TrendCEEMD = Rn(2019) – Rn(1979)
Evolution of temperature
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works
Increase
Low temperature
Stable

## Slide 19: Time Frequency analysis of Wildfires in California-Effects
2011
2021
Vegetation Cover Analysis 2001~2021 (monthly)
NDVI (Normalized Difference Vegetation Index) (MODIS)
Evolution of the variable
TrendCEEMD = Rn(T) – Rn(2001)
mean
Standard
Deviation
Higher coverage rate
Higher variability
Increase
decrease
Evolution of NDVI
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works

## Slide 20: Time Frequency analysis of Wildfires in California-Effects
mean
Standard
Deviation
Soil Moisture (%) 2006~2020 (monthly)
Evolution of the variable
TrendCEEMD = Rn(T) – Rn(2006)
2011
2016
Evolution of NDVI
Higher moisture
decrease
decrease
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works
Unstable

## Slide 21: Taiwan
Wildfire severity
Causes:
  Precipitation
  Relative Humidity
  Temperature
  Religious activities
Effects:
  Vegetation Cover
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works

## Slide 22: Time Frequency analysis of Wildfires in Taiwan
IMF | (days) | (yrs)
1 | 4.9 | 0
2 | 10.5 | 0
3 | 23.2 | 0
4 | 50.7 | 0
5 | 116.7 | 0
6 | 258.6 | 1
7 | 490.1 | 1
8 | 1517.5 | 4
Wildfire Severity 2010~2021 (daily)
Severity (ha/day) burnt area/ day
Characteristic timescale The timescale of high energy IMFs
IMFs/ characteristic timescale of wildfire time series in Taiwan
Distribution of wildfire in Taiwan
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works
Energy concentration

## Slide 23: Time Frequency analysis of Wildfires in Taiwan-Causes
2010~2021 The causes of Wildfire occurrence in Taiwan | 
Littering cigarette butts | 8%
Other Anthropogenic effects | 13%
garbage burning | 13%
Accidental use of fire in mountain activities | 15%
Inadvertent use of fire in folk rituals | 11%
deliberate arson | 10%
under investigation | 0%
Farmland set fire accidentally | 28%
Natural factors such as lightning strikes | 3%
Chart: 2001.12~2020.12 The causes of Wildfire occurrence in Taiwan
| Anthropogenic-Caused | Under Investigating | Lightning-Caused
 | 0.84149 | 0.13869 | 0.019814
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works

## Slide 24: Time Frequency analysis of Wildfires in Taiwan-Causes
2020
mean
Standard
Deviation
Precipitation (mm) 1960~2020 (daily)
Evolution of the variable
TrendCEEMD = Rn(2020) – Rn(1960)
Evolution of precipitation
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works
Increase
More precipitation
Higher variability

## Slide 25: Time Frequency analysis of Wildfires in Taiwan-Causes
Mean Relative Humidity (%) 1980~2020 (daily)
Evolution of the variable
TrendCEEMD = Rn(2020) – Rn(1980)
mean
Standard
Deviation
2020
Evolution of Humidity
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works
Very wet
unstable
Decrease

## Slide 26: Time Frequency analysis of Wildfires in Taiwan-Causes
Mean Temperature (oC) 1960~2020 (daily)
Evolution of the variable
TrendCEEMD = Rn(2020) – Rn(1960)
mean
Standard
Deviation
2020
Evolution of Temperature
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works
hottest
unstable
Decrease
Increase

## Slide 27: Time Frequency analysis of Wildfires in Taiwan-Causes
Religious activities (Taoism) 2010~2021 (daily)
Times of Taoism activities in Taiwan
IMF | (days) | (yrs)
1 | 4.6 | 0
2 | 8.7 | 0
3 | 20.1 | 0
4 | 43.7 | 0
5 | 152.8 | 0
6 | 311.1 | 1
7 | 623.7 | 2
8 | 1576.4 | 4
Times of Taoism activities
Timescale Identification
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works

## Slide 28: Time Frequency analysis of Wildfires in Taiwan-Effects
2011
2021
Vegetation Cover Analysis 2001~2021 (monthly)
NDVI (Normalized Difference Vegetation Index) (MODIS)
Evolution of the variable
TrendCEEMD = Rn(T) – Rn(2001)
Evolution of NDVI
mean
Standard Deviation
Higher coverage rate
Low variability
decrease
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works

## Slide 29: Time Frequency analysis of Wildfires in Taiwan
Intensity: burnt area/ hr
Duration: 1, 2, 3, 6, 12, 24 hours
Frequency (return period): 2, 5, 10, 25, 50, 100 years
Chart: Intensity-Duration-Frequency (IDF) Curve of Anthropogenic-Caused Wildfire Events in Taiwan
| 1 | 2 | 3 | 6 | 12 | 24
2 yr | 0.44166 | 0.68249 | 0.25767 | 0.34622 | 0.11726 | 0.090936
5 yr | 0.80814 | 1.2695 | 0.44581 | 1.0005 | 0.25715 | 0.14887
10 yr | 1.0805 | 1.5035 | 0.54616 | 1.8714 | 0.37955 | 0.18161
25 yr | 1.4477 | 1.6574 | 0.64351 | 3.874 | 0.567 | 0.21605
50 yr | 1.7288 | 1.7071 | 0.69689 | 6.3705 | 0.72696 | 0.23681
100 yr | 2.0273 | 1.7281 | 0.73921 | 10.3792 | 0.91185 | 0.25485
6 hr
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works
 | 1 | 2 | 3 | 6 | 12 | 24
mean | 0.51 | 0.73 | 0.26 | 0.76 | 0.17 | 0.09
SD | 0.48 | 0.60 | 0.18 | 1.09 | 0.13 | 0.06
Cs | 2.17 | 0.80 | 0.86 | 1.68 | 0.74 | 0.06

## Slide 30: 04 Conclusions and Ongoing Works

## Slide 31: Conclusions-California
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works
Variables |  |  | Sierran | North Coast | Central Coast | South Coast
Causes | Precipitation | Mean | High | High | High | High
 |  | SD | High | High | High | High
 |  | Trend | Decrease↓ | Decrease↓ | - | -
 | Relative Humidity | Mean | - | - | - | -
 |  | SD | High | High | - | -
 |  | Trend | Decrease↓ | - | - | -
 | Temperature | Mean | Low | Low | - | -
 |  | SD | - | Low | Low | Low
 |  | Trend | - | - | - | -
Effects | Vegetation Cover | Mean | High | High | - | -
 |  | SD | High | High | High | -
 |  | Trend | Increase↑ | - | Decrease↓ | Decrease↓
 | Soil Moisture | Mean | High | High | - | -
 |  | SD | - | - | High | -
 |  | Trend | - | - | - | Decrease↓
Distribution of wildfire in California
Sierran
South Coast
Central Coast
North Coast

## Slide 32: Conclusions-Taiwan
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works
Variables |  |  | Mountain | Other
Causes | Precipitation | Mean | High | -
 |  | SD | High | 
 |  | Trend | - | -
 | Relative Humidity | Mean | High | -
 |  | SD | High | -
 |  | Trend | - | -
 | Temperature | Mean | Low | High
 |  | SD | - | -
 |  | Trend | - | -
Effects | Vegetation Cover | Mean | High | Low
 |  | SD | Low | High
 |  | Trend | - | -
Distribution of wildfire in Taiwan

## Slide 33: Conclusions
Both in the cases of wildfire in Taiwan and California, the increasing tendency was indicated by CEEMD.
After analyzing the evolution of potential cause and effect factors, the following hypotheses can be proposed：
  The probability of wildfire occurrences in north California is positively correlated to precipitation and relative humidity.
  The probability of wildfire occurrences in Taiwan’s mountain areas is correlated to meteorological factors (precipitation, relative humidity, and temperature).
  The probability of wildfire occurrences in Taiwan’s non-mountain areas is affected more by human activities.
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works

## Slide 34: Ongoing works
Evaluating public health potential harm by utilizing a medical database in Taiwan.
Developing the correlation between wildfire events and other factors by TDIC/ TDICC.
Establishing risk maps of wildfire occurrences of Taiwan and California, USA.
Contact us
Conference poster:
  Tung, Y.-J and Tsai, C. W. (2022): Spatiotemporal Analysis of Wildfire Occurrences in Taiwan and California, USA, 2022 Soil Hydrology and Water Resources Management Modeling Summit, Taichung, Taiwan, 19-20 March 2022.
E-mail:
  r09521307@ntu.edu.tw, cwstsai@ntu.edu
Abstract & slides
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works

## Slide 35: Acknowledgements
MOST 110-2628-E-002-008-
Stochastic Environmental
Hydraulics and Hydrology

## Slide 36: Wildfire in 2 Study Areas
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works
 | California | Taiwan
Trend | Increase↑ | Increase↑
Characteristic Timescale | ½ year | 1 year
Nature-Caused Wildfire | 10-15% | 2%
Anthropogenic activities | Firearms and explosives use | Burning paper money
Taiwan
California

## Slide 37: What is IDF-Curve?
Intensity-Duration-Frequency Curve
  An idea inspired from Hydrology, which typically applied in rainfall.
  Select annual maximum intensity in different burnt duration.
  Fit Log-Pearson Type 3 distribution.
  P=1/T (exceed probability)
  XTr= σ + k Tr
 | 1 | 2 | 3 | 6 | 12 | 24
2010 | 0.56 | 0.64 | 0.30 | 0.15 | 0.04 | 0.02
2011 | 0.56 | 0.02 | 0.22 | 0.70 | 0.02 | 0.10
2012 | 0.56 | 0.64 | 0.30 | 0.14 | 0.20 | 0.04
2013 | 0.56 | 0.41 | 0.05 | 0.14 | 0.03 | 0.18
2014 | 0.21 | 0.21 | 0.30 | 0.52 | 0.44 | 0.10
2015 | 0.30 | 0.35 | 0.35 | 3.17 | 0.31 | 0.15
2016 | 0.30 | 0.38 | 0.16 | 0.44 | 0.10 | 0.07
2017 | 0.70 | 0.70 | 0.41 | 0.42 | 0.15 | 0.18
2018 | 0.08 | 0.71 | 0.71 | 0.46 | 0.08 | 0.12
2019 | 0.40 | 1.11 | 0.23 | 0.07 | 0.23 | 0.11
2020 | 1.90 | 1.90 | 0.29 | 2.93 | 0.05 | 0.05
2021 | 0.42 | 1.75 | 0.04 | 0.22 | 0.30 | 0.04
mean | 0.51 | 0.73 | 0.26 | 0.76 | 0.17 | 0.09
SD | 0.48 | 0.60 | 0.18 | 1.09 | 0.13 | 0.06
Cs | 2.17 | 0.80 | 0.86 | 1.68 | 0.74 | 0.06
2 yr | 0.4 | 0.7 | 0.3 | 0.3 | 0.1 | 0.1
5 yr | 0.8 | 1.3 | 0.4 | 1.0 | 0.3 | 0.1
10 yr | 1.1 | 1.5 | 0.5 | 1.9 | 0.4 | 0.2
25 yr | 1.4 | 1.7 | 0.6 | 3.9 | 0.6 | 0.2
50 yr | 1.7 | 1.7 | 0.7 | 6.4 | 0.7 | 0.2
100 yr | 2.0 | 1.7 | 0.7 | 10.4 | 0.9 | 0.3
Curve

## Slide 38: Time Frequency analysis of Wildfires in Taiwan
IMF | (days) | (yrs)
1 | 6.3 | 0
2 | 12.1 | 0
3 | 28.1 | 0
4 | 58.1 | 0
5 | 112.7 | 0
6 | 241.6 | 1
7 | 558.8 | 2
8 | 1471.6 | 4
9 | 2833.5 | 8
IMF | (days) | (yrs)
1 | 5.2 | 0
2 | 8.9 | 0
3 | 20.1 | 0
4 | 48.1 | 0
5 | 112.0 | 0
6 | 253.3 | 1
7 | 622.7 | 2
8 | 1204.4 | 3
9 | 3579.8 | 10
IMF | (days) | (yrs)
1 | 4.9 | 0
2 | 10.4 | 0
3 | 23.9 | 0
4 | 53.3 | 0
5 | 129.8 | 0
6 | 280.2 | 1
7 | 526.0 | 1
8 | 1044.5 | 3
9 | 2412.5 | 7
IMF | (days) | (yrs)
1 | - | -
2 | 10.7 | 0
3 | 25.5 | 0
4 | 54.2 | 0
5 | 111.4 | 0
6 | 245.7 | 1
7 | 501.9 | 1
8 | 1190.4 | 3
9 | 2383.7 | 7
Wildfire Severity 1984~2020 (daily) (i.e. burnt area)
Trend of wildfire in 4 Taiwan regions
Introduction/ Methodology/ Results and Discussions/ Conclusions and Ongoing Works