## Slide 1
Qingwen Lu
luqw@hhu.edu.cn
College of Hydrology and Water Resources, Hohai University, China
Risk analysis for reservoir flood control operation considering
two-dimensional uncertainties based on Bayesian network
Notes: 【感谢陈宇的投稿】
字体：思源宋体Heavy

## Slide 2
hydrometeorological forecast
uncertainty
Research Background
flood forecast
uncertainty
Reservoir Flood Control Operation
initial flood regulation water level exceeds the designed flood limited water level (initial level uncertainty caused by floodwater conservation)
flood forecast uncertainty caused by real time flood forecast error
Risk Analysis Based on Bayesian Network
Model structure: directed acyclic graph (DAG)
Model parameters: conditional probability table (CPT)
Bayesian network (BN) can be used to deal with the uncertainties caused by the conditional correlation among different variables
Notes: 【感谢陈宇的投稿】
字体：思源宋体Heavy

## Slide 3
Risk Factors Identification
Risk source 1
Risk source 2
Reservoir inflow
Lateral inflow
Normal distribution
Uncertainty Quantification
Analytical derivation
Notes: 【感谢陈宇的投稿】
字体：思源宋体Heavy

## Slide 4
Risk Analysis Model based on BN
BN structure for reservoir flood control operation
1
Structure learning
DAG
—reservoir storage at the beginning/end of time period t
—reservoir level at the beginning/end of time period t
—average reservoir inflow in time period t
—average reservoir outflow in time period t
—average lateral inflow in time period t
—average flow at downstream
control point in time period t
Notes: 【感谢陈宇的投稿】
字体：思源宋体Heavy

## Slide 5
Risk Analysis Model based on BN
2
Parameter learning
Generating the training samples: Monte Carlo simulation
CPTs
Discretizing the variables: equal distance method
Parameter learning: maximum likelihood estimation (MLE)
Generate random samples of
Qt, IUt
Vt, Ht
qt, QCt
Notes: 【感谢陈宇的投稿】
字体：思源宋体Heavy

## Slide 6
Risk Analysis Model based on BN
Prediction: from cause to effect
Diagnosis: from effect to cause
4
Risk calculation
given V0, Q, IU, calculate the probability distributions of H and QC
given H, QC, calculate the probability distributions of V0, Q and IU
Reservoir
Downstream control point
3
Probability inference
Prior probability inference
Posterior probability inference
evidence variables
Notes: 【感谢陈宇的投稿】
字体：思源宋体Heavy

## Slide 7
Case Study
Xianghongdian Reservoir System
Case 1: Only considering the uncertainty of initial water level
Case 2: Only considering the uncertainty of flood forecast
Case 3: Simultaneously considering the uncertainties of initial water level and flood forecast
case 2 > case 3 > case 1
Numerical experiment setting
Prior probability inference
Notes: 【感谢陈宇的投稿】
字体：思源宋体Heavy

## Slide 8
Predicted risk for reservoir given values of risk factors (V0, Qmax, IUmax)
Diagnosed probabilities of initial storage with different (L1,L2,L3) evidence values (Hmax, QCmax)
Case Study
Posterior probability inference
Notes: 【感谢陈宇的投稿】
字体：思源宋体Heavy

## Slide 9
Conclusions
Flood control risk is mainly caused by flood forecast error, but the uncertainty of initial condition can not be neglected.
BN model can realize bi-directional inference which can be used to achieve effective risk management.
Notes: 【感谢陈宇的投稿】
字体：思源宋体Heavy

## Slide 10
Thanks for your attention!
Qingwen Lu
luqw@hhu.edu.cn
College of Hydrology and Water Resources, Hohai University, China
Notes: 【感谢陈宇的投稿】
字体：思源宋体Heavy