## Slide 1: Identification and quantification of sources and sinks of carbonyl sulfide
EGU22 – BG2.2, May 24th, 2022
Alessandro Zanchetta – a.zanchetta@rug.nl
ESRIG – CIO, University of Groningen – Nijenborgh 6, Groningen (NL)
Alessandro Zanchetta, Linda M.J. Kooijmans, Steven van Heuven, Andrea Scifo, Bert Scheeren, Jin Ma,
Ivan Mammarella, Ute Karstens, Harro A.J. Meijer, Maarten Krol, and Huilin Chen
Grant N°742798

## Slide 2: Introduction
Carbonyl sulfide (COS): a gas species involved in C and S cycles.
Currently associated to a slightly negative net radiative forcing.
Absorbed by plants similarly to CO2: potential tracer for GPP.
But there are many uncertainties: estimated missing source is 230-800 GgS/year.

## Slide 3
Kooijmans (2018): Monthly average diurnal cycle of COS mole fractions minus the mean daytime mole fractions to indicate the seasonal variation of the diurnal cycle amplitude.
Lutjewad
Nighttime sinks related to sites rich in vegetation
Median nighttime F(COS) = -3.0 ± 2.6 pmol m-2 s-1
-2.9 ± 2.2 pmol m-2 s-1 from August to November 2015
-7.2 ± 2.8 pmol m-2 s-1 in April 2015
A few positive F(COS) were measured during
nighttime in the ploughing season
(Kooijmans, 2018)
(Kooijmans, 2018)
Introduction
Lutjewad, ICOS measurement station

## Slide 4: Research questions
Are there known and/or unaccounted anthropogenic COS sources in the province of Groningen?
Could they explain the enhancements that have been observed in Lutjewad?
COS plumes observed in Lutjewad.
(Kooijmans, 2018)

## Slide 5: Methodology
Identification of local anthropogenic sources
  Sampling activities
  Known sources from literature (e.g. industries, power plants)
  Potential sources (mobile sampling)
Quantification of COS emissions
Implementation of COS data in available models and databases
  Stocastic Time-Inverted Lagrangian Transport (STILT)
  F(COS) – biospheric and anthropogenic databases, plus the new sources
Discrete sampling of waste treatment plant and biodigesters (June 2019)
Inlet
Pump and flask

## Slide 6: First step: sampling activities
In-situ mobile sampling and flasks measurements: COS emissions at biodigesters and at (bio)gas- and coal-related industries.
Highest estimated COS flux: 31.4 µmol/s. Correlation with CO emissions (2-10 pptCOS/ppbCO), occasional correlations with CH4 and CO2
Somewhat similar to the emissions measured in Lutjewad…
Ploughing was not proven as a COS source.
ppb
Wind direction
Farmsum
Delfzijl

## Slide 7: Second step: implementation in models
Background + (Footprint * Flux ) = COS
STILT
Biospheric + Anthropogenic
(SiB4, Kooijmans)
Zumkehr et al. (2018)
and local sources
(ICOS carbon portal)
TM5-4DVAR
Ma et al. (2021)
Longitude
Latitude

## Slide 8: Results: models
Measurements
Model - total
COS background
Direct anthro
Direct bio
Indirect anthro

## Slide 9: Results: models and measurements

## Slide 10: Results: models and measurements
∆COS = Measured COS – Modelled COS
∆CO2 = Measured CO2 – Modelled CO2

## Slide 11: Results: models and measurements
∆COS = Model with local sources – Model without local sources

## Slide 12: Discussion: localization of sources
Highest peaks can be partially justified by known industrial sources in Europe.
Lutjewad’s surroundings show potentially high influence with footprints, but very limited COS fluxes with current databases.
Latitude
Longitude

## Slide 13: Discussion: models and measurements
The model follows the general trend in the measurements rather well.
The mismatch is consistent in time for both CO2 and COS,
suggesting possibly unknown
(or imprecisely assessed) industrial sources.
The introduction of the measured local sources
had only marginal effects on the final modelled results.

## Slide 14: Conclusion
Local sources of COS were identified in the province of Groningen
  Biodigesters are not included in current databases
European industrial areas have influenced the measurements in Lutjewad
Local sources could not explain the remaining gap
  Need for further measurements (single samples)
  Considering also time variability or specific events as a cause of the plumes
Further measurements and/or modelling is needed to understand what could close the ‘gap’.

## Slide 15
Thank you! Questions?
Grant N°742798