## Slide 1
Tamagnone P.1, Caporali E.1, Sidoti A.2
1 University of Florence
2 Opificio delle Pietre Dure conservation workshops
Safeguarding heritage sites from hydrometeorological extremes: the Santa Croce district
in Florence
NH1.4
Extreme meteorological and hydrological events induced by severe weather and climate change
EGU22-7449

## Slide 2
Intro
Project
R.P. 1
R.P. 2
R.P. 3
Pluvial flood risk
in city environment
Pluvial floods may threat the safety of people and important assets.
www.newindianexpress.com, 2021
www.livesicilia.it, 2020
www.sixthtone.com, 2021
www.jewish-heritage-europe.eu, 2021
Furthermore, they can cause incalculable damages to historical buildings and the inestimable cultural heritage preserved
inside.

## Slide 3
TALETE project
Protecting the cultural heritage from pluvial floods:
the Santa Croce district in Florence
The study area is dangerously exposed to multiple sources of flood hazard:
1. river flooding due to the proximity to the Arno River
2. flooding by sewage since that the internal drainage network is linked with the main sewer conduits of the city
Tamagnone P., Caporali E., Sidoti A. Facing climate extremes to protect the heritage: the Santa Croce District In Florence, 2022, Climate.Culture.Peace
Intro
Project
R.P. 1
R.P. 2
R.P. 3

## Slide 4
TALETE project : research phases
Research, survey, digitalization: reconstruction of the drainage network of historic buildings and detection of connections with the urban sewer network
Retrieving geometrical features and technical specifications of the drainage network
Monographs of manholes
National Central Library of Florence
Opera di Santa Croce
Intro
Project
R.P. 1
R.P. 2
R.P. 3

## Slide 5
Hydrological and hydraulic modelling: evaluation of the interactions between the internal drainage network, the urban sewer system and surface runoff processes
1D/2D dual drainage model implemented to simulate all hydraulic phenomena occurring both on the surface and through the sewer network (software: InfoWorks ICM)
Intro
Project
R.P. 1
R.P. 2
R.P. 3
TALETE project : research phases

## Slide 6
Simulation of multiple extreme hydrometeorological events
Tamagnone P., Caporali E., Sidoti A. Protecting heritage cities from pluvial flooding: the Santa Croce district in Florence, 2022, 39th IAHR World Congress, Granada, Spain (accepted)
Intro
Project
R.P. 1
R.P. 2
R.P. 3
TALETE project : research phases
Hydrological and hydraulic modelling: evaluation of the interactions between the internal drainage network, the urban sewer system and surface runoff processes

## Slide 7
Hydrological and hydraulic modelling: evaluation of the interactions between the internal drainage network, the urban sewer system and surface runoff processes
Simulation of multiple extreme hydrometeorological events
Tamagnone P., Caporali E., Sidoti A. Protecting heritage cities from pluvial flooding: the Santa Croce district in Florence, 2022, 39th IAHR World Congress, Granada, Spain (accepted)
Intro
Project
R.P. 1
R.P. 2
R.P. 3
TALETE project : research phases

## Slide 8
Prevention and mitigation strategies: identification of critical issues and development of structural and non-structural strategies for the management of hydraulic risk induced by pluvial floods
Proposal of
structural strategy
Anti-flooding
barrier
Sewer overflow and flooding of interior rooms
Actual
Proposal
Intro
Project
R.P. 1
R.P. 2
R.P. 3
TALETE project : research phases

## Slide 9
Intro
Project
R.P. 1
R.P. 2
R.P. 3
Prevention and mitigation strategies: identification of critical issues and development of structural and non-structural strategies for the management of hydraulic risk induced by pluvial floods
Proposal of
non-structural strategy
Flood risk map
TALETE project : research phases

## Slide 10
NH1.4
Extreme meteorological and hydrological events induced by severe weather and climate change
EGU22-7449
Tamagnone Paolo
paolo.tamagnone@unifi.it
Caporali Enrica
enrica.caporali@unifi.it
Sidoti Alessandro
alessandro.sidoti@opificiodellepietredure.com
THANK YOU FOR YOUR ATTENTION
Ivo Bazzechi Cimabue Flood, marked as public domain -Wikimedia Commons
Let’s
protect
our heritage