## Slide 1
Calibration of the physics-based ground motion
model of the 2019 Mw4.9 Le Teil earthquake (France)
Fanny Lehmann1,2, F. Gatti2, M. Bertin1, D. Clouteau2
1 CEA/DAM/DIF, F-91297, Arpajon, France
2 Université Paris-Saclay, ENS Paris-Saclay, CentraleSupélec, CNRS, LMPS - Laboratoire de Mécanique Paris-Saclay, 91190 Gif-sur-Yvette, France

## Slide 2
2
2
Regional context
The lower Rhône Valley is ‘rather poorly seismic’. [Larroque 2021]
The Le Teil earthquake is the largest (Mw4.9) in metropolitan France since 1996.
Le Teil earthquake (Mw 4.9)
November 11, 2019
Recorded by 23 stations within 70km of epicentral distance
Epicenter: -1.3km depth
Renewed interest for seismic hazard analysis in the region
What can be achieved with numerical simulation in a data sparsity context?
[Schlupp et al. 2021]

## Slide 3
3
3
3
Ground motion model
a) National 3-layer
homogeneous model
(LDG [Duverger 2021])
b) National spatially-varying
model (EDF [Arroucau 2020])
Geophysical description
c) Random fluctuations
(cx= cy= 10km, cz= 1km, cv = 0.1)
b) Kinematic rupture model [Vallage 2021]
a) Equivalent moment tensor [Delouis 2021]
Source model
Numerical propagation code
SEM3D [CEA, IPGP, Centrale Supélec] Spectral element method
Domain: 42 x 110 x 45km3
fmax = 5Hz
min. element size = 260m
6 million elements
~109 dofs
Addition of topography but sedimentary basin not included yet
2,600h CPUs
for 60s of signal
42km
45km
110km

## Slide 4
4
4
4
Results (1): Geophysical description
Although simple, the models provide satisfying goodness-of-fit scores.
Comparison between numerical results and records
Mean horizontal component of PGV, PGA, Pseudo Spectral Acceleration at 1s.

## Slide 5
5
5
5
Results (2): Adding random fluctuations
No consistant effect on horizontal Peak Ground Velocity (PGVh) and Acceleration (PGAh)
Mean improvement of 0.4 GOF point for horizontal pseudo-spectral acceleration (SAh 1s)
Example: OGDF station (epicentral distance = 32km)
GOF scores in 23 stations
Smaller peaks and oscillations with heterogeneities

## Slide 6
6
6
6
Conclusion and perspectives
Despite their geophysical simplicity, available models provide coherent results (wave arrival times, peak ground motion, pseudo-spectral acceleration).
Random fluctuations give more realistic ground motion.
Open question:
Why are the results obtained with a finite fault model so different from the equivalent point source?
Perspectives:
Improve the geophysical description by including the sedimentary basin
 fanny.lehmann@centralesupelec.fr