## Slide 1: New environmental restrictions – aggregate effects on the Norwegian power system
Lennart Schönfelder, Birger Mo, Ingeborg Graabak, Atle Harby
Notes: Bildet illustrerer:
· bredden i SINTEFs ekspertise, fra havrom til verdensrom.
· hvilke områder og bransjer vi jobber innen for å realisere visjonen Teknologi for et bedre samfunn.
Bildestilen er basert på stikkordene fremtidsrettet, teknologi og norsk natur (naturressurser). SINTEFs visuelle univers er utviklet for SINTEF av Headspin Productions AS.

## Slide 2: Background
Norway: hydropower nation
>400 hydropower plant concessions: revision of terms
  Environmental flow
  Reservoir filling
  Production restrictions: minimum & ramping
2030: consequences for the power market
  Production – loss and impact on flexibility
  Market response
Industry project: Sumeffekt
Reservoir
Bypass reach
Downstream reach
Notes: Hydropower nation: favorable precipitation and topology. 1690 plants, more than 90% of power production originates in hydro
updated & new restrictions
Typical set-up, very simple example
Q95 very low flow, exceeded 95% time
Reservoir filling is too low

## Slide 3
Photo: Atle Harby
Notes: Example for a bypass reach

## Slide 4: Modelling framework
New Restrictions :
Environmental flow release: Q95 (seasonal)
Summer filling of reservoirs
0-scenario
2030 dataset
wind, solar, thermal
Int. interconnectors
Power demand
Scenario Fan Simulator (FanSi)
-stochastic market model
-detailed hydro
Result: Scenario comparison
30 inflow years
New bypass reach

## Slide 5: Results – production loss
Joint effect
Reservoir
restrictions
Environmental flow
Production loss: flood spill and env. flow release (Norway)
GWh / week
Week
Seasonal Q95 (summer/winter)  Seasonal power loss
Production loss 5.1 TWh/a (total 150TWh/a)
Main driver: env. flow release
Notes: Increased production loss
uke 1-17 og uke 40-52): 1.6 TWh
Summer uke 18-39): 3.6 TWh
Main driver: environmental flows

## Slide 6: Results – power price
Power price, Norway
Power price + 0.8 €/MWh
  Rainy sommer periods
Maximum prices similar
Many other effects
Notes: Results of 30 weather years, all prices sorted from lowest to highest