## Slide 1: The effect of relative humidity on eddy covariance latent heat flux measurements and its implication for partitioning into transpiration and evaporation
Weijie Zhang1,2, Jacob A. Nelson1, Mirco Migliavacca3, Rafael Poyatos4,5, Diego G. Miralles2, Tarek S. El-Madany1, Nuno Carvalhais1,6, Markus Reichstein1,7, Martin Jung1
1Department of Biogeochemical Integration, Max Planck Institute for Biogeochemistry, Jena, Germany
2Hydro-Climate Extremes Lab (H-CEL), Faculty of Bioscience Engineering, Ghent University, Ghent, Belgium
3European Commission, Joint Research Centre, Ispra (VA), Italy
4CREAF, Cerdanyola del Vallès, Spain
5Universitat Autònoma de Barcelona, Cerdanyola del Vallès, Spain
6Departamento de Ciências e Engenharia do Ambiente (DCEA), Faculdade de Ciências e Tecnologia (FCT),
Universidade Nova de Lisboa, Lisbon, Portugal
7Michael-Stifel-Center Jena for Data-Driven and Simulation Science, Jena, Germany
wzhang@bgc-jena.mpg.de
EGU22-8416

## Slide 2
41 Closed-Path Sites
@FLUXNET 2015
@Hourly
No RH dependence
Water fluxes are generally underestimated by eddy covariance systems under high relative humidity conditions. (RH-dependent errors)
EGU22-8416

## Slide 3
41 Closed-Path Sites
@FLUXNET 2015
@Hourly
No RH dependence
RH dependence
LE
underestimation
H underestimation
Water fluxes are generally underestimated by eddy covariance systems under high relative humidity conditions. (RH-dependent errors)
EGU22-8416

## Slide 4
LE is increased by
~58%
at very high RH
A machine-learning based emperical method to ‘correct’ for the error
@ Hourly
Bowen ratio method does NOT correct for the error (data not shown)
EGU22-8416

## Slide 5
@ Daily
Implication of RH-dependent errors for partitioning ET into transpiration and evaporation.
Increased ET goes to:
TEA: Transpiration
uWUE: Evaporation
EGU22-8416

## Slide 6: Summary
The underestimation of hourly LE at high RH (RH > 90%) is pronounced at closed-path sites in the FLUXNET2015 dataset;
Bowen ratio based energy balance closure method likely does NOT correct for these systematic errors (NOT shown in this presentation);
The systematic errors in LE potentially affects T/ET and WUE estimation under high RH (i.e. low VPD) conditions;
Future studies based on energy fluxes should take these effects into consideration because these errors could be also present in future datasets if not correctly addressed with the setup (heating) and processing (spectral corrections).
EGU22-8416

## Slide 7
THANKS to:
Principal Investigators at the eddy covariance sites
and the FLUXNET comunity:
              AmeriFlux
              AfriFlux
              AsiaFlux
              ChinaFlux
              ICOS
              OzFlux-TERN
              ......
        SAPFLUXNET
Pre-print:
EGU22-8416
Abstract:
wzhang@bgc-jena.mpg.de

## Slide 8
THANKS to:
Principal Investigators at the eddy covariance sites
and the FLUXNET comunity:
              AmeriFlux
              AfriFlux
              AsiaFlux
              ChinaFlux
              ICOS
              OzFlux-TERN
              ......
        SAPFLUXNET
Pre-print:
EGU22-8416
Abstract:
wzhang@bgc-jena.mpg.de
Thank You!