## Slide 2: Operation of a Differential Quantum Gravimeter Camille Janvier 1, Vincent Ménoret 1, Sébastien Merlet 2, Arnaud Landragin 2, Franck Pereira dos Santos 2, and Bruno Desruelle 1 (1) iXblue Quantum Sensors, Talence, France (2) LNE-SYRTE, Observatoire de Paris, Université PSL, CNRS, Sorbonne Université, Paris, France

## Slide 3: iXblue Quantum Sensors (former Muquans)
    Cold atom gravity meters
    (Δg/g ≈ 10-9)
Cold atom atomic clock
(Δf/f ≈ 10-15)
Laser and subsystem solutions
(Δλ/λ ≈ 10-10)
Optical frequency transfer
(Δf/f ≈ 10-20)
Quantum sensors & laser systems
Make atom quantum technology turn-key
OUR
WHY

## Slide 4: DQG: A Gravimeter + Gradiometer in a single package
A Differential Quantum Gravimeter
g1
g2
L
Weight:
  Sensor head: ~ 70kg
  Laser system: ~ 33kg
Power: ~ 200W
Notes: Insister sur Differential gravimeter = Gravity + Gravity gradiometer
Faire animation avec atomes qui chutent

## Slide 5: A new type of device: DQG
Continuous measurement
3 weeks long measurement
A very calm moment during public holidays
66 µGal/√𝜏
55 E/√𝜏
Public holidays
 Applications: reservoir monitoring (water, geothermy, gas, etc.), infrastructure monitoring

## Slide 6: DQG: Gravimeter + Gradiometer
Ground survey
First proof of principle survey
Performed outside
Two 1m3 cavities at shallow depth

## Slide 7: A new type of device: DQG
Survey measurements
Gravity gradient anomaly very well resolved
Gravity anomaly present a strong spatial drift
The 2 signatures are sensitive to different type of sources
Modeling ongoing
 Applications: civil engineering, infrastructure monitoring, archeology, prospection

## Slide 8: Conclusion
A new industry-grade quantum sensor available for accurate underground mapping
  PRA: https://doi.org/10.1103/PhysRevA.99.033601
  arXiv: https://doi.org/10.48550/arXiv.2201.03345
Promising results for continuous measurements as well as ground surveys.
The DQG is available commercially (please contact jean.lautier-gaud@ixblue.com)
Funding awarded by Horizon Europe to develop an instrument for robotized survey
More work by iXblue : GI6.1 Gas bubbling monitoring using sonars by Guillaume Jouve (Replay) + Booth 17

## Slide 10: Zoom on the public holidays
50 µGal/√𝜏
53 E/√𝜏

## Slide 11: A geophysical application: Densitometry
The DQG can be used as a densimeter
We present here a toy model based on Bouguer plates
A 1kg/m3 sensitive densitometer.
Bouguer plate 1
Bouguer plate 2
Bouguer plate 3
gt
gb
Hence:
H1
H2
H3
DQG
 Applications: Hydrology, non-invasive measurements