## Slide 1: Title Slide
1School of Geography, Earth and Environmental Sciences, University of Plymouth, Plymouth, U.K.
2School of Geography, College of Life and Environmental Sciences, University of Exeter, Exeter, U.K.
3Universidad Nacional Santiago Antunez de Mayolo (UNASAM), Huaraz, Ancash, Peru
Dylan B. Beard1, Caroline Clason1, Sally Rangecroft1,2, Wilmer Sánchez Rodríguez3, and William Blake1
Catchment scale variation of contaminants in glacial sediments
from the Cordillera Blanca, Peru

## Slide 2: Background
Contaminants have been found in all glaciers around the world
They are largely released through anthropogenic activities and are likely to increase in the future
Contaminant types and amount varies dependant on geographical location, precipitation levels and distance from source
They have the potential to impact plants, animals and humans downstream once released into meltwater
(Beard et al., Accepted – Progress in Physical Geography)
Background

## Slide 3: Aim and research questions
Questions
Do fallout radionuclide and potentially toxic element loads vary between glaciers in the Corderilla Blanca?
Do these contaminant loads vary between samples taken from the same glacier?
How mobile are these contaminant loads and do they vary between different glaciers?
Is there a relationship between the organic content of glacial sediment and the quantity and/or mobility of the contaminants?
Aim: To determine the variation of contaminant (fallout radionuclide and potentially toxic element) loads from glacier sediments at both glacier and catchment scales within the Corderilla Blanca, Peru
Aim and research questions

## Slide 4: Sample locations
Sample Locations
Sample Collection
17 samples collected between October and December 2020 in the Corderilla Blanca, by Wilmer Sánchez Rodríguez
Cryoconite hole on Pastoruri glacier (Rodríguez, 2020)
Cryoconite = windblown sediment found on glacier surfaces and in water filled holes
Cordillera Blanca
Cordillera Negra
Huaraz
Pastoruri
Shallap
Yanapaccha
Vallunaraju
The Rio Santa Catchment
Lima
PERU

## Slide 5: Methods
Gamma spectroscopy for FRN activity
XRF for elemental composition
ICP-MS and ICP-OES for element mobility
Sample Analysis
LOI for organic content
In-progress
Methods
Analytical Methods
Coming soon!
Samples were analysed at the Consolidated Radio-isotope Facility (CORIF), University of Plymouth, U.K.

## Slide 6: Fallout Radionuclide Activity
*World Health Organization (2018) Management of radioactivity in drinking-water
Cryoconite range: 0 - 7.5 Bq Kg-1
Moraine range: 0 – 1.4 Bq Kg-1
WHO*: 1 Bq L-1
Cryoconite range: 8430 – 27353 Bq Kg-1
Moraine range: 314.8 - 3443 Bq Kg-1
WHO*: 0.1 Bq L-1
Cryoconite range: 2.7 – 305.7 Bq Kg-1
Moraine range: 8.3 – 11.3 Bq Kg-1
WHO*: 10 Bq L-1
Moraine Sample
Fallout Radionuclide Activity

## Slide 7: Elemental Composition of cryoconite (1/2)
Smaller compositional components are more varied between cryoconite from different glaciers
Chart: 
| As | Ba | Bi | Br | Ce | Cl | Co | Cr | Cu | Ga | Mn | Mo | Nb | Ni | Pb | Pr | Rb | Sr | Zn | Zr
Shallap | 164.575 | 261.7 | 21.575 | 10.975 | 277.975 | 223.7 | 93.2 | 66.6 | 171.8 | 27.025 | 533.225 | 16.4 | 17.2 | 55.05 | 579.825 | 116.1 | 119.075 | 250.025 | 265.925 | 309.7
Vallunaraju | 92.375 | 267.75 | 13.375 | 7.0667 | 265.85 | 182.325 | 90.3 | 35.9 | 66.675 | 26.775 | 514.15 | 0 | 17.35 | 43.1 | 340.25 | 148.475 | 289.025 | 18.4 | 144.225 | 261.5
Yanapaccha | 56.85 | 336.05 | 11.7 | 5.65 | 256.9 | 158.55 | 0 | 79.575 | 72.525 | 24.1 | 340.4 | 17.6 | 89 | 56.275 | 229.65 | 110.1 | 145.8 | 19.4 | 129.35 | 256.25
Pastouri | 219 | 437.55 | 47.95 | 12.4 | 147.6 | 184 | 107.3 | 73.55 | 207.35 | 24.35 | 501.45 | 18.5 | 19.5 | 58.9 | 876.6 | 134.05 | 183.4 | 50.6 | 296.95 | 357.7
Larger compositional components are similar to each other
Chart: Composition (ppm)
| Al2O3 | CaO | Fe2O3 | K2O | MgO | Na2O | P2O5 | SiO2 | SO3 | Ti
Shallap | 209904.925 | 15375.45 | 72776.025 | 26182.875 | 16530.1 | 19904.875 | 3412.9 | 597482.775 | 4149.775 | 5664.95
Vallunaraju | 208729.075 | 13986.075 | 54051.775 | 30443.975 | 13156.675 | 29057.925 | 3214.5 | 606824.2 | 2902.3 | 4274.225
Yanapaccha | 210422.625 | 6036.375 | 67330.2 | 27839.225 | 11838.475 | 17943.225 | 3157.9 | 599049.75 | 2117.35 | 5872.15
Pastouri | 176201.95 | 8349.25 | 77747.7 | 26082.4 | 13848.55 | 12761.3 | 3260.25 | 542641.6 | 2276.55 | 5762.9
Elemental Composition of cryoconite (1/2)

## Slide 8: Elemental Composition of cryoconite (2/2)
Elemental Composition of cryoconite (2/2)
Cryoconite samples from all 4 glaciers are grouped and show similar differences in composition
Moraine samples are compositionally different to cryoconite samples from the same glacier
Moraine from Shallap shows similar composition to cryoconite from Vallunaraju
Cryoconite from different glaciers in the same region have different compositions
Shallap
Moraine
Vallunaraju
Moraine
Yanapaccha
Moraine
Yanapaccha
Cryoconite
Pastoruri
Cryoconite
Shallap
Cryoconite
Vallunaraju
Cryoconite

## Slide 9: In progress: Element Mobility
In progress: Element Mobility
Stage 1 [of 4] extractions (0.5M acetic acid)
Chart: 
| Na | Pb | Zn | As
Shallap | 50.7531 | 422.6109 | 335.3698 | 32.6745
S Moraine | 5.5119 | 304.798 | 728.7869 | 4.8391
Vallunaraju | 1011.1605 | 670.2346 | 219.2983 | 1.4232
V Moraine | 743.3139 | 59.55 | 234.1329 | 0.99047
Yanapaccha | 706.7371 | 121.76 | 143.0385 | 10.5765
Y Moraine | 363.6747 | 31.3152 | 456.5634 | 465.7917
Pastouri | 542.0679 | 944.251 | 274.1366 | 1.2892
Chart: Element Mobility (µg/l)
| Al | Cu | Fe | K
Shallap | 19164.1991 | 13803.5497 | 13619.7951 | 3641.9888
S Moraine | 47774.0507 | 1968.1439 | 3256.8877 | 783.8199
Vallunaraju | 14694.034 | 175.7548 | 22762.5009 | 6695.5277
V Moraine | 14906.8395 | 8.8865 | 762.8433 | 11187.4753
Yanapaccha | 10629.4042 | 40.3695 | 3056.7306 | 9368.8945
Y Moraine | 2514.5123 | 21.5073 | 32112.3812 | 6460.3868
Pastouri | 13797.1816 | 324.1586 | 8518.9405 | 6450.7639
Chart: 
| Be | Cd | Cr | Ni
Shallap | 1.6047 | 6.2004 | 21.0883 | 20.6131
S Moraine | 1.2058 | 4.3953 | 51.6607 | 13.7157
Vallunaraju | 2.6924 | 35.0168 | 12.8273 | 18.6399
V Moraine | 5.9737 | 8.5838 | 0 | 0.25031
Yanapaccha | 1.2287 | 1.964 | 6.7808 | 27.0311
Y Moraine | 11.7918 | 2.4239 | 2.2821 | 17.8477
Pastouri | 3.4151 | 46.544 | 12.8328 | 27.1563
13
13
1233
10.93
503
323
29001
200004
7.22
125
1.52
202
EQS values (µg/l): 1. Health Canada (2019) 2. European Parliament and of the Council (2008) 3. Water Framework Directive (2014) 4. Environmental Protection Agency (2003) 5. World Health Organization (2017)

## Slide 10: Take home message
Take home message
FRN activity and PTE quantities in glacial sediments have high variability at both glacier and catchment scales
Some PTEs are found in greater amounts in cryoconite sediment, while others are greater in moraine sediment
Future research on the variability of contaminant mobility will improve out understanding of potential downstream impacts
Contaminant levels in glacial sediments vary both locally and globally and thus it is important to sample across multiple glaciers when looking at catchment scale risk from their release into downstream environments
FRN activity is higher in cryoconite than moraine samples

## Slide 11: Questions?
Thank you!
Questions
?
Contact: Dylan.beard@plymouth.ac.uk
*Photography by Wilmer Sánchez Rodríguez and Dylan Bodhi Beard