## Slide 1
Using disdrometers data to evaluate GPM-DPR products over Italy
Elisa Adirosi1, Federico Porcù2, Mario Montopoli1, Luca Baldini1, Alessandro Bracci1,2, Vincenzo Capozzi3, Clizia Annella3, Giorgio Budillon3, Edoardo Bucchignani4, Alessandra Lucia Zollo4, Orietta Cazzuli5, Giulio Camisani5, Renzo Bechini6, Roberto Cremonini6, Andrea Antonini7, Alberto Ortolani7,8, Samantha Melani7,8
1 National Research Council of Italy, Institute of Atmospheric Sciences and Climate (CNR-ISAC), Rome, Italy
2 Department of Physics and Astronomy “Augusto Righi”, University of Bologna, Bologna, Italy
3 Department of Science and Technology, University of Naples “Parthenope”, Naples, Italy
4 Meteorology Lab, Centro Italiano Ricerche Aerospaziali (CIRA), Capua, Italy
5 Regional Agency for the Protection of the Environment of Lombardia (ARPA Lombardia), Milano, Italy
6 Regional Agency for the Protection of the Environment of Piemonte (Arpa Piemonte), Torino, Italy
7 Laboratory of Environmental Monitoring and Modelling for the sustainable development (LaMMA), Sesto Fiorentino (Florence), Italy
8 National Research Council of Italy, Institute for the Bioeconomy (CNR-IBE), Sesto Fiorentino (Florence), Italy
European Geosciences Union
General Assembly 2022
Vienna , 27 May 2022
Notes: 1
1

## Slide 2
GPM (Global Precipitation Measurement) precipitation products
Dual-Frequency Precipitation Radar (DPR):13.6 GHz and 35.5 GHz.
Footprint of 5 km and swath of 245 km (for Ku band) and 125 km (for Ka band).
Scan modes: Normal Scan (NS), Matched Scan (MS), High Sensitivity (HS)
From ”GPM/DPR Level-2 Algorithm Theoretical Basis Document”
GPM DPR Products: precipitation Level 2 (L2) products (version 6A), in particular the dual-frequency products 2ADPR-NS, 2ADPR-MS and 2ADPR-HS, and the single frequency products 2AKa-MS, 2AKa-HS and 2AKu-NS.
Variables: precipRateNearSurface (R), zFactorCorrectedNearSurface (Z), paramDSD (Nw e Dm). All the variables have been obtained at the first available (i.e. clutter free) bin near the ground that in our analysis range between 0.60 km and 1.48 km.
Example of Z from GPM DPR on 21 December 2019

## Slide 3
Ground based devices: disdrometers
Only for two sites the disdrometer measurements are available form 2014 (i.e. launch of the GPM core satellite)
In total more that 580.000 1-minute sample are available form ground based devices.
All the devices belong to the Italian disdrometer network (GID, https://www.gid-net.it/)
In order to uniform and maximize the quality of the data the same processing has been adopted to all the disdrometer raw data and then the DSD (drop size distribution) has been computed each minute:
R, Zka, Zku, Dmas, Nw
2D scatterplot of disdrometer based R vs Dm. Black and red lines represent the relations adopted by GPM algorithms for DSD parameter estimation.

## Slide 4
GPM and disdrometer comparison strategies
Selection of the GPM pixels
- Selection of the 5 × 5 km2 DPR pixel at ground that contains
the location of the disdrometer.
- The disdrometer measurement is taken as representative of the areal estimate.
Point
Selection of the matched minutes
For each GPM overpass in rainy conditions (at least one pixel with R > 0.1 mm h-1), the disdrometer data within ±∆t minutes with respect to the GPM overpass time were selected and averaged. was set equal to 5 minutes.
GPM Product | # minutes (Point) | # minutes (mean) | # minutes (optimal)
DPR NS | 54 | 61 | 68
DPR MS | 29 | 31 | 36
DPR HS | 11 | 17 | 19
Ka HS | 11 | 17 | 20
Ka MS | 22 | 28 | 33
Ku NS | 53 | 61 | 68
Disdrometer data
- DPR pixels whose centers are within 5 km from the disdrometers are averaged.
- The possible mismatch between DPR pixel aloft and disdrometer at ground due to advection is limited.
Mean
- Among the DPR pixels in a 3 × 3 box around the disdrometer, the one whose reflectivity value is closest to that estimated by the disdrometer is selected.
- This should provide the best match.
Optimal

## Slide 5
Results (1/2)
Scatterplot of R, Zka, Zku, Dmas e Nw obtained from disdrometer data (x-axis) and from GPM products as reported in the legend (y-axis).
R
Considering all the DPR products and all the comparison modes, NMAE ranges between 30.3% and 63.4%
The maximum rainy intensity is 10 mm h-1
Z
Ku-band shows an higher dispersion of the data with respect to Ka-band.
The bias values are small for both the frequencies.
For the optimal comparison mode NMAE values are less than 10%.
Dmas
NMAE values are less than 29% although the correlation coefficients are low.
GPM algorithms overestimate small Dmas and underestimate Dmas >1.5 mm.
Nw
The agreement in terms of 10log10Nw is not good. Similar results have been shown in the literature.

## Slide 6
Results (2/2)
NMAE, MAE, NB and correlation coefficient
In this case only the GPM overpasses where all the DPR products are available (i.e. the ones in single and double frequency).
The agreement between satellite and ground-based estimates depends on the considered precipitation variable.
The optimal comparison mode (colored bars) provides, in most of the cases, better results with respect to the point comparison mode (grey bars).
The comparison shows limited differences in the performances of the different GPM products, although in most cases, the dual-frequency algorithms present the better performances.
Reference: Adirosi, E.; Montopoli, M.; Bracci, A.; Porcù, F.; Capozzi, V.; Annella, C.; Budillon, G.; Bucchignani, E.; Zollo, A.L.; Cazzuli, O., Camisani, G., Bechini, R., Cremonini R., Antonini, A., Ortolani, A., Baldini, L.; Validation of GPM Rainfall and Drop Size Distribution Products through Disdrometers in Italy. Remote Sens. 2021, 13, 2081. https://doi.org/ 10.3390/rs13112081

## Slide 7
Conclusions and future works
The first validation study of the GPM DPR products (V06) in Italy with disdrometer data has been presented. In particular:
different comparison strategies have been presented and evaluated,
the agreement between disdrometer data and different DPR GPM products have been reported in terms of rainfall rate (R), radar reflectivity (Z), and DSD parameters (Dmas and Nw). In particular, for R, Z and Dmas the agreement is good, while Nw satellite estimates need to be improved.
Recently a new version of the GPM DPR products is available, namely Version 07A, where, along with an upgrade of the retrieval algorithm, the dual-frequency retrievals are available in the full swath (i.e. 245 km long). In the near future:
the validation of V07 with disdrometers over Italy will be provided
other disdrometer sites will be added to the ground based devices used for the validation of GPM DPR products over Italy