## Slide 1: A biogeochemical approach to build a perceptual hydrological model for a small peri-urban catchment
Olivier Grandjouan, Flora Branger, Matthieu Masson, Benoit Cournoyer, Marina Coquery
Session HS2.2.1 – 24 may 2022

## Slide 2
Goals and method
Site : Ratier watershed, 19 km²
Data : major parameters, dissolved metals, and microbiological parameters
Monthly sampling (2017-2019) at two stations
Development of a biogeochemical approach to better understand main hydrological contributions on a peri-urban catchment
Set up of a perceptual model to reproduce our understanding of the catchment behaviour

## Slide 3
Build of a hypothetical perceptual model of the Ratier catchment
G
S
D
Groundwater flow
Subsurface flow
Direct surface runoff
3 main hydrological contributions
Not represented in monthly samples
G
S

## Slide 4
Source identification their biogeochemical signature
1. Correlation analysis
2. Hydro-climatologic indicators
3 . Principal components analysis (PCA)
n = 26
G
S
Identification and grouping of parameters with similar behaviour
Simplification of dataset for further analysis
HF183 : human-specific Bacteroides
rum-2-bac : ruminant-specific Bacteroides
P.Aeruginosa : bacteria linked to sewage network
Linking concentration with hydrologic and climatologic conditions
Ca
Sr
Li
DOC
Cr
Cu
Al
Ni
Prev_day_discharge
P.aeruginosa
API
HF183

## Slide 5
Completion of the perceptual model based on the results
2 groundwater contributions : gneiss aquifer (Ca2+, Sr) and colluvium aquifer (Li)
2 main hydrologic contributions :
groundwater (Ca2+, Li…) and subsurface (DOC, Cr, P.aeruginosa…)
Lithium (µg/L)
Sewage overflow not only found at the downstream urban part
P. aeruginosa (nb copy/100mL)
n = 12
n = 13
P.aeruginosa
P.aeruginosa
DOC, Cr, Al
Ca2+, Sr
Li
n = 24
n = 26
a
a
a
b
Tukey test
Tukey test

## Slide 6
From perceptual to mixing and distributed hydrological model
1
Estimate volume contribution using biogeochemical mixing models (package nnls on R)
2
Enhance flow decomposition with hydrological event sampling
3
Compare with results from a distributed hydrological model
Discharge (L/s)
First results
18h event sampling
03-10-21 13:00
15:00
17:00
19:00
21:00
23:00
04-10-21 01:00
03:00
05:00
07:00

## Slide 7
Thank you for your attention !
Link to the ANR Project : https://anr.fr/Projet-ANR-21-CE34-0013