## Slide 1: Estimation of geostationary satellite-based hourly daytime and nighttime AOD using machine learning
Sanghyeon Song, Yoojin Kang, Jungho Im
Department of Urban and Environmental Engineering, Ulsan National Institute of Science and Technology, Ulsan, South Korea
24 April 2023

## Slide 2: Estimation of geostationary satellite-based hourly daytime and nighttime AOD using machine learning
Sanghyeon Song, Yoojin Kang, Jungho Im
Department of Urban and Environmental Engineering, Ulsan National Institute of Science and Technology, Ulsan, South Korea
PICO 5.11
Novelty
Study Object
In East Asia, continuous and frequent aerosol monitoring is highly required due to large-scale natural and artificial aerosol emissions.
Geostationary satellite provides continuous aerosol retrieval over a specific area, however, the observation is limited to the daytime.
Background
AOD by All-day BT model (proposed)
GK-2A RGB image
Study flow
Time series comparison
Development of a machine learning-based model for estimation of temporally continuous aerosol optical depth (AOD) at 550 nm during both daytime and nighttime using geostationary satellite (i.e., GK-2A) and other data
First study to …
estimate nighttime AOD using geostationary satellite data
estimate of the satellite-based nocturnal variation of AOD
monitor nighttime aerosol transport in East Asia by geostationary satellite
Models
All-day BT model
  - Daytime + Nightime estimation
  - BT variables
Daytime TOA model (for comparison)
  - Daytime estimation
  - TOA reflectance + BT variables
Abstract
Notes: In East Asia, due to large-scale aerosol emissions from natural and artificial sources, it is essential to continuously monitor the atmospheric aerosols.
Geostationary satellite provides temporally continuous monitoring of aerosol over a specific area, however, the observation is only limited to the daytime.
In this study, developed machine learning-based models for estimating temporally continuous aerosol optical depth (AOD) over East Asia including nighttime using the geostationary satellite, GK-2A, and other data.
Using the model proposed in this study, it is possible to continuously monitor the diurnal variation of AOD in the local area, and the aerosol transport in East Asia, including nighttime. To our knowledge, it is the first attempt at hourly continuous aerosol monitoring including nighttime over East Asia from the geostationary satellite.

## Slide 3
1
Introduction
2
Data
3
Method
4
Result
5
Conclusion
Overview

## Slide 4: Estimation of geostationary satellite-based hourly daytime and nighttime AOD using machine learning
Sanghyeon Song, Yoojin Kang, Jungho Im
Department of Urban and Environmental Engineering, Ulsan National Institute of Science and Technology, Ulsan, South Korea
Background
In East Asia, continuous aerosol monitoring is highly required due to large-scale natural and artificial aerosol emission
Geostationary satellite provides temporally continuous aerosol optical depth (AOD) retrieval over a specific area, however, the observation is only limited to the daytime
Introduction
Objective
Development of a machine learning-based model for estimation of temporally continuous AOD at 550 nm during both daytime and nighttime over East Asia using a geostationary satellite (i.e., GK-2A) and other data
Solar AOD (Level 2.0): 15 stations
Lunar AOD (Level 1.5): 7 stations
Both Solar and Lunar AOD: 22 stations
AERONET (AErosol RObotic NETwork) ground-based observation stations
Data
Study domain
East Asia
August 2019 – August 2021
Source | Variables
GK-2A | Level 1B Reflectances variables (ch01-ch06): Top-of-atmosphere (TOA) reflectances differences with recent 30-day minimum Brightness Temperature (BT) variables (ch07-ch16): BT differences and ratios between channels, BT differences with recent 30-day maximum Level 2 Cloud, TPW
Meteorological data | RDAPS numerical weather forecasting model Temp, Dew, RH, WS, U_wind, V_wind, PBLH, Visibility, Psrf
Geographical data | MODIS Land Cover ratio, NDVI SRTM DSM
Auxiliary data | SZA (Solar Zenith Angle), DOY (Day Of Year), HOD (Hour Of Day)
Reference data | AERONET AOD (Solar, Lunar)
Data
Method
Models
All-day BT model
  - Daytime + Nightime estimation
  - BT variables
Daytime TOA model
  - Daytime estimation
  - TOA reflectance + BT variables
Study flow for model training
Test days
Training
Test station
DOY: not multiple of 5
DOY: multiple of 5
43 stations
1 station
input variables
Estimated AOD (hourly, 12 km)
AERONET AOD (solar, lunar)
target variable
Machine learning based model
LightGBM (Light Gradient Boosting Machine)
GK-2A L1B
BT variables
MODIS
LC, NDVI
GK-2A L2
TPW, cloud
Auxilairy data
SZA, DOY, HOD
JAXA/ALOS
DSM
Daytime TOA model
All-day BT model
GK-2A L1B
TOA reflectance variables
RDAPS
Meteorological data
GK-2A cloud mask
Dataset split
Overview
Source: KMA
Asian dust
Abstract
shsong15@unist.ac.kr

## Slide 5: Estimation of geostationary satellite-based hourly daytime and nighttime AOD using machine learning
All-day BT model
Daytime TOA model
AHI-YAER
All-day BT model
Daytime TOA model
Sanghyeon Song, Yoojin Kang, Jungho Im
Department of Urban and Environmental Engineering, Ulsan National Institute of Science and Technology, Ulsan, South Korea
Model Performance
The scatter plots of random 10-fold cross validation of the proposed models on the training data
Daytime TOA model shows slightly higher performance than Daytime result of All-day BT model
Result
Conclusion
Summary
Temporally continuous AOD at 550 nm during both daytime and nighttime is estimated using geostationary satellite (i.e., GK-2A) and other data thgouth a machine learning approach.
Based on geostationary satellite data, it is possible to …
  estimate the diurnal variation of AOD
  monitor aerosol transport in East Asia including nighttime
Time series comparison
The time series from the proposed models with CAMS and AERONET AOD on the test AERONET station (KORUS_UNIST_ULSAN)
Overall, the proposed models estimate with similar patterns to CAMS and AERONET AOD
All-day BT model provides continuous diurnal variation of AOD on specific location
Spatial distribution comparison
The spatial distribution of AOD estimated from the proposed models with AHI-YAER AOD during the test day (2021 DOY 75)
All-day BT model can provides continuous aerosol monitoring over East Asia during both day and night
Novelty
First study to …
estimate nighttime AOD using geostationary satellite data
estimate of the satellite-based nocturnal variation of AOD
monitor nighttime aerosol transport in East Asia by geostationary satellite
0
0.5
1.0
1.5
, 16 March (DOY 75), 2021
Day
Night
All-day BT model
Day
Daytime TOA model
  AHI-YAER: Advanced Himawari Imager (AHI) Yonsei Aerosol Retrieval (YAER) algorithm
Abstract
Overview
shsong15@unist.ac.kr

## Slide 6: Background
GK-2A AOD
UTC 08, 1 Feb. 2021
Night
Day
https://climate.nasa.gov/news/3065/nasa-funded-network-tracks-the-recent-rise-and-fall-of-ozone-depleting-pollutants/
Atmospheric aerosol affects human health, the ecosystem, Earth's radiative budget and the climate.
Aerosol is quantified by aerosol optical depth (AOD):
  the extinction of radiation due to the atmospheric aerosol integrated over the atmospheric column as a function of wavelength.
Atmospheric Aerosol
In East Asia, continuous and frequent aerosol monitoring is highly required due to large-scale natural and artificial aerosol emissions:
  Natural sources: dust, volcano, smoke, plants
  Artificial sources: industry, urban, transport, agriculture
Geostationary satellites provide temporally continuous AOD retrieval over a specific area, however, the observation is only limited to the daytime.
Aerosol Monitoring
https://caice.ucsd.edu/introduction-to-aerosols/
1. Introduction
shsong15@unist.ac.kr

## Slide 7: Study object
1. Introduction
Development of a machine learning-based model for estimation of temporally continuous AOD at 550 nm during both daytime and nighttime using geostationary satellite (i.e., GK-2A) and other data
Based on geostationary satellite data …
  Estimating the diurnal variation of AOD
  Monitoring aerosol transport in East Asia
Study Object
Novelty
First study to …
estimate of the diurnal variation of AOD in the local area
monitor aerosol transport in East Asia including nighttime
estimate nighttime AOD using geostationary satellite data
Temporally continuous all-day AOD estimation from GK-2A satellite using machine learning
shsong15@unist.ac.kr

## Slide 8: Study domain and data
2. Data
East Asia
August 2019 –August 2021
Study area and period
Solar AOD (Level 2.0): 15 stations
Lunar AOD (Level 1.5): 7 stations
Both Solar and Lunar AOD: 22 stations
AERONET (AErosol RObotic NETwork) ground-based observation stations
Source | Variables | Spatial resolution
GK-2A L1B | TOA reflectance differences with recent 30-day minimum: ch01_diff, ch02_diff, ch03_diff, ch04_diff, ch05_diff, ch06_diff | 0.5 - 2 km
 | BT differences (BTD) between channels (3): ch07 - ch13 ch13 - ch15 ch11 - ch13 BT ratios (BTR) between channels (2): ch13 / ch11 ch13 / ch15 BT differences with recent 30-day maximum (4): ch11_diff, ch13_diff, ch14_diff, ch15_diff | 2 km
GK-2A L2 | Cloud TPW (total precipitable water) | 2 km 6 km
RDAPS | Temp, Dew, RH, WS, U_wind, V_wind, Visibility, PBLH, Psrf | 12 km
MODIS | Land Cover ratio (3): vegetation, water, urban Normalized Difference Vegetation Index | 0.5 km 1 km
Auxiliary Data | SZA (Solar Zenith Angle) DOY (Day Of Year) HOD (Hour Of Day) | - - -
AERONET (reference) | AOD | Point
Data
Channel (type) | Central Wavelength
1 (vis) | 0.47 μm
2 (vis) | 0.51 μm
3 (vis) | 0.64 μm
4 (vis) | 0.86 μm
5 (NIR) | 1.38 μm
6 (NIR) | 1.6 μm
7 (SWIR) | 3.8 μm
8 (WV) | 6.3 μm
9 (WV) | 6.9 μm
10 (WV) | 7.3 μm
11 (IR) | 8.7 μm
12 (IR) | 9.6 μm
13 (IR) | 10.5 μm
14 (IR) | 11.2 μm
15 (IR) | 12.3 μm
16 (IR) | 13.3 μm
GK-2A AMI Spectral Channels
TOA reflectance: Top-of-Atmosphere reflectance
BT: Brightness Temperature
shsong15@unist.ac.kr

## Slide 9: Study flow
3. Method
The all-day BT model uses the same variable combination during both daytime and nighttime
The daytime TOA model uses GK-2A L1B TOA reflectance as input variables additionally with the same variable combination of the all-day BT model
input variables
Estimated AOD (hourly, 12 km)
AERONET AOD (solar, lunar)
target variable
GK-2A cloud mask
Machine learning based model
LightGBM (Light Gradient Boosting Machine)
GK-2A L1B
BT variables
MODIS
LC, NDVI
GK-2A L2
TPW, cloud
Auxilairy data
SZA, DOY, HOD
JAXA/ALOS
DSM
Daytime TOA model
All-day BT model
GK-2A L1B
TOA reflectance variables
RDAPS
Meteorological data
Analysis
1. Model validation
10-fold cross validation
Comparison of validation results by two models
2. Spatial distribution comparison of AOD
Analysis of spatiotemporal AOD map over study area
Comparison of the estimated AOD with other AOD products from YAER, CAMS, GK-2A and AERONET
3. Time series comparison of AOD
Time series analysis of model-estimated AOD with CAMS and AERONET AOD
Process flow
Models
shsong15@unist.ac.kr

## Slide 10: Dataset split and validation
3. Method
Dataset split
DOY
5
3
4
8
6
7
9
…
1
2
10
11
Test days
Training
Test station
DOY: not multiple of 5
DOY :multiple of 5
43 stations
1 station
Dataset used during training
Dataset not used for training
(unseen data)
Training and Test stations
1 AERONET station was leaved out for a spatial test
Among the remaining AERONET stations, the data with DOY of multiple of 5 was leaved out for a temporal test
The remaining datasets were used for training the model and conducting 10-fold cross validation.
43 stations
1 station
10-fold Cross Validation
Test
Training
Validation
Training
Validation
Training
Validation
…
k iterations
Test
shsong15@unist.ac.kr

## Slide 11: Scatter plots: LightGBM, 10-fold CV
4. Result
DOY
Stations
Test (station)
Test (DOY)
Training
The scatter plots of random 10-fold cross validations for the all-day BT model and the daytime TOA model
In the all-day BT model, R2 is higher at nighttime than at daytime, however, RMSE and MAE are also higher at night.
Compared to the daytime result of the all-day BT model, the daytime TOA model shows slightly higher performance.
Random 10-fold CV
Day (BT)
Night (BT)
Day (TOA+BT)
Performance comparison
BT model < TOA model (daytime)
daytime < nighttime (by R2)
daytime > nighttime (by error)
shsong15@unist.ac.kr

## Slide 12: Spatial distribution and comparison
4. Result
Daytime TOA model
All-day BT model
AHI-YAER
GK-2A
CAMS forecast
AERONET
The comparison of estimated AOD with other AOD products
The estimated AOD showed similar spatial distribution pattern to AHI YAER, CAMS AODs
  AHI-YAER: AHI Yonsei Aerosol Retrieval (YAER) algorithm
  CAMS: Copernicus Atmosphere Monitoring Service (CAMS) global atmospheric composition forecasts
  GK-2A: Level 2 AOD product
DOY
Stations
Test (station)
Test (DOY)
Training
16 March, 2021
(DOY 75)
shsong15@unist.ac.kr

## Slide 13: Time series comparison on the test station
4. Result
The time series of LightGBM-based estimated AOD for both model with CAMS and AERONET AOD for December 2020 at AERONET test station (Ulsan, South Korea)
Overall, the LightGBM-based model estimates AOD with similar patterns to AERONET and CAMS AOD
The daytime TOA model shows more similar time series pattern to AERONET AOD than the all-day BT model
DOY
Stations
Test (station)
Test (DOY)
Training
AERONET station: KORUS_UNIST_Ulsan
shsong15@unist.ac.kr

## Slide 14: Summary and conclusion
5. Conclusion
Hourly AOD at 550 nm was estimated using data from geostationary satellite, GK-2A, through machine learning-based models (i.e., LightGBM)
The estimated AOD was validated with in-situ reference AERONET AOD by k-fold cross validation (random and temporal), and tested using test datasets separated by DOY and station which were not used for training
The estimated AODs during day and night by each scheme were mapped and its spatiotemporal distributions were compared with AHI-YAER, CAMS, GK-2A, and AERONET AOD product
Time series comparison of estimated AOD with CAMS and AERONET AOD was conducted for the in-situ test station
Conclusion
Summary
The model using TOA reflectance as input variables (Daytime TOA model) shows slightly better performance than the model without using TOA reflectance (All-day BT model)
The nighttime AOD was estimated based on a machine learning-based model using geostationary satellite data.
The continuous AOD monitoring will be possible during all-day including nighttime in East Asia
shsong15@unist.ac.kr

## Slide 15: Reference
Kang, Y., Kim, M., Kang, E., Cho, D., & Im, J. (2022). Improved retrievals of aerosol optical depth and fine mode fraction from GOCI geostationary satellite data using machine learning over East Asia. ISPRS Journal of Photogrammetry and Remote Sensing, 183, 253-268.
Park, S. S., Kim, J., Lee, J., Lee, S., Kim, J. S., Chang, L. S., & Ou, S. (2014). Combined dust detection algorithm by using MODIS infrared channels over East Asia. Remote sensing of environment, 141, 24-39.
Seidel, F. C., & Popp, C. (2011). Critical surface albedo and its implications to aerosol remote sensing. Atmospheric Measurement Techniques Discussions, 4(6), 7725-7750.
shsong15@unist.ac.kr
shsong15@unist.ac.kr

## Slide 16
Thank you
https://iris.unist.ac.kr
Facebook @UNIST.IRIS
Instagram @iris.unist
Twitter @IRIS_UNIST
Sanghyeon Song (shsong15@unist.ac.kr)
Our Research Group

## Slide 17: Atmospheric Aerosols
Supplementary
Atmospheric aerosols consist of solid particles and liquid droplets suspended in the air that are originated from both anthropogenic and natural sources
Atmospheric aerosols affect the climate the radiation energy budget of the earth by scattering and absorbing solar radiation and indirectly affect the climate
Aerosols are quantified using the Aerosol Optical Depth (AOD)
  extinction of solar radiation due to aerosols and integrated over the atmospheric column
AOD is one of the important optical parameters for characterizing the distribution of atmospheric aerosols and estimating ground-level particulate matter (PM) concentrations from satellite remote sensing
AOD products are retrieved from top of atmosphere (TOA) reflectance through an atmospheric radiative transfer model (RTM)
https://caice.ucsd.edu/introduction-to-aerosols/
https://www.gi.alaska.edu/news/research-aims-understand-chemical-compound-discovered-fairbanks-winter-air
Wang, L., Yu, C., Cai, K., Zheng, F., & Li, S. (2020). Retrieval of aerosol optical depth from the Himawari-8 advanced Himawari imager data: Application over Beijing in the summer of 2016. Atmospheric Environment, 241, 117788.

## Slide 18: Aerosol Monitoring of East Asia
In East Asia, continuous and frequent aerosol monitoring is highly required due to large-scale natural emissions and artificial aerosol emissions:
  Natural source: dust, volcano, smoke, plants
  Artificial source: industry, urban, transport, agriculture
GK-2A AOD
GK-2A RGB image
1 Feb. 2021, UTC 08
Geostationary satellite provides temporally continuous AOD retrieval over a specific area, however, the observation is only limited to the daytime.
  Daytime: satellite-based AOD is retrieved by attenuation of solar radiation
  Nighttime: multispectral satellite sensors do not provide AOD products due to the absence of solar radiation
Currently, there is no operational algorithm for retrieving nighttime AOD from geostationary satellite with full-time coverage over specific region
https://climate.nasa.gov/news/3065/nasa-funded-network-tracks-the-recent-rise-and-fall-of-ozone-depleting-pollutants/
Asian dust
Supplementary

## Slide 19
Atmospheric aerosols …
  increase TOA reflectance
  reduce BT
TOA reflectance
minimum TOA reflectance within the recent 30 days
TOA reflectance contributed by aerosol
-
=
BT
maximum BT within the recent 30 days
BT contributed by aerosol
-
=
background
contribution of aerosol
Decoupling surface and aerosol reflectances
surface reflectance
TOA reflectance
Solar radiation
scattering
absorption
TOA reflectance
BT difference between two wavelength channels has been used in dust detection methods.
BT ratio between two wavelength channels has been used to distinguish between the dust and surface signals more accurately
BT differences and ratios
Supplementary
GK-2A L1B data
Notes: atmospheric aerosol increases TOA reflectance
  Seidel, F. C., & Popp, C. (2011). Critical surface albedo and its implications to aerosol remote sensing. Atmospheric Measurement Techniques Discussions, 4(6), 7725-7750.
BT, BTD, BTR
  Park, S. S., Kim, J., Lee, J., Lee, S., Kim, J. S., Chang, L. S., & Ou, S. (2014). Combined dust detection algorithm by using MODIS infrared channels over East Asia. Remote sensing of environment, 141, 24-39.

## Slide 20: Machine Learning Model
Supplementary
A tree-based ensemble learning algorithm based on the Gradient Boosting framework.
While other tree-based machine learning models grow trees horizontally (level-wise tree growth), LightGBM grows trees vertically (leaf-wise tree growth)
LightGBM features …
  Gradient-based One-Side Sampling (GOSS)
    The samples with large gradients are retained, while samples with small gradient are randomly selected and given constant weights
  Exclusive Feature Bundling (EFB)
    The mutually exclusive features in sparse features are bound together to reduce the number of features
LightGBM (Light Gradient Boosting Machine)
Level-wise growth: XGBoost, CatBoost
Leaf-wise growth: LightGBM
Gradient descent graph
https://towardsdatascience.com/what-makes-lightgbm-lightning-fast-a27cf0d9785e

## Slide 21: Model interpretation: LightGBM, SHAP
Supplementary
The additionally used TOA reflectance difference variables, which represent the aerosol reflectance, were important variables that highly contribute to the model result.
All-day BT model
Daytime TOA model
SHAP summary plots with feature importance and contribution for the all-day model with BT as input variables and the daytime model with additional TOA reflectance as input variables for LightGBM model. (only top-10 variables)
TPW and DOY has a dominant contribution to estimating the AOD
In the all-day BT model, variables of BT differences were important, which are usually used for dust aerosol or cloud detection
ch13 - ch15
ch07 - ch13

## Slide 22: Scatter plots: LightGBM, Tests
Supplementary
DOY
Stations
Test (station)
Test (DOY)
Training
The scatter plots of test results (for test dataset by DOY and station) for the all-day BT model and the daytime TOA model
For the both tests, the daytime result is better than the nighttime, and during the daytime, daytime TOA model shows better performance than the all-day BT model.
Test (DOY)
Test (station)
Day (BT)
Night (BT)
Day (TOA+BT)
Performance comparison
temporal test > spatial test
BT model < TOA model (daytime)
daytime > nighttime