## Slide 1
EGU General Assembly 2023 – EGU23-12659 – Supplement Version
Mobility of total carbon, nitrogen and polyphenols from grape pomace in the soil column
S. Korz, C. More, S. Sadzik, C. Buchmann, E. Richling and K. MuÑoz

## Slide 2: Relevance
Use of grape pomace (GP) as an organic fertilizer
→ Wide C/N ratio
→ Rich in phenolics
→ Low pH → Seasonality depended
but
→ Rich in nutrients (N,P,K) → Cheap and readily available
→ Closing nutrient cycles

## Slide 3: Relevance
→ Focus on industrial use of GP
→ Maximization of extraction efficacy
→ Environmentally relevant processes neglected
→ Nutrient mobility between varieties in different soil types is almost unknown
Use of grape pomace (GP) as an organic fertilizer

## Slide 4: Pomace and soil sampling
Fig. 1: Sampling site (Map data: Destatis, Federal Statistical Office, 2023)
Sampling in Neustadt (Weinstraße, Rhineland-Palatinate, Germany)
Grape pomace from 4 Vitis varieties: Dornfelder (DF), Pinot Noir (PN), Riesling (RS) and Pinot Blanc (PB) during the harvesting season of 2021 (fresh, directly after pressing)
A representative soil sample from the Vineyard + reference soils (sand and silt loam)
Proportion of total area in use for agriculture
3 % 80 %

## Slide 5: Methods (Based on OECD)
E2) Rainwater extraction
Ex. in 1:5 sterilized artificial rainwater (0.01 M CaCl2 + 0.05 % NaN3)
Rainwater analysis (TOC and TN)
Polyphenols directly via FCR
E3) Soil column and leachate
Fresh GP application at max. allowed dose
Simulation of a heavy rainfall event
Soil elementary analysis (C and N)
TPC via aqueous soil extraction
E1) GP and soil characterization
Freeze drying and pulverization
Elementary analysis (C and N)
Polyphenols via SPE and Folin-Ciocalteu photometrical assay

## Slide 6: Pomace characterization
Fig. 2: Nutrient content in GP and rainwater extraction. Error bars indicate the standard deviation of four replicates. DF=Dornfelder, RS=Riesling, PN=Pinot noir, PB=Pinot blanc
Despite lower total C content, the water extractable amount is higher in white GP
Despite drastically lower total N, the water extractable amount is equal in red and white GP
TPC in red GP is ~twice as high as in white GP

## Slide 7: Soil characterization
 | R01A | R02A | Vineyard NW | 
Texture | Sandy loam | Silt loam | Sandy clay loam | 
Total C (%) | 0.95 | 1.06 | 1.5±0.4 | 
Total N (g kg-1) | 0.08 | 0.11 | 0.12±0.01 | 
WHC (g % d.w.) | 29.3 | 47.1 | 46.8±1.3 | 
pH (CaCl2) | 5.6 | 6.5 | 7.3±0.1 | 
Basal respiration (µg CO2-C g-1 soil h-1) | < LOD | 0.05±0.01 | 0.10±0.06 | 
Glucose respiration (µg CO2-C g-1 soil h-1) | 0.02±0.02 | 0.26±0.06 | 1.0 ±0.12 | 
Cmic (mg kg-1) | 174 | 794 | 449±20 | 
Table 1: Parameter of used soils

## Slide 8: Leaching parameters
Column dimensions Glass, 300 mm x 50 mm (Length x inner diameter)
Soil filling
Dry filling of fixed volume, saturation to 100 % WHC
GP Application rate 30 t ha-1 or 1:100 (GP:Soil)
Rainfall event simulation 200 mm over 48 h or 400 mL of artificial rainwater
Soil sample preparation Freezing → fractionating by depth → homogenization → freeze drying
Fig. 3: Soil columns

## Slide 9: Total Carbon and Nitrogen
Fig. 4: Total C (4a) and N (4b) content in soils and leachate compared to non-treated soil. Error bars indicate the standard deviation of three column replicates. Statistical differences are analyzed by a Dunnett test comparing the values to the untreated reference group via a t-test. C=Control, DF=Dornfelder, RS=Riesling, PN=Pinot noir, PB=Pinot blanc Significant differences are indicated as: ns: p > 0.05, *: p <= 0.05, **: p <= 0.01, ***: p <= 0.001, ****: p <= 0.0001

## Slide 10: Soil and leachate pH
Fig. 4: Soil and leachate pH compared to non-treated soil. Error bars indicate the standard deviation of three column replicates. Statistical differences are analyzed by a Dunnett test comparing the values to the untreated reference group via a t-test. C=Control, DF=Dornfelder, RS=Riesling, PN=Pinot noir, PB=Pinot blanc Significant differences are indicated as: ns: p > 0.05, *: p <= 0.05, **: p <= 0.01, ***: p <= 0.001, ****: p <= 0.0001
DF increased the pH in the vineyard soil
In two cases leachate pH was decreased
Leachate pH higher than soil pH

## Slide 11: Total polyphenolic content
Fig. 5: : TPC in three different soil depths, leachate and total content. Vertical lines indicate the mass balance between leaching and maximum aqueous extractable TPC of fresh GP (rainwater experiment). Points indicate the recovery (%) between total and soil water extractable TPC. Mean values of the total content were set to 100%. Numbers indicate the recovery (%) of soil water-extractable content based on maximum aqueous-extractable TPC. Blank treatments were subtracted from GP treatments.
Lowest recovery in the vineyard soil
Highest recovery in the RS treated ref. soils
Highest recovery in the upper soil layer

## Slide 12: Soil content after pomace treatment
 | C | N | TPC | pH
Soil | No effect (Exception: Increased in Sand-PB) | No effect | ↑ increased Silt < Sand, Lower < Upper, No effect of GP variety | No effect (Exception: Increased in Vineyard-DF)
Leachate | ↑ increased RS<PB<PN<DF, No effect of soil type | ↓ decreased Red < White, No effect of soil type | ↑ increased DF<PN<PB<RS, No effect of soil type | ↑ increased No effect of GP and soil type (Exception: Decreased in Vineyard-PB and 02A-RS)

## Slide 13: Take home messages
C and N are more mobile from white GP
  → water solubility
C is hardly retained, especially by sandy soils
  → C leaching
N input from GP is mainly due to mineralization and not due to initial leaching
  → Seasonality needs to be taken into consideration
In silty soils, polyphenols from GP are most relevant in the upper 10 cm
  → highest microbial activity → need for incubation studies
Strong dependency on soil parameters
  → chemical stability (soil pH) and sorption processes
Soil buffer capacity stable against acid GP medium

## Slide 14: Acknowledgements
The project is being funded by Carl-Zeiss-Foundation, project number P2021-00-004
Department of Chemistry Division of Food Chemistry and Toxicology
https://chem.rptu.de/ags/ag-richling
Institute for Environmental Sciences
Working Group of Soil Chemistry
https://nuw.rptu.de/ags/uchemie
Contact: