## Slide 1: Unreported VOC emissions from road transport including from electric vehicles
Samuel J. Cliff, Alastair C. Lewis, Marvin D. Shaw, James D. Lee, Michael Flynn, Stephen J. Andrews, James R. Hopkins, Ruth M. Purvis and Amber M. Yeoman
Motivation
Methodology
Measurement results
Inventory comparison
Future implications
Exhaust
Fuel-tank evaporation
Brake and tire wear
Missing screenwash source
58 mg veh-1 km-1
24 mg veh-1 km-1
31 mg veh-1 km-1
sjc613@york.ac.uk

## Slide 2
Poor monitoring coverage.
No oxygenated VOC measurements.
In the UK there is:
Motivation
1Department for Business, Energy and Industrial Strategy, National Atmospheric Emissions Inventory (NAEI), 2019, https://naei.beis.gov.uk/data/.
1
Home

## Slide 3
3 x weeks of measurements in summer 2021 & winter 2022 in Manchester, UK.
Measurement sites
Home

## Slide 4
Measured data
Positive roadside increment observed for summer and winter measurements.
Winter tracks traffic flow diel.
Summer is influenced by meteorology and boundary layer height.
Home

## Slide 5
Where:
= concentration
= tracer species (CO2 or NOx)
= dilution factor
= emission factor
= vehicle type
= number of vehicles
= VOC species
Expand
Emission factor calculation methodology
Home

## Slide 6
Inventory estimated annual emissions for different VOCs.
Traffic data breakdown at roadside site.
UK specific characteristics e.g. average trip length.
Convert into mg veh-1 hr-1 emission factor.
Generating inventory estimations
Meteorological conditions e.g. Temperature, RH.
Home

## Slide 7: Emission factors
A factor of 45 underestimation in ethanol and methanol!
Home

## Slide 8: Discrepancy between measured and COPERT for ethanol and methanol agrees very well with scaled industry sales statistics for screenwash
Comparison with industry sales statistics
35 kT of screenwash VOC emissions in 2018 for 537 billion vehicle km.
  64 mg veh-1 km-1.
  Inventory estimates 92 % (32 kT) is from ethanol and methanol.
Discrepancy of seasonal average measured ethanol and methanol emission factors.
  58 ± 39 mg veh-1 km-1 : Excellent agreement!
  Speciation agrees well with headspace analysis of different screen wash brands on the UK market.
  Screen wash emissions are 2x greater than exhaust emissions (31 mg veh-1 km-1) and not in road transport emissions inventories.
Product | Methanol % | Ethanol %
1 | 25.1 | 3.41
2 | 4.95 | 17.5
3 | 4.54 | 7.75
4 | 4.53 | 0.00
5 | 4.50 | 8.12
6 | 4.11 | 18.3
7 | 0.00 | 0.00
8 | 1.95 | 7.29
9 | 4.58 | 22.8
10 | 0.00 | 22.5
Average | 5.42 | 10.8
Table 1: Headspace analysis results of different screen wash brands on the UK market.
Home

## Slide 9: Future predictions
Use predictions of vehicle mileage and electric vehicle uptake to estimate future emissions.
Increase in vehicle kilometers expected due to increased population and reduced running costs of electric vehicles.
Transition from fuel to non-fuel-related emissions.
Globally important transition due to planned bans on sales of new petrol and diesel-powered vehicles.
Future emissions
Home

## Slide 10
Implications
6 % of the UK’s VOC National Emission Ceilings Directive (NECD) ceiling.
Relatively simple source for policy consideration to reduce a country’s VOC emissions.
Complete respeciation of road transport VOCs over the coming decade.
Models which do not include NFNE emissions may underestimate future ozone concentrations.
Increased production of PAN.
Peroxyacetyl nitrate (PAN)
Ozone (O3)
Acetaldehyde/formaldehyde
2Lewis, A. C. et al. An increasing role for solvent emissions and implications for future measurements of volatile organic compounds, Phil. Trans. A. 378, 20190328, 2020.
2
Home