## Slide 1
Progress on FCDR of MWRI onboard FY-3 Series Satellites
EGU 2023
Shengli WU 1, Ling SUN 1, Hongxin XU 2, Jiakai HE 2, Fenglin SUN 1, Songyan Gu 1and Peng ZHANG 1*
1 National Satellite Meteorological Center, Beijing 100081, China
2 Shanghai Institute of Space Communication Technology, Shanghai 201109, China

## Slide 2
 | sensors | Freq Range | Total
 | SSMI/SSMIS | 18-89GHz | 10
 | TMI/GMI | 10-183GHz | 2
 | AMSR | 6-89GHz | 2+1
 | MWRI | 10-183GHz | 4+4
Global Microwave Imagers

## Slide 3: Potential Application in Climate Change

## Slide 4
Sea Ice Concerntration Monitoring using MWRI

## Slide 5: FY-3/MWRI Introduction （A/B/C/D）
Frequency(GHz) | 10.65 | 18.7 | 23.8 | 36.5 | 89
Polarization | V.H | V.H | V.H | V.H | V.H
Band Width(MHz) | 180 | 200 | 400 | 900 | 2×2300
NeDT(k) | 0.5 | 0.5 | 0.5 | 0.5 | 0.8
Accurancy(k) | 2.0 | 2.0 | 2.0 | 2.0 | 2.0
BT Range(k) | 3～340 |  |  |  | 
Scan Points | 266(1.8s) |  |  |  | 
Black Body Stability | 0.3K |  |  |  | 
Nonlinear | <1K |  |  |  | 
Main Beam | ≥90% |  |  |  | 
Resolution ≤(km×km) | 51×85 | 30×50 | 27×45 | 18×30 | 9×15
Beam of different Channel | <0.07° |  |  |  | 
Scan | Conic |  |  |  | 
Orbit Width(Km) | ≥1400 |  |  |  | 
Antenna angle(°) | 45 |  |  |  | 
Scan Period(s) | 1.80.1（1.7/2.0） |  |  |  | 
Scan Period Stability(ms) | ≤0.36ms*（2 Scan lines） |  |  |  | 
 | ≤1ms(30 minutes) |  |  |  | 

## Slide 6
MWRI-II/MWRI-RM
MWRI-II
Morning orbit/Afternoon orbit
MWRI-RM
Drift orbit

## Slide 7
一、研制进展情况
MWRI-II/MWRI-RM
7
  2022:FY-3F(Morning orbit, Antenna size: 1.6m);
  2022:FY-3G(Drift orbit, Antenna size: 1.2m);
  2023:FY-3H(Afternoon orbit, Antenna size: 1.6m);
  Antenna performance and NedT improved based on FY-3A/B/C/D
 | MWRI | MWRI-II/RM | GMI | AMSR2 | MWI | SSMIS
Nation | China | China | US | Japan | EU | US
Antenna size(m) | 1 | 1.6/1.2 | 1.2 | 2 | 0.75 | 0.6
Main beam(%) | 90 | 95 | 90 | 90 | 90 | 90
Frequency range(GHz) | 10-89 | 10-183 | 10-183 | 6.9-89 | 18-183 | 18-183
Channels | 10 | 26 | 13 | 16 | 18 | 24
NedT | 0.5-0.8 | 0.5-0.8 | 0.6-1.5 | 0.4-1.4 | 0.6-1.2 | 0.4-1.9

## Slide 8: Calibration Equation and Parameters
Calibration Target
Receiver
Reflector
Source
Receiver
Parameters type

## Slide 9: MWRI Recalibration Algorithm
Algorithm | V1.0 | V2.0 | 
 |  | V1.1 | V1.2
Back lobe | Using single orbit get back lobe factor | Global data | Improve data quality control
Hot reflector | Correction based on A/D Bias | Correction based on difference of physical temperature of hotload and hot reflector | Improve data quality control
Hot load | - | Using rain forest data to get better hot load parameter | Using data near the hotload temperature
Nonlinear | - | Using new back lobe, hot reflector and hot load parameters, and double difference data of ocean surface, do the correction of u, and the releation ship between u and receiver temperature. | Using different AGC
 | Re-cal Parameters | Re-cal time series
FY-3B/MWRI | 2014 | 2010-2019
FY-3C/MWRI | 2014 | 2013-2019
FY-3D/MWRI | 2018 | 2017-2019

## Slide 11
FY-3B/C/D MWRI time series
Operational
Recal V1.0
Recal V2.0

## Slide 12
Operational
Recal V1.0
Recal V2.0
Notes: 最小统计单元：15天

## Slide 13: FY-3B/C/D MWRI
channel | Typical BT (K) | Mean of RMSE (K) |  | 
 |  | operational | Recal V1.0 | Recal V2.0
FY-3B |  |  |  | 
10V | 166.2 | 5.00 | 5.00 | 1.15
10H | 91.8 | 5.66 | 5.68 | 1.21
18V | 119.4 | 1.91 | 1.87 | 1.26
18H | 127.5 | 3.12 | 3.15 | 1.34
23V | 224 | 2.51 | 2.46 | 1.29
36V | 223.5 | 5.76 | 5.59 | 0.94
36H | 172.1 | 1.62 | 2.03 | 1.10
89V | 268.8 | 2.13 | 2.19 | 1.02
89H | 248.8 | 4.24 | 3.85 | 1.34
FY-3C |  |  |  | 
10V | 166.2 | 5.85 | 5.85 | 0.88
10H | 91.8 | 8.12 | 8.15 | 0.91
18V | 119.4 | 2.27 | 2.72 | 1.07
18H | 127.5 | 2.13 | 2.13 | 1.08
23V | 224 | 1.95 | 1.95 | 1.10
36V | 223.5 | 3.69 | 3.69 | 1.04
36H | 172.1 | 2.87 | 2.87 | 1.26
89V | 268.8 | 1.62 | 1.62 | 0.88
89H | 248.8 | 1.38 | 1.38 | 1.15
FY-3D |  |  |  | 
10V | 166.2 | 5.51 | 5.51 | 0.91
10H | 91.8 | 6.80 | 6.87 | 1.04
18V | 119.4 | 1.32 | 1.33 | 0.93
18H | 127.5 | 1.79 | 1.80 | 1.08
23V | 224 | 1.41 | 1.45 | 1.02
36V | 223.5 | 4.28 | 4.24 | 0.94
36H | 172.1 | 4.41 | 4.39 | 1.09
89V | 268.8 | 1.64 | 1.63 | 0.93
89H | 248.8 | 1.82 | 1.76 | 1.33

## Slide 14
wusl@cma.gov.cn
FCDR of MWRI
Papers JMR 2023; TGARS 2022; AAS 2022,2023; ATMOSPHERE 2022; ESSD 2023;
Data DOI:10.12185/NSMC.RICHCEOS.FCDR.MWRIRecalOrb.FY3.MWRI.L1.GBAL.POAD.NUL.010KM.HDF.2021.2.V1
Name | MWRI FCDR
Platform | FY-3B, FY-3C, FY-3D
Range | 2011-2021
Coverage | Global
Temporal Resolution | Daily
Spatial Resolution | 25km
Operational (attenuation)
Re-Calibrated
Operational (status jump)
Re-Calibrated

## Slide 15
FY-3 MWRI ASI sea ice concentration
MWRI-ASI SIC – SSMIS-ASI SIC
Monthly sea ice extent
MWRI-ASI SIC has lower difference with SSMI ASI SIC
Zhao 2023
Notes: 左上图为MWRI ASI算法海冰密集度与SSMIS ASI海冰密集度差异，1-4子图时间分别为2018年北极海冰范围较大的时期（3月15日），北极海冰范围较小的时期（9月19日），南极海冰范围较小时期（2月17日），南极海冰范围较大时期（9月29日）
左下图为MWRI ASI算法海冰密集度与SSMI ASI算法，AMSR ASI算法日均海冰密集度、日海冰范围比较。时间为2010年11月-2019年
右图为基于MWRI ASI算法，SSMI Bootstrap算法，SSMI Nasa Team算法，OSISAF，Sea Ice Index算法的海冰密集度数据得到1978-2019年的月平均海冰范围，风云系列数据的每月海冰范围从2010年11月开始。
表格为MWRI ASI算法海冰密集度与SSMI ASI算法，AMSR ASI算法日均海冰密集度比较的统计结果（偏差，绝对差异，标准差，相关系数）

## Slide 16
MLSE Retrieval Result
Hu et al., 2021, Satellite Retrieval of Microwave Land Surface Emissivity under Clear and Cloudy Skies in China Using Observations from AMSR-E and MODIS. Remote Sensing. https://doi.org/10.3390/rs13193980
Li et al., 2021, Spatiotemporal Variations of Microwave Land Surface Emissivity (MLSE) over China derived from 4-Year Recalibrated Fengyun 3B MWRI data. Advances in Atmospheric Sciences (minor revision)
FY-3 MWRI MLSE
MLSE Retrieval Result (average)
Notes: 中国科学技术大学的李锐教授团队专注于使用被动微波遥感对地气系统之间的碳水和能量交换进行研究。先后使用AMSR-E，GMI和风云卫星搭载的MWRI等仪器的观测进行微波地表比辐射率这一关键微波参数的反演，其大致的反演流程如图所示。其联合使用了MWRI L1级再定标微波亮温产品，葵花8-AHI静止卫星云产品，ERA-Interim再分析资料反演MLSE产品. 经过时空匹配，降水扣除，云水匹配等过程和微波辐射传输计算来扣除大气中的云水和各种气体的辐射贡献，进而反演出地表的微波比辐射率。
瞬时反演结果结合葵花8的即时云水分布可以看出，云的影响得到了合理的扣除。并且在多年平均分布上，该MLSE数据集和Norouzi et al., 2011以及Moncet et al.,2011的结果在10年尺度上具有较高的一致性。

## Slide 17
Selected SMAP SSM as reference，using artificial neural networks (ANN)approach, and FY-3B MWRI TB data with as input, intend to transfer high accuracy in soil moisture of L band to C/X band
A global daily soil moisture dataset derived from FY-3B MWRI and SMAP(2010-2019)
The trend of FYNNsm(Blue) is consistent with that of SMAPsm(red)and in situ SM (Obs-sm,grey), and FYNNsm well capture the temporal dynamic and annual variation of in situ SM. The performance of FYNNsm relative to Obs-sm is similar to SMAP as shown over most sites.
Yao, 2023

## Slide 18: F/T detection Using MWRI
Accuracy and performance:
Study area | Time range | F/T products | Time range
Ngari | 2010.7-2019 | AMSR | 2010.1-2019.12
Mqau | 2008.6-2019 | FY-3B(3D) | 2010.11-2019.6 2017.12-2019.12
Naqu | 2010.8-2016.12, 2017.12-2019.12 | MEaSUREs | 2010.1-2019.12
Pali | 2015.6-2016.12, 2017.12-2019.12 | SMAP | 2015.4-2019.12
F/T algorithm | Seasons |  |  |  | Overall
 | Spring | Summer | Autumn | Winter | 
New (FY-3D) | 68% | 97% | 77% | 91% | 83.49%
AMSR2 | 56% | 92% | 69% | 89% | 76.74%
SMAP | 67% | 87% | 85% | 93% | 83.03%
MEaSUREs | 37% | 85% | 45% | 94% | 65.99%
Evaluation：New (FY-3D)>SMAP>AMSR2>MEaSUREs
L-band is more sensitive to F/T detection;
The new algorithm developed in this study improves the F/T monitoring capability with high frequencies.
Wang 2022

## Slide 19
Thanks
Shengli Wu
wusl@cma.gov.cn