## Slide 1
FORECASTING KARST SPRING DISCHARGE WITH EXPLAINABLE MACHINE LEARNING MODELS
Anna Pölz1*, Julia Derx1*, Andreas Farnleitner2,3*, Alfred Paul Blaschke1*
MOTIVATION & OBJECTIVES
Karst systems exhibit complex hydrological characteristics including sinking streams, caves and networks of conduits and fractures. We propose data-driven modelling approaches to forecast dynamic karst spring discharge, based on a large variety of variables.
Compare ML modelling approaches of varying complexity.
Apply the DeepSHAP method for local model explanations.
Identify seasonal differences through model explanations.
STUDY SITE & DATA
Hydrological data: spring discharge
Meteorological data: rainfall, snow height, air temperature (2 stations)
Physicochemical data: turbidity, SAC at 254nm, electrical conductivity, water temperature
METHODS
RESULTS
CONCLUSION
We found that a higher model complexity coincides with a more accurate model for our test case. For all seasons the largest attributor is the historic discharge data. In winter there are no further major attributors. In spring air temperature, conductivity and snow influenced the model the most. In summer and autumn rainfall, SAC 254nm and turbidity were the main attributors. The findings correspond to the physical understanding of snow-melt and rainfall events in karst systems.
ACKNOWLEDGEMENTS & REFERENCES
This work was realised in the frame of the Vienna Water resource systems project (ViWa 2020+) and supported by the Austrian Science Fund (FWF) as part of the Vienna Doctoral program on water resources systems [grant number W1219].
Lundberg, S., & Lee, S.-I. (2017). A Unified Approach to Interpreting Model Predictions, Advances in Neural Information Processing Systems 30 (NIPS 2017) Shrikumar, A., Greenside, P., & Kundaje, A. (2017). Learning Important Features Through Propagating Activation Difference, Proceedings of Machine Learning Research 70 (PMLR 2017)
Shapley Value
The Shapley value determines the contribution of each feature to the prediction.
Feature attribution via SHAP
To explain the predictions, DeepSHAP is used. It is a combination of the DeepLIFT algorithm and SHAP, an approximation of Shapley values, which provides additive local explanations.
Spring | Limestone karst aquifer spring LKAS2 (AUT)
Catchment area | 70 km2
Catchment altitude | 2300 m a.s.l.
Mean discharge | 5.88 m3/s
Max/min - ratio | 57.5
Fig 1. Mean errors over hourly discharge forecasts from 0 - 96h ahead.
Fig 2. DeepSHAP attribution results by season and sorted by SHAP value magnitude.
Fig 3a. Per sample explanation during low flow (12/2018)
Fig 3b. Per sample explanation during high flow (07/2019)
1 Institute of Hydraulic Engineering and Water Resources Management, TU Wien, Vienna, Austria,
2 Institute of Chemical, Environmental and Bioscience Engineering, TU Wien, Vienna, Austria,
3 Research Division Water & Health, Karl Landsteiner University for Health Sciences, Krems, Austria,
* Interuniversity Cooperation Centre (ICC) Water & Health, Austria
Model comparison
We compare the predictive performance of the following models for karst spring discharge forecasting:
Multivariate Adaptive Regression Spline (MARS)
Feed-forward neural network (ANN)
Long short-term memory model (LSTM)
They reflect a wide range of ML modelling approaches with regards to complexity. The performance is evaluated using the four metrics Nash-Sutcliffe efficiency (NSE), mean absolute error (MAE), root mean square error (RMSE) and symmetric mean absolute percent error (sMAPE).
Model performance increases with model complexity for the test case LKAS2.
Model explanations results vary greatly between seasons. Predictions in spring are attributed to snow-related features. In summer and autumn mostly rainfall and physicochemical features are attributors.
The explanations obtained by SHAP values indicate that the model's predictions are influenced by rainfall events at high flows and accumulated snow during low flows.