## Slide 1
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
Yongpeng Lin1, Chenge An1, Shan Zheng2, Ruihua Nie3, Gary Parker4, Marwan A. Hassan5, Matthew J. Czapiga6, Xudong Fu1
1Tsinghua University, 2Wuhan University, 3Sichuan University, 4University of Illinois, Urbana-Champaign, 5University of British Columbia, 6University of South Carolina.
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
Idealized Cases:
A Single Weir
More Realistic Cases: Cascading Weirs & Mining
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
QR Code for the Abstract:
1/4
Since the 2008 Wenchuan (Ms. 8.0) Earthquake, the Shi‑ting River in the Longmen Mountain, China, experienced more than 20 m bed degradation in 7 years.
Potential reasons:
Sediment dis-connectivity due to in-channel weirs
The mobilization (“magic sand”) effect of fine sediment supply due to post-earthquake landslides
Sediment mining

## Slide 2
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
QR Code for the Abstract:
2/4
Questions:
What is the effect of weirs on bed degradation when coupled with fine sediment supply?
How much does sediment mining contribute to the dramatic degradation in the Shi-ting River?
Methods:
1-D river morphodynamic model
Analysis of satellite images
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
More Realistic Cases: Cascading Weirs & Mining
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
Idealized Cases:
A Single Weir
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 3
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
QR Code for the Abstract:
3/4
Key points:
The weir preferentially traps coarse sediment and delivers fine sediment, enhancing the “magic sand” effect of increased gravel mobility and thus downstream degradation.
The contribution of sediment mining (16 Mt/year) is one order of magnitude larger than the contribution of weirs and fine sediment.
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
More Realistic Cases: Cascading Weirs & Mining
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
Idealized Cases:
A Single Weir
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 4
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
QR Code for the Abstract:
4/4
You are kindly invited to click on the different steps outlined on this slide to obtain more information on this particular subject.
Clicking the close button on the top right-hand corner will always bring you back to the first slide.
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
More Realistic Cases: Cascading Weirs & Mining
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
Idealized Cases:
A Single Weir
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 5
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
Results for Idealized Cases with a Single Weir
Results for More Realized Cases with Cascading Weirs
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
Aerial photo of the Renmin Canal (Weir) in the Shi-ting River.
The weir was buried beneath the riverbed before the earthquake in 2008, but was 24 m above the riverbed in 2021.
The Renmin Weir
24 m
Downstream of the Renmin Weir, severe bed incision occurred and led to the exposure of bridge foundations.
Severe bed degradation
in the Shi-ting River:
X
1/3
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 6
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
Results for Idealized Cases with a Single Weir
Results for More Realized Cases with Cascading Weirs
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
Drop height: elevation difference between the weir crest and the downstream riverbed.
Cascading weirs
in the Shi-ting River:
X
2/3
1
2
3
4
5
6
Weir No. | Initial drop height* (m) | Drop height in 2015 & 2022 (m) | 
1 | 2 | 7.1 | 4.7
2 | 1 | 19.5 | 30.1
3 | 1 | 18.8 | 24.0
4 | 5.5 | - | -
5 | 5 | 12.5 | -
6 | 7 | - | -
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 7
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
Results for Idealized Cases with a Single Weir
Results for More Realized Cases with Cascading Weirs
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
Sediment mining
in the Shi-ting River:
3/3
Distribution of mining sites in the Shi-ting River in 2022 (Yellow Pins)
Observed from Google Earth
X
Typical mining sites
Area of the sand pile: 150 m × 80 m (left figure); 1000 m × 500 m (right figure).
Mining rates of 0-2 m/year are applied in simulation at the mining sites for calibration.
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 8
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
Results for Idealized Cases with a Single Weir
Results for More Realized Cases with Cascading Weirs
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
Model formulations:
(1) Flow hydraulics: Back water equation
(2) Sediment conservation: Exner equation with an active layer formulation
Notation:
hw: flow depth S: bed slope
Sf: friction slope Fr: Froude number
Cf: bed resistance coefficient
U: flow velocity
If: flood intermittency factor
p: porosity of the bed deposit
zb: bed elevation
qbT: total sediment transport rate
qbi: sediment transport rate of the i-th grain size range
Fi: fraction of surface material in the i-th grain size range
fIi: exchange fraction in the i-th grain size range
La: thickness of active layer
1/4
X
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 9
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
Results for Idealized Cases with a Single Weir
Results for More Realized Cases with Cascading Weirs
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
Model formulations:
(3) Sediment transport relation: Wilcock and Crowe
Notation:
Wi*: dimensionless sediment transport rate of the i-th size range
u*: flow shear velocity
R: submerged specific gravity of sediment
fi: the ratio of bed shear stress to reference shear stress for the i-th grain size range
fi: fraction of substrate material in the i-th grain size range
h: thickness of deposit above the weir
qbi,up: sediment transport rate from upstream
2/4
X
(4) Maximum sediment transport rate at the weir
※ The weir is non-erodible.
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 10
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
Results for Idealized Cases with a Single Weir
Results for More Realized Cases with Cascading Weirs
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
Computational conditions:
Channel length: 50 km
Discharge per unit width qwf : 6 m2/s (close to 10-year flood)
Flood intermittency factor If : 0.03
Pre-earthquake sediment feed: 2×10-3 m2/s gravel
Post-earthquake sediment feed: 2×10-3 m2/s gravel + 2×10-3 m2/s sand
Initial bed slope: 5.2 ‰
Initial surface geometric mean grain size: 30.4 mm
Initial substrate texture: the same as gravel supply
※ Initial condition: pre-earthquake equilibrium
3/4
X
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 11
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
Results for Idealized Cases with a Single Weir
Results for More Realized Cases with Cascading Weirs
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
Computational Scenarios (Single weir):
4/4
X
Case No. | Weir height (m) | Weir location (km)
1 | No weir | 
2 | 0 | 5
3 | 2 | 5
4 | 5 | 5
5 | 5 | 10
6 | 5 | 20
7 | 10 | 5
Pre- and post-earthquake sediment feed conditions
No sediment mining
Cases 4-6: effect of weir location
Cases 2-4 & 7: effect of weir height
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 12
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
Idealized Cases:
A Single Weir
More Realistic Cases: Cascading Weirs & Mining
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
X
Effect of weir location
Only gravel supply: weir location hardly affects the degradation depth downstream of the weir.
Both gravel and sand supply: larger degradation depth with a closer weir.
1/2
Weir locations = 5 km, 10 km, and 20 km; Weir height = 5 m.
dzb: denotes deviatoric bed elevation
Only gravel supply
Gravel and sand supply
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 13
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
Idealized Cases:
A Single Weir
More Realistic Cases: Cascading Weirs & Mining
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
X
2/2
Effect of weir height
Only gravel supply: degradation depth is almost equal to the weir height.
Both gravel and sand supply: even a sill with zero weir height leads to 10 m degradation.
Only gravel supply
Gravel and sand supply
Weir locations = 5 km; Weir height = 0, 2, 5 and 10 m.
dzb: denotes deviatoric bed elevation
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 14
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
Results for Idealized Cases with a Single Weir
More Realistic Cases: Cascading Weirs & Mining
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
X
Simulation vs. Observation (drop height at Weir 3)
The observed drop height at Weir 3 increases rapidly from 0 m to about 20 m before 2013, but keeps relatively stable afterwards.
In our simulation, mining rates of 0-2 m/year are applied.
1.2 m/year (16 Mt/year): Simulation agrees reasonably with the observed trend, with a generally declining rate of bed degradation over time.
2 m/year: Simulated drop height increases consistently even after 2013, which is different from the observation.
Simulated and observed drop height at Weir 3
1/3
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 15
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
Results for Idealized Cases with a Single Weir
More Realistic Cases: Cascading Weirs & Mining
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
X
Simulated spatiotemporal variation of dzb (deviatoric bed elevation), mining rate = 1.2 m/year
2/3
Spatiotemporal variation of dzb
Upstream of the weir: traps bedload and leads to bed aggradation
Downstream of the weir: causes significant bed degradation
The largest degradation occurs in the region 15-35 km downstream of the inlet, mostly due to the large interval between two weirs.
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 16
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
Results for Idealized Cases with a Single Weir
More Realistic Cases: Cascading Weirs & Mining
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
X
Contribution of sediment mining to bed degradation
Observed Vrm: 1×108 m3 in 2015, 1.5×108 m3 in 2022.
Simulated Vrm without sediment mining: 2×106 m3 in 2015, 9×106 m3 in 2022, which are 1-2 orders of magnitude smaller than observation.
Simulated Vrm agrees well with the observation with mining rate = 2 m/year (2015) and 1.5 m/year (2022).
3/3
Observed and simulated Vrm (net volume of sediment eroded from the channel) in the Shi-ting River with different mining rates.
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 17
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
Results for Idealized Cases with a Single Weir
Results for More Realized Cases with Cascading Weirs
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
Panel a: Dimensionless sediment transport rate
Panel b: Ratio of sand transport rate to gravel transport rate
X
1/2
(a)
(b)
Bedload transport across the weir
The weir generally reduces the bedload transport rate by about 30% within 20 years.
The weir preferentially delivers fine sediment, which leads to a finer bedload downstream.
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 18
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
Results for Idealized Cases with a Single Weir
Results for More Realized Cases with Cascading Weirs
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
X
2/2
Coupling effect: weir & fine sediment
When weir location < 12.5 km：
> +
coupling effect > sand effect + weir effect
The weir traps gravel and delivers sand, enhancing the “magic sand” effect on bed degradation.
Simulated bed degradation immediately downstream of the weir after 20 years.
: degradation induced only by “magic sand”
: degradation induced only by the weir
: degradation induced by the two effects
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 19
Degradation of a foreland river after the Wenchuan Earthquake, China:
A complex interaction among weirs, sediment supply and sediment mining
Research Prototype
1-D Morphodynamic Model & Computational Scenarios
Results for Idealized Cases with a Single Weir
Results for More Realized Cases with Cascading Weirs
Take Home Messages
Effect of Weirs on bedload transport & bed degradation
Sediment mining, not excess sand from the Wenchuan earthquake, is likely the key factor for the dramatic bed degradation in the Shi-ting River.
A longer spatial interval between weirs leads to larger bed degradation.
The weir preferentially traps gravel and delivers sand, which can enhance the “magic sand” effect on downstream degradation.
X
The QR code for the abstract
My email: linyp19@mails.tsinghua.edu.cn
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021

## Slide 20
24 m
in 2021
Background picture: Aerial photo of the Renmin Canal, Shi-ting River, Sichuan, China, taken in 2021
X