## Slide 1: Foam Composition and Surfactant Sources in an Urban Foaming Lake: A Comprehensive Analysis
Reshmi Das
Centre for Sustainable Technologies
IISc Bangalore, India

## Slide 2
2.1 Untreated discharge- direct & indirect source of surfactant
Foam Composition and Surfactant Sources in an Urban Foaming Lake: A Comprehensive Analysis
Reshmi Das , Chanakya Hoysall , Lakshminarayana Rao
Centre for Sustainable Technologies , Indian Institute of Science (IISc), Bangalore, India
1. What causes foam?
Up to 20 mg/ l of surfactant in lake water
Sorption:
< 3.5 mg surfactant / g Sediment
53.5 ± 4 mg surfactant/g TSS
More organic matter more sorption
2.2 Desorption of surfactant by Sediment & suspended solids (TSS)
Desorption:
73% surfactant TSS
53% surfactant sediment
Bacterial genus | Population % |  | Biosurfactant
 | soil | water | 
Pseudomonas | 19.2 | 23.5 | Glycolipipeptide/Rhamnolipid by Pseudomonas aeruginosa Viscosin by Pseudomonas florescens
Rhodococcus |  | 0.03 | Trehalose lipids by Rhodococcus erythropolis
Arthrobacter | 0.06 | 0.54 | Trehalose lipids Lipopeptide by Arthrobacter oxydans LBBMA 201
Bacillus | 0.03 | 0.01 | Lipopeptide by Bacillus sp. LBBMA 111A, LBBMA 155 Surfactin by Bacillus subtilis Lichenysin by Bacillus licheniformis Lipopeptide by Bacillus circulans
Gordonia | 0.02 |  | Lipopeptide
Nocardia | 0.02 |  | Glycolipids/ Trehalose Lipids by Nocardia erythropolis
Leuconostoc | 0.16 |  | Viscosin by Leuconostoc mesenteoids
Dietzia |  | 0.11 | Glycolipid by Dietzia maris LBBMA 191
Flavobacterium | 0.11 | 5 | Mixed flavolipids by Flavobacterium sp. LBBMA 168
Acinetobacter | 2.2 |  | Emulsan by Acinetobacter lwoffii
Weissella | 0.01 |  | Glycolipid by Weissella cibaria PN3
Halomonas | 0.01 |  | Exopolyschharide/Glycolipipeptide by Halomonas sp. ANT-3B
2.3 Bacterial Biosurfactant – sediment and water
Anthropogenic source sewage /industrial effluents
Naturogenic sources  Bacteria , Plants
2. Sources of Surfactant?
3. Conclusion
Direct source: Loaded with surfactants from personal care products like shampoo, hand and body washes , toothpaste , Laundry detergents and room cleaner
Indirect source: Phosphorus(P) in sewage acts as nutrient to aquatic plants that produce biosurfactants
Sewage
Phosphorus
Bio-surfactant
Algae &
Aquatic Plant
Algae and Aquatic Plants
Synthetic Surfactant
Personal care
products
Reference:
"Study towards understanding foaming and foam stability in urban lakes."
Das, Reshmi, H. N. Chanakya, and Lakshminarayana Rao.
Journal of Environmental Management 322 (2022): 116111.
Surfactant in aquatic system can originate from anthropogenic and naturogenic sources
Untreated sewage is a direct source of surfactant
Phosphorus in untreated sewage is an indirect source of bio-surfactant
Sediment and suspended solids has sorbed surfactants , which desorbs to cause foam
Sediment and water has as high as 23% of surfactant producing bacteria
Solution : Preventing ingress of untreated sewage and Sediment dredging/desilting
Reshmi Das | Ph.D. Student, Senior Research Fellow, IISc
Research Areas | Wastewater , Soil biogeochemistry, Microbiology, Environmental Chemistry , Water quality modelling & Waste management.
Contact | reshmidas@iisc.ac.in
mg of surfactant sorbed

## Slide 3: EXPLANATION

## Slide 4: INTRODUCTION
BELLANDUR LAKE, BANGALORE
MARINA BEACH, CHENNAI
RHINE RIVER, SWITZERLAND
AUSTRALIA
SPAIN
FRANCE
FIRE
DISRUPT TRAFFIC
SMELL
FISH KILL

## Slide 5: SURFACTANT
Source?????
Notes: The central unexplored question in this domain is - what compounds make up a foam? Foam is caused by surface-active compounds called surfactants.. We try to comprehensively identify all the sources of surfactants in foaming waterbody of Bellandur

## Slide 6: SURFACTANT SOURCES
1. Untreated sewage as direct and indirect source of surfactant

## Slide 7
SURFACTANT SOURCES
2. Desorption from sediment and suspended solid
More Organic Matter , More sorption
More Suspended solid (TSS) , more sorption
Particle size analysis shows that TSS had D60 of 1877 nm
Sorption by TSS is 53.5±4 mg SDBS/ g TSS
Maximum sorption by sediment is 5.3 mg SDBS /g sediment
TSS: up to 75 % desorption
During RAIN : Desorption of surfactant from TSS, increases foaming potential

## Slide 8
SURFACTANT SOURCES
3. From bacteria in water and sediment
Bacterial genus | Population % |  | Biosurfactant
 | soil | water | 
Pseudomonas | 19.2 | 23.5 | Glycolipipeptide/Rhamnolipid by Pseudomonas aeruginosa Viscosin by Pseudomonas florescens
Rhodococcus |  | 0.03 | Trehalose lipids by Rhodococcus erythropolis
Arthrobacter | 0.06 | 0.54 | Trehalose lipids Lipopeptide by Arthrobacter oxydans LBBMA 201
Bacillus | 0.03 | 0.01 | Lipopeptide by Bacillus sp. LBBMA 111A, LBBMA 155 Surfactin by Bacillus subtilis Lichenysin by Bacillus licheniformis Lipopeptide by Bacillus circulans
Gordonia | 0.02 |  | Lipopeptide
Nocardia | 0.02 |  | Glycolipids/ Trehalose Lipids by Nocardia erythropolis
Leuconostoc | 0.16 |  | Viscosin by Leuconostoc mesenteoids
Dietzia |  | 0.11 | Glycolipid by Dietzia maris LBBMA 191
Flavobacterium | 0.11 | 5 | Mixed flavolipids by Flavobacterium sp. LBBMA 168
Acinetobacter | 2.2 |  | Emulsan by Acinetobacter lwoffii
Weissella | 0.01 |  | Glycolipid by Weissella cibaria PN3
Halomonas | 0.01 |  | Exopolyschharide/Glycolipipeptide by Halomonas sp. ANT-3B

## Slide 9: CONCLUSION
Surfactant in aquatic system can originate from anthropogenic and naturogenic sources
Untreated sewage is a direct source of surfactant
Phosphorus in untreated sewage is an indirect source of bio-surfactant
Sediment and suspended solids has sorbed surfactants , which desorbs to cause foam
Sediment and water has as high as 23% of surfactant producing bacteria
Solution : Preventing ingress of untreated sewage and Sediment dredging/desilting