## Slide 1: How AuScope 3D Geomodels Portal integrates relatively metadata-poor geological models into its metadata infrastructure
Python scripts
The AuScope 3D Geomodels Portal is a website designed to display a variety of geological models and associated datasets and information from all over the Australian continent. The models are imported from publicly available sources, namely Australian government geological surveys and research organisations. Often the models come in the form of downloadable file packages designed to be viewed in specialised geological software applications. They usually contain enough information to view the model’s structural geometry, datasets and a minimal amount of geological textual information. Seldom do they contain substantial metadata, often they were created before the term ‘FAIR’ was coined or the importance of metadata had dawned upon many of us. This creates challenges for data providers and aggregators trying to maintain a certain standard of FAIR compliance across all their offerings. How to improve the standard of FAIR compliance of metadata extracted from these models? How to integrate these models into existing metadata infrastructure? For the Geomodels portal, these concerns are alleviated within the automated model transformation software. This software transforms the source file packages into a format suitable for display in a modern WebGL compliant browser. Owing to the nature of the model source files only a very modest amount of metadata can be extracted. Hence other sources of metadata must be introduced. For example, often the dataset provider will publish a downloadable PDF report file or a description on a web page associated with the model. Automated textual analysis is used to extract more information from these sources. At the end of the transformation process, an ISO-compliant metadata record is created for importing into a GeoNetwork catalog. The GeoNetwork catalog record can be used for integration with other applications. For example AuScope’s flagship portal, the AuScope Portal, displays information, download links and a geospatial footprint of models on a map. The metadata can also be displayed in the Geomodels Portal.
Join us online: auscope.org.au | Twitter, LinkedIn and YouTube @AuScope | info@auscope.org.au
Vincent Fazio, CSIRO Mineral Resources, Australia (vincent.fazio@csiro.au)
Model transformation software (geomodel-2-3dweb)
dSpace
GeoNetwork
ckan
OAI-PMH
Keywords
(YAKE & USGS Thesaurus)
Output ISO19115 metadata
(pygeometa)
AuScope GeoNetwork metadata catalog
AuScope Portal
CKAN API
Model source files
e.g. GOCAD object files
Models’ geological reports (PDF)
ISO19115-3 & ISO19139 XML
records
AuScope
Geomodels Portal
Summarizer (T5)
Augmented records: sourced from websites and services
{
Generated records: sourced from PDF reports
{
Only a few metadata fields can be gleaned from website model creation process e.g. bounding box coordinates, model URLs, title
WebGL assets
Config files
More Information
AuScope Portal http://portal.auscope.org.au/
AuScope Geomodels Portal http://portal.auscope.org.au/
bas-metadata-library https://github.com/antarctica/metadata-library
CKAN https://ckan.org/
dSpace https://dspace.lyrasis.org/
FAIR https://www.go-fair.org/
geomodel-2-3dweb https://github.com/AuScope/geomodel-2-3dweb
GeoNetwork https://www.GeoNetwork-opensource.org/
GPT-J https://en.wikipedia.org/wiki/GPT-J
ISO19115-3 XML https://www.GeoNetwork-opensource.org/manuals/4.0.x/en/annexes/standards/iso19115-3.2018.html
ISO19139 XML https://GeoNetwork-opensource.org/manuals/4.0.x/en/annexes/standards/iso19139.html
OAI-PMH https://www.openarchives.org/pmh/
pygeometa https://geopython.github.io/pygeometa/
T5 https://huggingface.co/docs/transformers/model_doc/t5
USGS Thesaurus https://apps.usgs.gov/thesaurus/
WebGL https://en.wikipedia.org/wiki/WebGL
YAKE https://pypi.org/project/yake/
References
T5-Base Raffel, C., Shazeer, N., Roberts, A., Lee, K., Narang, S., Matena, M., ... & Liu, P. J. (2020). Exploring the limits of transfer learning with a unified text-to-text transformer. J. Mach. Learn. Res., 21(140), 1-67.
YAKE Campos, R., Mangaravite, V., Pasquali, A., Jatowt, A., Jorge, A., Nunes, C. and Jatowt, A. (2020). YAKE! Keyword Extraction from Single Documents using Multiple Local Features. In Information Sciences Journal. Elsevier, Vol 509, pp 257-289. https://doi.org/10.1016/j.ins.2019.09.013
XML
Results
Samples of augmented GeoNetwork records (ISO19115-3 XML):
Sandstone http://portal.auscope.org.au/GeoNetwork/srv/api/records/9d8d8f91-39b9-454b-b47b-8bb231e710bc/formatters/xml (Source: Western Australian Department of Mines, Industry Regulation and Safety https://www.dmp.wa.gov.au/)
Curnamona Province http://portal.auscope.org.au/GeoNetwork/srv/api/records/7b38d137-9600-4f61-8f29-c90ffbb82229/formatters/xml (Source: Department for Energy and Mining https://www.energymining.sa.gov.au/)
Samples of generated GeoNetwork records (ISO19115-3 XML):
Otway http://portal.auscope.org.au/GeoNetwork/srv/api/records/c32245c9-0d11-403d-8772-fa9ac41cdb15/formatters/xml (Source: Earth Resources Victoria https://earthresources.vic.gov.au/)
Bendigo http://portal.auscope.org.au/GeoNetwork/srv/api/records/3b3fa2fa-7967-470c-baef-45e6abbf1169/formatters/xml (Source: Earth Resources Victoria https://earthresources.vic.gov.au/)
Output ISO19115
(bas-metadata-library)
Insert missing fields via XSLT (lxml)
Geomodels website model creation process
Conclusion
This exercise has shown that a set of Python scripts can complete many of the fields required to fill out a minimal ISO19115 metadata record, without the need for human input. The generation of a human-like summary/description field could be improved with the use of larger language models and more compute power.
Future improvements:
Improve accuracy by training models with geological texts
Use larger, more powerful language models (e.g. GPT-J)
Display metadata directly in Geomodels Portal
Metadata generation process
Introduction
This poster documents the exploitation of recent advancements in open source metadata software and natural language processing/machine learning software in order to generate metadata records for geological models. Using modest compute resources ISO19115 metadata records can be generated from a variety of different sources, for example websites, metadata catalog services and geological PDF reports, as well as model files sourced from geological software applications. Each source has a different amount of metadata. The challenge lies in folding the wide swathe of sources into one type of metadata record and bolstering the poorest sources so that all records contain an adequate minimal set of fields.
Process
Acknowledgements: AuScope and NCRIS funding
website
XML