## Slide 1
Towards Temporal Scaling Laws for the Risk Analysis of Rare Flood Events
Kanneganti Bhargav Kumar1 and Pradeep P Mujumdar1,2
1Department of Civil Engineering, Indian Institute of Science, Bengaluru, India (kannegantibhargavkumar@gmail.com)
2Interdisciplinary Centre for Water Research, Indian Institute of Science, Bengaluru, India
INTRODUCTION
Extreme flood events are rare but catastrophic and have tremendous adverse impacts on human lives and the economy.
To estimate the extreme quantiles of flood risk, traditional methods depend on historical data recorded at gauge stations, assuming that they capture a spectrum of extreme flood magnitudes.
However, the available gauge station record lengths are often small for several gauge stations, and these records are less likely to capture the full range of likely flood magnitudes.
Therefore, there is a need to develop methods that can better extrapolate the dynamics of large and rare events from historical data containing only small but frequent fluctuations.
CONCLUSIONS
OBJECTIVES
Perform detrended fluctuation analysis to understand the long term correlations in streamflow series.
Estimation of probability distribution function of return intervals to understand occurrence of each extreme return intervals.
Estimation of threshold invariant scaling laws to extrapolate the risk to large to rare events.
ACKNOWLEDGEMENTS
The first author acknowledges the financial support received through the Prime Ministers' Research Fellowship (ID no: 0200367), The Ministry of Education, Government of India. This work was partially funded by the project, “Advanced Hydrologic Research and Knowledge Dissemination” sponsored by the Ministry of Earth Sciences, Government of India (Project No. MOES/PAMC/H&C/41/2013-PC-II). The second author acknowledges the support received through the J.C. Bose Fellowship (grant number JCB/2018/000031).
STUDY AREA AND DATASETS
Figure 1: Geographical extent of the study region, and streamflow gauge locations in peninsular India.
Figure 2: Histogram of streamflow records length(years) in study region.
RESULTS
It is observed that return intervals are long term correlated with same exponent as original record for long time scales.
This may indicate large and small return intervals are not arranged in random fashion but are expected to form clusters.
The streamflow series show that the Hurst exponent values of 35 streamflow series greater than 1.0 which indicates hydrologic processes in these catchments are non-stationary.
A threshold invariant scaling relationships are observed for the return intervals of extreme events in the study regions. These relationships can be helpful in extrapolating the risk associated with rare events at a specific site.
METHODOLOGY
Figure 3: Histogram of the Hurst exponent(H) for 242 daily discharge series of peninsular India.
Step -3
Step-1
Step -2
Step -4
Step -5
Future step
RESULTS
The framework is implemented at all gauge stations of study region, but for the purpose of illustration, results at Warunji station in Krishna basin, India are presented.
Figure 4:Double logarithmic plots of the fluctuation functions versus window length(S) obtained from
Figure 5: (a) Discharge of the Krishna river at Warunji gauge station (from 1 July 2006 until 31 October 2007).The seasonal trend(black line) and the seasonal standard deviation (magenta dotted line). (b) Corresponding detrended dataset. The horizontal lines in the detrended records refer to two thresholds and , with return periods of 64 and 118 days, respectively.
Step-1
Step-2
Step-3
Step -4
The distribution of return intervals is
Where,
Step -5
Figure 7: Distribution of of the return intervals of the thresholds 64 , black colour), 118 , orange colour) for streamflow data at warunji, Krishna basin, India. The slope of the both lines are same indicating a threshold invariant relation between return levels of events.
Figure 6: Autocorrelation functions(ACFs) of the original data and of the return interval series for = 118 (blue circles) and =64(red circles).The ACFs of both original data and return interval series are characterised by the same exponent for long time scales.
Long term memory implies slowly decaying auto correlation function(like shown in Figure 6) that decays by a power law i.e., In this case, the intervals between events are likely to be long term correlated with same exponent as the original record.
The presence of long term memory in series significantly alter the occurrence of extreme events.
The distribution of the return intervals, for and for two thresholds as a function of , where is the mean return interval is shown in Figure 7.
The is only function of ratio , this scaling is important, since it allows us to extrapolate the behaviour at very large values from the behaviour at smallvalues that are not rare.
Step -5