## Slide 1
Probabilistic modelling of water distribution networks and resilient reduction of leakages: Large scale application to the city of Patras in western Greece
Athanasios V. Serafeim, Department of Civil Engineering, University of Patras, Greece
George Kokosalakis, School of Business and Economics Department of Maritime Transport and Logistics, Deree American College of Greece, Athens, Greece
Roberto Deidda, Dipartimento di Ingegneria Civile, Ambientale ed Architettura Università degli Studi di Cagliari
Nikolaos Th. Fourniotis, Department of Civil Engineering, University of the Peloponnese, Patras, Greece
Irene Karathanasi, Municipal Enterprise of Water Supply and Sewerage of the City of Patras, Patras, Greece
Andreas Langousis, Department of Civil Engineering, University of Patras, Patras, Greece
EGU General Assembly 2023

## Slide 2
Initial
Final

## Slide 3
Irrespective of their age, water distribution networks (WDNs) exhibit water losses with important environmental and financial consequences.
Their quantification is a crucial task towards the development of proper strategies to reduce them and therefore increase the network’s efficiency.
Water losses undermine WDNs’ financial viability, as the lost water (which remains unbilled) results in the reduction of the net revenue while increasing the overall operational cost of the water supply agency.
1
Introduction

## Slide 4
System Input Volume (SIV)
Authorized Consumption
(AC)
Water Losses
(WL)
Apparent Losses
(AL)
Billed Metered Consumption
Billed Unmetered Consumption
Sold Water in other Water Agencies
Unbilled Metered Consumption
Unbilled Unmetered Consumption
Unauthorized Consumption (UC)
Inaccuracies and Data Errors
Leakage in Transmission and Distribution
Service Connection Leaks
Storage Leaks and Tanks Overflows
Unbilled Authorized Consumption
(UAC)
Billed Authorized Consumption
(BAC)
Real Losses
(RL)
Revenue Water
(RW)
Non-Revenue Water
(NRW)

## Slide 5
Global Non-Revenue Water
Chart: 
| colored | blank
% | 17.5 | 82.5
North America
Level of NRW: 17.5%
NRW: 119 l/capita/d
Cost: 0.38 USD/m3
Latin America and the Caribbean
Level of NRW: 42.3%
NRW: 121 l/capita/d
Cost: 0.32 USD/m3
Chart: 
| colored | blank
% | 42.3 | 57.5
Africa
Level of NRW: 36.5%
NRW: 64 l/capita/d
Cost: 0.25 USD/m3
Chart: 
| colored | blank
% | 36.5 | 63.5
Australia and New Zealand
Level of NRW: 15.0%
NRW: 36 l/capita/d
Cost: 0.38 USD/m3
Chart: 
| colored | blank
% | 15 | 85
Chart: 
| colored | blank
% | 29.2 | 70.8
Europe
Level of NRW: 29.2%
NRW: 50 l/capita/d
Cost: 0.35 USD/m3
Chart: 
| colored | blank
% | 21 | 50
East Asia
Level of NRW: 21.0%
NRW: 42 l/capita/d
Cost: 0.34 USD/m3
129 billion Cubic meters per year, which cost 39 billion USD.
By: Liemberger, R.; Wyatt, A. Quantifying the global non-revenue water problem. Water Supply 2018, 19, 831–837. https://doi.org/10.2166/ws.2018.129.

## Slide 6
NRW Reduction Steps
Most commonly through network sectorization into Pressure Management Areas (PMAs) towards effective pressure regulation to the lowest permissible level.
Leakage Reduction
All network’s specific characteristics (i.e., altimetry, length of the pipeline grid, pipe diameters, density of connections, system input volume, operating pressures, user’s consumption)
Data Collection
The most common approaches for real losses (i.e., leakage) estimation are: a) the IWA water balance (top-down) and b) the Minimum Night Flow (MNF; bottom-up)
Leakage estimation
Probabilistic modeling and optimization of leakages in water distribution networks

## Slide 7
Probabilistic Leakage Estimation
Herein we introduce two alternative probabilistic approaches for minimum night flow (MNF) estimation in water distribution networks (WDNs), which are particularly suited to minimize noise effects, allowing for a better representation of the low flows during night hours, as well as the overall condition of the network. Their strong point is that they both allow for confidence interval estimation of the observed MNFs.
2

## Slide 8
Estimate MNF as the ensemble mean , of the minimum average flows over duration D in the low consumption period of the year (November - February):
u is the night hour range (in our case 12:00 am - 6:00 am)
D is a properly selected averaging duration
increases with increasing D
is the flow time series at its nominal resolution in day j
The observed minima increase fast with increasing size of the averaging window D up to 60 min, with the minimum rate of increase being observed somewhere between 60 and 120 min.
Method 1

## Slide 9
Estimate MNF as the ensemble mean, , of the lowest modal values observed during the night hours of different days j in the low consumption period of the year (November - February):
is the lowest modal value of the empirical probability density function (PDF).
n is the number of days.
Region A contains flow values observed between 00:00 am - 01:05 am (late night), Region B is composed by flow values observed between 01:05 am – 03:40 am (late night) and 05:40 am – 06:00 am (early morning), and Region C includes the low flows during the night hours from 03:40 am – 05:40 am.
An important observation is that the lowest modal value (i.e. the lowest most frequent value) of the distribution is observed in Region C, and can be considered representative of the MNF, as the latter is linked to the most probable low-consumption state of the PMA during night hours, when human activity is minimal.
Method 2
(L/s)
time
Region A
Region B
Region C
Region C
Region B
Region A
Region B
a
(L/s)
PDF
Region C
Region B
Region A
Lowest Mode
b
6 December 2019

## Slide 10
Data and Area of Application
Area of Application
The network consists of more than 700 km of (mainly) HDPE and PVC pipes, covers an area of approximately 27 km2, serves more than 200000 consumers and is divided into 86 PMAs.
Flow – Pressure Data
Flow – pressure data at 1 min temporal resolution for the 4 -month low consumption period of the year, from 01 Nov. 2018 – 28 Feb. 2019, were acquired from the pressure regulation stations of the WDN of the City of Patras in Western Greece.
Quality assessment
Flow – pressure data were quality assessed to detect and remove errors related to communication glitches. Finally, 65, out of 86, PMAs were used for MNF estimation.

## Slide 11
Application Results
The point estimates and 95% - confidence interval estimates of the average MNF obtained using the 2 methods lie along the 1-1 line.
Although conceptually and methodologically different, the two approaches converge to very similar results, indicating the robustness of the developed approaches
(l/s)
1:1 - line
measurements
20
40
60
10
30
50
70
10
30
50
70
0
20
40
60
(l/s)
0

## Slide 12
Pressure Tests
In PMAs where the normality assumption is substantiated statistically, MNF increases with increasing inlet pressures, according to Torricelli's law (extended leakages indicator).
In PMAs where the normality assumption is not statistically significant, MNF is not affected by pressure changes (good condition indicator).
Flow-pressure tests conducted in 43 out of the 65 PMAs studied. Three different night pressure set points were applied for a minimum of 5 nights each.

## Slide 13
Comparison between WB and MNF approaches
PMA name | WB RL (%) | MNF RL low limit (%) | MNF RL upper limit (%) | Absolute relative difference (%)
Boud | 38.05 | 41.04 | 41.36 | 7.28 – 7.99
Kentro | 48.41 | 46.37 | 47.32 | 2.30 – 4.39
Panachaiki | 30.66 | 28.99 | 30.28 | 1.25 – 5.77
Prosfygika | 53.72 | 58.40 | 59.39 | 8.01 – 9.54
Estimates of real losses (RL) obtained using the water balance (WB) and MNF approaches as a fraction of the system input volume (SIV)
The two approaches lead to very similar results, with absolute relative differences lower than 10% for all 4 PMAs. This indicates that the top-down (water balance) and bottom-up (MNF) approaches effectively converge when:
  The network’s specific characteristic are known and there is sufficient understanding of the consumption types and patterns during day and night hours, and
  MNF estimation is done in a rigorous statistical setting from high resolution flow-pressure timeseries.

## Slide 14
Partitioning
Herein we use hierarchical clustering enriched with topological proximity constrains to develop an approach for the optimal sizing and allocation of PMAs (or DMAs) in water distribution networks, which seeks for minimization of leakages in WDNs while maintaining a sufficient level of hydraulic resilience. To quantify the latter, we introduce a resilience index that accounts for water leakages and nodal heads in a pressure driven and mixed pressure - demand ways, respectively.
3

## Slide 15
Sectorization Steps
Analytical estimation of the Water Balance Equilibrium using the probabilistic Minimum Night Flow method described in Section 2, for the optimal estimation of leakages
Water Equilibrium
Nodal density should be high enough to effectively describe both the area’s topographic variability as well as the original connectivity of the network, while taking into account all necessary hydraulic parameters
Design of network’s hydraulic model
Distribute the water demand at each computational node of the network, as the sum of a demand-driven and a pressure-driven component
Distribution of Water Balance components
System input volume estimation using flow timeseries and allocation to its components using user’s consumption data and operating pressures
Nodes at: a) intersections between two or more pipes, b) changes in pipes’ diameters and/or material, c) fire hydrant locations, d) dead ends, and e) at high water demand locations
Initial distribution of all components using nodal active lengths

## Slide 16
We use a variant of the original Todini’s index that accounts for the leakages and nodal heads in a pressure driven and mixed pressure-demand ways, respectively.
Estimation of initial hydraulic resilience
We use a hierarchical clustering approach enriched with topological proximity constrains to develop an algorithm for the optimal sizing and allocation of PMAs
Hierarchical clustering
Selection of a proper solution is case specific, providing an optimal balance between RL reduction and the resulting hydraulic resilience level of the entire network.
Selection of the proper solution
Based on the clustering approach of Deidda et al., (2021) which has already been tested in hydrological applications
Application results in a pool of possible partitioning alternatives, each one having a different number of clusters.
While nodal pressure directly affects the leakage flow rates as well as the crack expansion rates, we re-distribute the RL component as a function of nodal pressures.
Distribution of leakages
Deidda, R.; Hellies, M.; Langousis, A. (2021) A critical analysis of the shortcomings in spatial frequency analysis of rainfall extremes based on homogeneous regions and a comparison with a hierarchical boundaryless approach. Stoch Environ Res Risk Assess, 35, 2605–2628. https://doi.org/10.1007/s00477-021-02008-x .

## Slide 17
Data and Area of Application
Area of Application
The 4 largest pressure management areas (PMAs) of the city of Patras, which consist of more than 200 km of (mainly) HDPE and PVC pipes, cover the entire city center of Patras, and serve approximately 58 000 consumers.
Flow – Pressure Data
Users’ consumption and flow-pressure data at 1 min temporal resolution for the 4-month low consumption period of the year (from 01 November 2018 to 28 February 2019) were acquired for each of the 4 installed stations
The network’s specific characteristics
All Topographic (e.g., mean elevation of the PMA), Pipeline related (e.g., mean diameter of the pipeline grid) and operational (e.g., inlet point hydraulic head) characteristics of the PMAs.

## Slide 18
Water Equilibrium and Hydraulic Models

## Slide 19
Final Partitioning “Boud”
2
3
1
-28.6%

## Slide 20
Final Partitioning “Kentro”
2
1
-13.7%

## Slide 21
Final Partitioning “Panachaiki”
2
3
1
-19.3%

## Slide 22
Final Partitioning “Prosfygika”
2
3
1
- 40.9%

## Slide 23
When high-resolution flow time series are available, the probabilistic MNF method should be used.
Introduced a user unbiased, clustering methodology, that uses the original pipeline grid as a connectivity matrix leading to realistic results while requiring minimal processing power.
When the MNFs do not follow the normal distribution, it is a strong sign that the PMA is in good overall condition
4
Conclusions
Future Work??

## Slide 24
For more info
01
02
03
Serafeim, A.V.; Kokosalakis, G.; Deidda, R.; Karathanasi, I. and Langousis, A. (2021) Probabilistic estimation of minimum night flow in water distribution networks: large-scale application to the city of Patras in western Greece, Stoch. Environ. Res. Risk. Assess., https://doi.org/10.1007/s00477-021-02042-9.
Serafeim, A.V.; Kokosalakis, G.; Deidda, R.; Karathanasi, I.; Langousis, A. (2022) Probabilistic Minimum Night Flow Estimation in Water Distribution Networks and Comparison with the Water Balance Approach: Large-Scale Application to the City Center of Patras in Western Greece, Water, 14, 98, https://doi.org/10.3390/w14010098.
Serafeim, A.V.; Kokosalakis, G.; Deidda, R; Karathanasi, I.; Langousis, A. (2022) Probabilistic framework for the parametric modeling of leakages in water distribution networks: large scale application to the City of Patras in Western Greece, Stoch. Environ. Res. Risk Assess. https://doi.org/10.1007/s00477-022-02213-2.
EGU General Assembly 2023
04
Serafeim, A.V.; Kokosalakis, G.; Deidda, R; Fourniotis N.Th.; Langousis, A. (2022) Combining Statistical Clustering with Hydraulic Modeling for Resilient Reduction of Water Losses in Water Distribution Networks: Large Scale Application Study in the City of Patras in Western Greece, Water, 14(21), 3493. https://doi.org/10.3390/w14213493.

## Slide 25
The research work was supported by the Hellenic Foundation for Research and Innovation (H.F.R.I.) under the “First Call for H.F.R.I. Research Projects to support Faculty members and Researchers and the procurement of high-cost research equipment grant” (Project Number: 1162).
Acknowledgements
EGU General Assembly 2023

## Slide 26
Thank you for your Attention
EGU General Assembly 2023