## Slide 1: A novel approach to improve the accuracy of locating agricultural tile drain and ditch networks
April 2023
By:
Estifanos Addisu, Shahla Yadollahi, Fatima-Ezzahra Riakhi, Imeshi Weerasinghe, Charlotte Wirion,
Jiri Nossent , Ann van Griensven

## Slide 2
Introduction and Problem statement
Drainage units (subsurface – tile drains / surface – ditches are needed!)

## Slide 3
Introduction and Problem statement
Advantages and disadvantages of drainage units
Advantages
Disadvantages
Increases crop productivity
Consistent yields
Fewer plant diseases
Increased water loss from GW
Increased ET
Increased pollutant transport
Increased vulnerability to drought
Increased salinity
Impact on water quality

## Slide 4
Introduction and Problem statement
Hence, they are important elements to investigate further!
However, their location is not well identified
Keep in mind agricultural drainage started centuries ago (2000 BC)
Decision tree classification (DTC)
Remote sensing-based approaches (RS)

## Slide 5
Apply already existing methodologies of drainage unit identification
Research objective
Apply novel additional filtering technique to improve the accuracy

## Slide 6
Study area and methodology

## Slide 7
Study area and methodology
Two already existing approaches applied  DTC and RS
1. Decision tree classification (DTC) – based on different land use, drainage class and slope

## Slide 8
Study area and methodology
2. RS-based approach
- Applying orbit file
- Thermal noise removal
- Radiometric calibration
- Speckle filtration
- Terrain correction
- Subset the study area out of the whole tile
https://github.com/google/snappy
Major steps:
Select a date with significant rainfall event (e.g around 25 mm)
Acquire surface reflectance imagery for days before and after the rainfall event
Deduct the imagery values after and before the rainfall event

## Slide 9
3. What do you think is missing?
Study area and methodology
Groundwater is the cause for drainage unit application, but its not used in any of the methods to identify drainage units

## Slide 10
Results
1. RS based approach (Ontario – Canada)

## Slide 11
Results
1. RS based approach (Ontario – Canada)
Accuracy of 87.8%

## Slide 12
Results
1. RS based approach (Kleine Nete - Belgium)
Accuracy of 17.3%

## Slide 13
Results
2. DTC (Ontario - Canada)

## Slide 14
Results
2. DTC (Ontario - Canada)
Accuracy of 96.7%

## Slide 15
Results
2. DTC (Kleine Nete)

## Slide 16
Results
2. DTC (Kleine Nete)
Accuracy of 58%

## Slide 17
Results
3. Additional technique based on groundwater (Ontario - Canada)
Additional 19.4 km2 area identified

## Slide 18
Results
1. Additional technique based on groundwater (Kleine Nete - Belgium)

## Slide 19
Conclusions
RS approach has indicated an accuracy of 87.8% for case study 1  useful method
  1.1 But for the second case study, it resulted in poor performance  the method is not always accurate
DTC resulted in 96.75 and 58% accuracy for the first and second case study area, respectively.
The novel approach of using groundwater increased the accuracy of RS by 19.4km2 area

## Slide 20: How will this affect the hydrology? Next question
for your time