## Slide 1
Using ambient vibration data for
predicting site amplification
for the city of Lucerne (Switzerland):
comparison between canonical correlation and
hybrid standard spectral ratio methods
Paulina Janusz 1, Francesco Panzera 1,2, Vincent Perron3, Paolo Bergamo1, Donat Fäh1
1SED, ETH Zürich, Switzerland
2University of Catania, Italy
3CEA, France
paulina.janusz@sed.ethz.ch

## Slide 2: Introduction
paulina.janusz@sed.ethz.ch

## Slide 3
Seismic risk in urban areas
theguardian.com
Urban vulnerability
Site effects
Mexico 1985
+
=
Elevated seismic risk
Introduction
Ciaccio and Cultrera (2014)
paulina.janusz@sed.ethz.ch

## Slide 4
How to get site amplification?
Introduction
paulina.janusz@sed.ethz.ch
Ambient noise
Direct measurements
Expensive
Time-consuming
Earthquakes
Proxies
Aim: spatial variability of the soil response
Cheap and fast
Quite inaccurate
Relatively cheap and fast
Quite good estimate
Just an estimate
Only some methods

## Slide 5
The idea and case study
Introduction
paulina.janusz@sed.ethz.ch
Comparison of two noise-based methods:
canonical correlation (CC)
hybrid standard spectral ratio (SSRh)
Case study:
LUCERNE in Central Switzerland
Low-to-moderate seismicity area with some strong historical earthquakes
SEISMIC HAZARD MAP
Mw 5.9 in year 1601
Lucerne
SA 5Hz 10% in 50 years
seismo.ethz.ch
Idea:
Very soft alluvial deposits (Vs30 ~ 300m/s)

## Slide 6: Methods and data
paulina.janusz@sed.ethz.ch

## Slide 7
Methods
paulina.janusz@sed.ethz.ch
Hybrid Standard Spectral Ratio
(SSRh - Perron et al., 2018)
earthquake recordings + ambient vibration
relatively cheap and fast, high spatial resolution
Janusz et al. 2022, Frontiers in Earth Science
rock
sediments
earthquake
ambient noise
Earthquake ground motion
Ambient noise recording

## Slide 8
Canonical correlations (CC, Cultrera et al. 2014, Panzera, et al. 2021, BSSA)
Methods
paulina.janusz@sed.ethz.ch
Empirical Amplification Functions
(EAF, Edwards, et al. 2013)
Earthquake ground motion
Direct measurement
Horizontal-to-Vertical spectral ratios
(H/V, Nakamura, 1989)
Ambient noise recording
Just a proxy of amplification
CORRELATION
of EAF and H/V
Seismic stations of Swiss network
Panzera, et al. 2021, BSSA
PREDICTING
EAF from H/V

## Slide 9
Data
paulina.janusz@sed.ethz.ch
Seismic stations
velocimeters
accelerometers
Ambient vibration measurements
100 points (2020-2021)
213 points (2001-2016)
Verification
SSRh amplification map
CC amplification map
map.geo.admin.ch

## Slide 10: Results
paulina.janusz@sed.ethz.ch
Comparison and verification

## Slide 11
Comparisons
Increased seismic hazard !!!
map.geo.admin.ch

## Slide 12
Comparisons
Increased seismic hazard !!!
map.geo.admin.ch

## Slide 13
Deep basin
SSRh > CC
Basin borders
SSRh < CC
Which is closer to the reality?
Comparisons
SSRh/CC amplification
map.geo.admin.ch

## Slide 14
Verification
paulina.janusz@sed.ethz.ch
Mean absolute error (MAE)
All seismic stations
SSRh generally better than CC
Good performance for both

## Slide 15
Deep basin
SSRh > CC
Basin borders
SSRh < CC
Comparisons
SSRh/CC amplification
map.geo.admin.ch
SSRh better
CC better
Deep basin
SSRh > CC
Basin borders
SSRh < CC
Closer to the reality?
Conservative model:
SSRh in deep basin
CC at the borders

## Slide 16: Summary and conclusions
paulina.janusz@sed.ethz.ch

## Slide 17
Summary
paulina.janusz@sed.ethz.ch
Both CC and SSRh:
reasonable estimate of amplification
increased seismic hazard for Lucerne
Even though,
SSRh performs generally better,
CC has wide applications

## Slide 18
References
paulina.janusz@sed.ethz.ch
Ciaccio, M. G. and Cultrera, G. (2014). Terremoto e rischio sismico, Ediesse, Italy
Cultrera, G., V. De Rubeis, N. Theodoulidis, H. Cadet, and P. Y. Bard (2014). Statistical correlation of earthquake and ambient noise spectral ratios, Bull. Earthq. Eng. 12, 1493–1514.
Edwards, B., Michel, C., Poggi, V., Fäh, D. (2013). Determination of Site Amplification from Regional Seismicity: Application to the Swiss National Seismic Networks. Seismol. Res. Lett. 84, 611–621. https://doi.org/10.1785/0220120176
Janusz, P., Perron, V., Knellwolf, C., & Fäh, D. (2022). Combining Earthquake Ground Motion and Ambient Vibration Recordings to Evaluate a Local High-Resolution Amplification Model—Insight From the Lucerne Area, Switzerland. Frontiers in Earth Science, 10. https://doi.org/10.3389/feart.2022.885724
Nakamura, Y., 1989. A method for dynamic characteristics estimation of subsurface using microtremor on the ground surface. Railw. Tech. Res. Inst. Q. Rep. 30, 25–33.
Panzera, F., Bergamo, P., & Fäh, D. (2021). Canonical Correlation Analysis Based on Site‐Response Proxies to Predict Site‐Specific Amplification Functions in Switzerland. Bulletin of the Seismological Society of America. https://doi.org/10.1785/0120200326
Perron, V., Gélis, C., Froment, B., Hollender, F., Bard, P.-Y., Cultrera, G., Cushing, E.M. (2018). Can broad-band earthquake site responses be predicted by the ambient noise spectral ratio? Insight from observations at two sedimentary basins. Geophys. J. Int. 215, 1442–1454. https://doi.org/10.1093/gji/ggy355