## Slide 1: Heavy Metal Contamination in Ganga River Basin Sediments, India
Presented By: Stuti Kushwaha
School of Environmental Sciences, Jawaharlal Nehru University, New Delhi, India

## Slide 2
Study Region

## Slide 3
Metal | Rainy Season | Dry Season
Co | 14.07 | 11.08
Cr | 49.52 | 61.38
Cu | 29.46 | 45.15
Ni | 28.03 | 23.62
Zn | 123.52 | 69.54
Average Concentrations in mg/kg
Rainy Season
Dry Season

## Slide 4
Introduction

## Slide 5: Description of Sampling Locations:
Sample id | Co-Ordinates |  | 
 | Rishikesh- Haridwar |  | 
T1 | N 30°02.248', E 78°14.691' |  | 
T2 | N 30°00.045', E 78°12.412' |  | 
T3 | N 30°01.920', E 78°16.498' |  | 
G1 | N 29°53.591', E 78°10.224' |  | 
 | Chambal- Yamuna |  | 
T'1 | N 26°32.730', E 79°05.422' |  | 
T4 | N 26°30.011', E 79°15.201' |  | 
T5 | N 26°25'29'', E 79°14'33'' |  | 
 | Kanpur |  | 
G2 | N 26°37.079', E 80°16.385' |  | 
G3 | N 26°22.785', E 80°29.666' |  | 
 | Allahabad |  | 
G4 | N 25°30.849', E 81°41.179' |  | 
T6 | N 25°20.644', E 81°38.374' |  | 
G5 | N 25°24.531', E 81°53.584' |  | 
Sample id | Co-Ordinates |  | 
 | Near Balia |  | 
G6 | N 25°46.601', E 84°23.166 |  | 
 | Ghaghara river |  | 
T7 | N 25°49.510', E 84°35.002' |  | 
 | After confluence |  | 
G7 | N 25°43.229', E 84°48.680' |  | 
 | Son River |  | 
T8 | N 25°31.744', E 84°45.604' |  | 
 | Gandak River |  | 
T9 | N 25°41.999', E 85°11.318' |  | 
T10 | N 25°41.989', E 85°11.812' |  | 
 | After confluence |  | 
G8 | N 25°32.963', E 85°16.691' |  | 
G9 | N 25°24.161', E 85°54.973' |  | 
 | Bhagalpur |  | 
T11 | N 25°25.403', E 87°03.579' |  | 
T12 | N 25°05.826', E 87°53.401' |  | 
 | West Bengal |  | 
G10 | N 23°37.455', E 88°11.124' |  | 
G11 | N 23°31.946', E 88°21.899' |  | 
G12 | 22°56'31''N, 88°24'28''E |  | 
 | Gomati |  | 
T13 | N 25°30.377', E 83°08.498' |  | 

## Slide 6: Objectives:
To find the variation in heavy metal concentration in wet and dry season
To find the possible sources of heavy metals
To evaluate the risk imposed by heavy metals

## Slide 7: Methodology:
Sample collection
Representative samples were collected in a plastic bag from stainless steel scoop, transferred to laboratory and kept below 4˚C
Pre-processing before digestion
Samples were completely dried and room temp. and sieved from 0.63µm sieve
Sample Digestion
Using the‘B’ solution method by Shapiro and Brannock (1962)
Sample Analysis
Digested samples analysed in ICP-OES Agilent (5110)
Quality Control: Buffalo river sediment SRM(8704), Blanks, Sample replicates were ran.
Samples were completely dried at room temp. and sieved from 0.63µm sieve
Using the‘B’ solution method by Shapiro and Brannock (1962)

## Slide 8
Heavy Metals in Rainy and Dry Season
Metal | Rainy Season | Dry Season
Co | 14.07 | 11.08
Cr | 49.52 | 61.38
Cu | 29.46 | 45.15
Ni | 28.03 | 23.62
Zn | 123.52 | 69.54
Average Concentrations in mg/kg
Co
Cr

## Slide 9: Heavy Metals in Rainy and Dry Season:
Ni
Ni
Zn
Cu

## Slide 10: Correlation for Rainy and Dry Season:
Grey shade indicating, p≤0.05
Rainy Season
Dry Season
Strong correlation is found between Co-Cr, Co-Ni ,Cr-Ni
Strong correlation is found between Cr-Ni, Cu-Zn

## Slide 11: Contamination Factor:
Rainy Season
Cf=Cmetal/Cbackground
Where, Cmetal - concentration of metal
Cbackground – values adopted from (Singh et al., 2003)
If: Cf<1 Low Contamination 1<Cf<3 Moderate Contamination 3<Cf<6 Considerable Contamination >6 Very High Contamination
Cf indicates low to moderate contamination in rainy season at some location for Co and Zn.
While moderate contamination of Zn at G5 location in Dry season.

## Slide 12: Pollution Load Index:
If, PLI=0 perfection
PLI =1 baseline level
PLI>1 polluted
PLI=
Where, Cf =contamination factor of metal
n =number of metals
PLI>1 for (G5) in Dry season, indicating polluted sediment

## Slide 13: Ecological Risk:
Rainy Season
Eri=
Where, Ci = concentration of metal i in sediment
Co= background concentration of metal
Tr =biological toxicity factor for individual metal
Er <40 for both the seasons, showing low risk

## Slide 14: Potential Ecological Risk:
Chart: RI (Dry Season)
RI=
Where, = concentration of metal i in sediment
= background concentration of metal
Tr =biological toxicity factor for individual metal
RI<150 for both the seasons , indicating low risk

## Slide 15: Conclusion:
• High conc. of Cr, Cu in dry season is probably from their natural sources.
• Moderate contamination of Zn indicates its anthropogenic origin.
• Strong correlations between Co-Cr, Co-Ni ,Cr-Ni (RS) and Cu-Zn and Cr-Ni(DS) indicates similar sources and their geochemical behaviour.
• Below Detection values at T10 location probably due to the dilution or washout of the metals or absence of metal in the source rock.
• Low ecological risk found for both seasons. PLI suggests pollution at G5 location.

## Slide 16: References:
Rapid analysis of silicate, carbonate, and phosphate rocks. (n.d.). Retrieved April 20, 2023, from https://pubs.er.usgs.gov/publication/b1144A
Frogner-Kockum, P., Göransson, G., & Haeger-Eugensson, M. (2020). Impact of Climate Change on Metal and Suspended Sediment Concentrations in Urban Waters. Frontiers in Environmental Science, 8. https://www.frontiersin.org/articles/10.3389/fenvs.2020.588335
Singh, M., Müller, G., & Singh, I. B. (2003). Geogenic distribution and baseline concentration of heavy metals in sediments of the Ganges River, India. Journal of Geochemical Exploration, 80, 1–17. https://doi.org/10.1016/S0375-6742(03)00016-5

## Slide 17
Thank you