## Slide 1: Improving methods to calculate monthly water budget for Lake Velence, Hungary
Máté Chappon – PhD candidate - chappon.mate@sze.hu
Katalin Bene PhD – associate professor - benekati@sze.hu
National Laboratory for Water Science and Water Security, Széchenyi István University, Department of Transport Infrastructure and Water Resources Engineering, Hungary
EGU23 - General Assembly
Section: HS 2.5.2
Abstract: EGU23-8334
PICO presentation
Vienna, 26th April 2023.

## Slide 3: Water level hit negative record in 2022
Chart: [mm]
| 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Z i | -132 | -70 | 31 | -48 | -90 | -75 | -45 | -122 | 73 | -105 | -65 | 7 | -70 | -45 | 72 | -66 | -115 | -93 | -157 | -155 | -86 | 67 | -65 | -19 | -187 | -57 | -102 | -13 | -63 | -14 | -31 | -60 | -78 | -141 | -124 | -104 | -226
ΣΔH(M) - MEASURED | -160 | 0 | -160 | -260 | -530 | -430 | -510 | -370 | -190 | 60 | 80 | -40 | 70 | 120 | -200 | -140 | -310 | -610 | -420 | 120 | -120 | -120 | -140 | -170 | 30 | -190 | -410 | -150 | 10 | -20 | -30 | -240 | -180 | -220 | -470 | -660 | -850

## Slide 4: What is wrong with the current calculation method?
Chart: [mm]
| 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Z i | -132 | -70 | 31 | -48 | -90 | -75 | -45 | -122 | 73 | -105 | -65 | 7 | -70 | -45 | 72 | -66 | -115 | -93 | -157 | -155 | -86 | 67 | -65 | -19 | -187 | -57 | -102 | -13 | -63 | -14 | -31 | -60 | -78 | -141 | -124 | -104 | -226
ΣΔH(M) - MEASURED | -160 | 0 | -160 | -260 | -530 | -430 | -510 | -370 | -190 | 60 | 80 | -40 | 70 | 120 | -200 | -140 | -310 | -610 | -420 | 120 | -120 | -120 | -140 | -170 | 30 | -190 | -410 | -150 | 10 | -20 | -30 | -240 | -180 | -220 | -470 | -660 | -850
ΣΔH(C) - CALCULATED | -292 | -202 | -331 | -479 | -839 | -814 | -939 | -921 | -668 | -523 | -568 | -681 | -641 | -636 | -884 | -890 | -1175 | -1568 | -1535 | -1150 | -1476 | -1409 | -1494 | -1543 | -1530 | -1807 | -2129 | -1882 | -1786 | -1830 | -1871 | -2141 | -2159 | -2340 | -2714 | -3008 | -3424

## Slide 5: What is wrong with the current calculation method?
www.dimensions.com/element/basketball-hoop
Chart: [mm]
| 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Z i | -132 | -70 | 31 | -48 | -90 | -75 | -45 | -122 | 73 | -105 | -65 | 7 | -70 | -45 | 72 | -66 | -115 | -93 | -157 | -155 | -86 | 67 | -65 | -19 | -187 | -57 | -102 | -13 | -63 | -14 | -31 | -60 | -78 | -141 | -124 | -104 | -226
ΣΔH(M) - MEASURED | -160 | 0 | -160 | -260 | -530 | -430 | -510 | -370 | -190 | 60 | 80 | -40 | 70 | 120 | -200 | -140 | -310 | -610 | -420 | 120 | -120 | -120 | -140 | -170 | 30 | -190 | -410 | -150 | 10 | -20 | -30 | -240 | -180 | -220 | -470 | -660 | -850
ΣΔH(C) - CALCULATED | -292 | -202 | -331 | -479 | -839 | -814 | -939 | -921 | -668 | -523 | -568 | -681 | -641 | -636 | -884 | -890 | -1175 | -1568 | -1535 | -1150 | -1476 | -1409 | -1494 | -1543 | -1530 | -1807 | -2129 | -1882 | -1786 | -1830 | -1871 | -2141 | -2159 | -2340 | -2714 | -3008 | -3424

## Slide 6: What is wrong with the current calculation method?
dimensions.com/element/basketball-hoop
Chart: [mm]
| 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Z annual calculation error | -132 | -70 | 31 | -48 | -90 | -75 | -45 | -122 | 73 | -105 | -65 | 7 | -70 | -45 | 72 | -66 | -115 | -93 | -157 | -155 | -86 | 67 | -65 | -19 | -187 | -57 | -102 | -13 | -63 | -14 | -31 | -60 | -78 | -141 | -124 | -104 | -226
ΣΔH(M) - MEASURED | -160 | 0 | -160 | -260 | -530 | -430 | -510 | -370 | -190 | 60 | 80 | -40 | 70 | 120 | -200 | -140 | -310 | -610 | -420 | 120 | -120 | -120 | -140 | -170 | 30 | -190 | -410 | -150 | 10 | -20 | -30 | -240 | -180 | -220 | -470 | -660 | -850
ΣΔH(C) - CALCULATED | -292 | -202 | -331 | -479 | -839 | -814 | -939 | -921 | -668 | -523 | -568 | -681 | -641 | -636 | -884 | -890 | -1175 | -1568 | -1535 | -1150 | -1476 | -1409 | -1494 | -1543 | -1530 | -1807 | -2129 | -1882 | -1786 | -1830 | -1871 | -2141 | -2159 | -2340 | -2714 | -3008 | -3424

## Slide 7: Water Budget calculation method
G - groundwater
CALCULATION
ERROR:
Z = ΔH(C) - ΔH(M)
ΔH(M)
ΔH(C) = P + Qsurf + Qres + Qext – ET – Qout – Quse a
Lake Velence

## Slide 8: THANK YOU FOR YOUR ATTENTION!
The research presented in this PICO presentation was carried out within the framework of the Széchenyi Plan Plus program with the support of the RRF 2.3.1 21 2022 00008 project.

## Slide 9: Lake Velence, Hungary
Catchment information
Total area: 615 km2
Elevation: 100 – 325 m.a.s.l.
Precipitation average: 540 mm/yr
Water surf. Evap. ave.: 930 mm/yr
Reservoirs: 2 large, several smaller
Lake dimensions: L = 10 km
W = 2.5 km
H = 1.9 m !!!
KDTVÍZIG

## Slide 10: Lake Velence, Hungary
Chart: Average contribution of inflow elements (1986-2022)
| P | Qsurf | Qres | Qext
Percentage of inflows | 0.54679 | 0.29006 | 0.1491 | 0.014044
Chart: Average contribution of outflow elements (1986-2022)
| ET | Qout | Quse
 | 0.86402 | 0.10599 | 0.029988
Water budget contributions
(based on the current calculation method b )
KDTVÍZIG

## Slide 11: Calculation error – definition
Negative Z value means underestimating influxes and/or overestimating outfluxes
CALCULATION ERROR: Z
Z = ΔH(C) - ΔH(M)
ΔH(C) – calculated change in water level
ΔH(M) – measured change in water level

## Slide 12: Calculation error – annual values
Weak negative correlation (-0.33) between P and Z
Chart: Annual calculation errors (Z)
| 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
 | -132 | -70 | 31 | -48 | -90 | -75 | -45 | -122 | 73 | -105 | -65 | 7 | -70 | -45 | 72 | -66 | -115 | -93 | -157 | -155 | -86 | 67 | -65 | -19 | -187 | -57 | -102 | -13 | -63 | -14 | -31 | -60 | -78 | -141 | -124 | -104 | -226
 | -132 | -70 | 31 | -48 | -90 | -75 | -45 | -122 | 73 | -105 | -65 | 7 | -70 | -45 | 72 | -66 | -115 | -93 | -157 | -155 | -86 | 67 | -65 | -19 | -187 | -57 | -102 | -13 | -63 | -14 | -31 | -60 | -78 | -141 | -124 | -104 | -226
Chart: Z-P
| -132 | -70 | 31 | -48 | -90 | -75 | -45 | -122 | 73 | -105 | -65 | 7 | -70 | -45 | 72 | -66 | -115 | -93 | -157 | -155 | -86 | 67 | -65 | -19 | -187 | -57 | -102 | -13 | -63 | -14 | -31 | -60 | -78 | -141 | -124 | -104 | -226
 | 405 | 575 | 434 | 482 | 416 | 535 | 496 | 505 | 472 | 722 | 559 | 357 | 663 | 746 | 355 | 528 | 505 | 366 | 631 | 786 | 477 | 568 | 588 | 507 | 973 | 295 | 436 | 571 | 719 | 502 | 625 | 536 | 570 | 596 | 477 | 495 | 462

## Slide 13: Calculation errors – monthly values
Annual errors accumulate in Jan-May period!
Chart: Monthly errors (Jan-May)
| 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
Jan | -14 | -16 | 7 | 2 | -9 | -11 | 8 | -9 | 28 | -4 | -15 | 14 | -4 | -2 | -6 | -14 | -20 | -38 | -5 | 3 | -43 | -1 | -25 | -3 | 9 | -16 | -9 | -25 | -4 | -43 | -2 | 9 | -11 | -7 | -9 | -2
Febr | 31 | -41 | -16 | -11 | -7 | 10 | 3 | 0 | 4 | -8 | 6 | -15 | -22 | -14 | -22 | -19 | -11 | 3 | -5 | -19 | -21 | 8 | -8 | -17 | -18 | -10 | -12 | -27 | -19 | 1 | -26 | -5 | -10 | -24 | -18 | -11
March | -69 | 2 | -9 | -5 | -21 | -31 | 13 | 20 | 2 | -11 | -53 | -5 | -2 | -37 | -5 | -36 | -25 | -36 | -41 | -29 | -42 | -2 | 11 | 0 | -12 | -5 | -5 | -36 | -27 | 11 | -1 | -9 | -45 | -25 | -28 | -1
Apr | -13 | -52 | -22 | -11 | -15 | 0 | -15 | -2 | -2 | -26 | -38 | 12 | -29 | -3 | 8 | -21 | -28 | -26 | -54 | -39 | -14 | -2 | -27 | 0 | 8 | -22 | -17 | -30 | -11 | -22 | -22 | -21 | -46 | -22 | -27 | -17
May | -21 | -56 | -9 | -24 | -9 | -8 | -6 | -17 | -14 | -3 | -4 | -19 | -1 | 0 | 64 | 12 | -14 | -37 | -19 | -27 | 13 | 23 | -11 | -9 | -38 | -10 | -11 | -14 | -5 | 3 | -4 | -19 | 19 | -37 | -6 | -33
Chart: Average monthly calculation error (Z) against average monthly precipitation (P), surface inflow (Qsurf), and evapotranspiration (ET)
Z | -7.9722 | -10.2778 | -16.5 | -18.5556 | -9.75 | 0.11111 | 0.19444 | 3.5833 | -1.1389 | -1.3056 | -0.47222 | -3.1111
P | 33.8333 | 31.5556 | 31.0833 | 36.75 | 58.7222 | 61.3333 | 57.3889 | 55.0556 | 47.5278 | 42.8611 | 45 | 39.8056
Qsurf | 30.7778 | 28.1389 | 35.7778 | 32.2222 | 28.2778 | 26.6944 | 20.7222 | 15.5278 | 14.5556 | 14.8611 | 17.8333 | 25.6111
ET | -12.9722 | -19.8333 | -45.5 | -89.9444 | -126.0833 | -147.9167 | -165.6667 | -142.1667 | -90.4444 | -51.1944 | -22.8611 | -13.3889

## Slide 14: Evapotranspiration - current method
Main focus on the January - May period
Calculation method: c
Based on ground measurements of temperature, windspeed, vapour pressure, and pan evaporation at Agárd.
Winter:
XI. – III.: modified Meyer equation:
P=0.55 × [(E-e)/1,33]0,9 × (1+T/273)9 × (1+0,015 × u)2 × n [mm/month]
Summer:
IV. – X.: pan evaporation (A), with reed constants (K):
P=1,11 × (0,58+0,42×K) × A0,79 × (1+u)0,13 × n [mm/month]
Chart: Average monthly calculation error (Z) and average monthly ET (-)
Z | -7.9722 | -10.2778 | -16.5 | -18.5556 | -9.75 | 0.11111 | 0.19444 | 3.5833 | -1.1389 | -1.3056 | -0.47222 | -3.1111
ET (-) | -12.9722 | -19.8333 | -45.5 | -89.9444 | -126.0833 | -147.9167 | -165.6667 | -142.1667 | -90.4444 | -51.1944 | -22.8611 | -13.3889

## Slide 15: Evapotranspiration – satellite data
GEE products yield low ET, EEFLUX closest to current results
Chart: Different satelite image and calculation products for ET 2020-2022
EEFLUX | 0.36246 | 1.1152 | 1.8591 | 2.9328 | 3.3116 | 4.3555 | 4.7558 | 4.9756 | 3.7181 | 1.86 | 0.66137 | 0.27343 | 0.35947 | 0.51346 | 2.0465 | 2.6694 | 4.5001 | 4.5521 | 7.4906 | 6.356 | 2.5787 | 1.4687 | 0.75945 | 0.41071 | 0.88286 | 0.8659 | 2.1412 | 2.3742 | 4.0864 | 8.2699 | 7.5788 | 7.0725 | 5.1738 | 2.6776 | 1.4233 | 0.16895
Google Earth Engine ET products d:
GLDAS: Nasa GLDAS V2.1
M-500: Modis 500 m, 8 day
ePML-V2: Penman Monteith- Leuning (Modis500, 8day, GLDAS forcing data) Zhang et al., 2019
dGEE code: https://github.com/ mikhailsmilovic/Earth-Engine/blob/main/ET
f EEFLUX: LANDSAT 30×30 m – METRIC method (Allen et. al 2007)

## Slide 16: Evapotranspiration – EEFLUX-METRIC
Clouds and other anomalies can cause large time-gaps!
Satellite data:
Landsat images – high resolution (30×30 meter) imagery of atmospheric variables
METRIC method:
Automatic calibration of Energy Balance equations with Penman-Monteith method
Image frequency:
~ 1-2 weeks, but clouds and other anomalies occur

## Slide 17: Evapotranspiration – EEFLUX-METRIC
With EEFLUX slightly smaller ET values for Jan-May period!
Chart: EEFLUX vs Current method january-may period (2020-2022)
| 11.236247812390696 | 32.341507923620497 | 57.6322378113017 | 87.982526070552041 | 102.66076068743432 | 11.143638792282964 | 14.377008685099362 | 63.440083358921086 | 80.081952171816795 | 139.50352714715473 | 27.368784674713215 | 24.245292748112838 | 66.37791634580887 | 71.226899276180987 | 126.67826723507639
 | 10 | 45 | 57 | 117.7 | 125.9 | 19 | 20 | 54 | 81 | 109 | 26 | 40 | 61 | 82 | 132
 | 0 | 250

## Slide 18: Groundwater flow mappingg
GW modelling of Lake Velence: EGU-HS8.2.3 - Friday
Calculation method:
Currently, the groundwater component is not included in the Lake Velence water budget calculation!
However evidence shows, that it should be included.
Modelling the groundwater flow system is in progress.
g Research paper:
P. Baják et. al, "Integration of a Shallow Soda Lake into the Groundwater Flow System by Using Hydraulic Evaluation and Environmental Tracers," Water 14, 2022, 951 doi:10.3390/w14060951
P. Baják et. al, 2022

## Slide 19: Surface inflow - current method
Need to revisit calculation method, include gauge (c.)
Calculation method: c
based on hydrological analogy
constants calculated in 1970-s
I. Császár-víz:
QCSV = [Gauge (a.) – Gauge (b.)] × 2.63
II. Vereb-P. vízf.:
QVPV = Gauge (d.)
III. Lake direct catchment:
QLDC = Gauge (d.) × 0.84

## Slide 20: Precipitation – current method
Calculation method:
Based on ground measurements, averaging data from 4 stations
No stations on the north shore of the lake.
Slight increasing trend in annual precipitation.
rain gauge
Chart: Precipitation and surface inflow trends
| 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
P (+) | 405 | 575 | 434 | 482 | 416 | 535 | 496 | 505 | 472 | 722 | 559 | 357 | 663 | 746 | 355 | 528 | 505 | 366 | 631 | 786 | 477 | 568 | 588 | 507 | 973 | 295 | 436 | 571 | 719 | 502 | 625 | 536 | 570 | 596 | 477 | 495 | 462
Qsurf (+) | 406 | 437 | 342 | 259 | 135 | 239 | 375 | 290 | 396 | 238 | 464 | 327 | 292 | 670 | 497 | 203 | 160 | 137 | 155 | 234 | 341 | 312 | 200 | 223 | 650 | 339 | 145 | 446 | 245 | 300 | 285 | 193 | 189 | 116 | 131 | 105 | 99
KDTVÍZIG

## Slide 21: Water replenishment from reservoirs (Qres)
Reservoirs:
Reservoir 1 (Zámolyi): max: 4 Mm3
Reservoir 2 (Pátkai): max: 7 Mm3
Lake Velence at stage 140 cm: 41 Mm3
Operation:
Filling up from floods, replenishment if lake level goes below 140 cm.
Calculation method:
Based on discharge curves of gates.
Aquamagazin.hu
KDTVÍZIG
Aquamagazin.hu

## Slide 22: External water replenishment (Qext)
External water replenishment in 1993-1994:
why?  water level under min. operational level for 3 consecutive years
how?  building a pipe system to divert karst water from an existing mine dewatering well
how much?  ~ 11 Mm3
External water replenishment 2023 ?
Not yet!
But ongoing negotiations on possibilities.
Chart: Lake Velence water levels (1986 – 2022)
External water replenishment '93-'94
??

## Slide 23: Water discharges (Qout ; Quse)
Lowering water levels (Qout):
When water levels in the lake exceed max operational level. Last time the water level was lowered: 2016.
Water use (Quse):
Water from the main tributary of the lake can be diverted towards the Dinnyés Fish Farm.
Calculation method:
Based on discharge curves of gates and weirs, with high uncertainty. b
Chart: Water discharges compared to Evapotranspiration (1986 - 2022)
| 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
ET | 1050 | 834 | 899 | 843 | 941 | 855 | 991 | 940 | 913 | 838 | 806 | 922 | 888 | 861 | 995 | 928 | 965 | 963 | 841 | 791 | 862 | 1040 | 968 | 971 | 855 | 994 | 1086 | 956 | 874 | 917 | 899 | 1033 | 971 | 991 | 976 | 950 | 1052
Qout | 203 | 237 | 49 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 254 | 34 | 0 | 894 | 564 | 0 | 0 | 0 | 0 | 0 | 248 | 0 | 0 | 0 | 1336 | 110 | 0 | 0 | 71 | 58 | 169 | 0 | 0 | 0 | 0 | 0 | 0
Quse | 132 | 108 | 96 | 87 | 53 | 45 | 39 | 0 | 3 | 7 | 20 | 31 | 29 | 27 | 46 | 34 | 23 | 22 | 22 | 27 | 34 | 30 | 17 | 16 | 21 | 17 | 13 | 24 | 11 | 13 | 86 | 25 | 19 | 9 | 6 | 4 | 0

## Slide 24: References
The research presented in this PICO presentation was carried out within the framework of the Széchenyi Plan Plus program with the support of the RRF 2.3.1 21 2022 00008 project.
a) Water Resources Research Center Hungary (VITUKI), "Hydrological and water quality characteristics of Lake Velence and its reservoirs," Budapest 1985
b) Middle Transdanubian Water Directorate (KDTVÍZIG), "Water budget of Lake Velence: 1986 - 2021," Available at: http://www.kdtvizig.hu/hu/velencei-to-vizmerleg (Accessed: 21st April 2023.)
c) Water Resources Research Center Hungary (VITUKI), "Monthly water budget calculation for Lake Velence and its catchment," Budapest, 1976
d) Google Earth Engine evapotranspiration products - EE code: https://github.com/mikhailsmilovic/Earth-Engine/blob/main/ET
e) Zhang, Y., Kong, D., Gan, R., et al., 2019. Coupled estimation of 500 m and 8-day resolution global evapotranspiration and gross primary production in 2002–2017. Rem. Sens. Environ. 222, 165–182.
f) Allen, R.G., Tasumi, M., Trezza, R., 2007a. Satellite-based energy balance for mapping evapotranspiration with internalized calibration (METRIC) Model. J. Irrig. Drain. Eng. 133 (4), 380–394. https://doi.org/10.1061/(ASCE)0733-9437(2007)133:4 (380). https://eeflux-level1.appspot.com/
g) Baják, P.; Hegedűs-Csondor, K.; Tiljander, M.; Korkka-Niemi, K.; Surbeck, H.; Izsák, B.; Vargha, M.; Horváth, Á.; Pándics, T.; Erőss, A. Integration of a Shallow Soda Lake into the Groundwater Flow System by Using Hydraulic Evaluation and Environmental Tracers. Water 2022, 14, 951. https://doi.org/10.3390/w14060951