## Slide 1
Take home
Study site
Scientific question
Motivation
Next
Results
Radar setup
LoSAR processing
Falk Oraschewski, Inka Koch, Reza Ershadi, Jonathan Hawkins, Olaf Eisen and Reinhard Drews
Layer-optimized SAR processing with a mobile pRES to illuminate the internal layering of an alpine glacier
Can we observe deep internal layers of cold alpine glaciers?
Data: Konrad et al., 2013
Normal GPR: No deep reflections
Discussion

## Slide 2
Study site
Colle Gnifetti, Monte Rosa, Switzerland/Italy
Elevation: 4.500 m
Cold glacier and climate archive
→ Need Geophysics to intercalibrate ice cores
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 3
Motivation
  Take coherent radars from the poles to the Alps
Radargram collected at Peterman Ice Stream, Greendland (Bell et al., 2014)
Coherent radars & SAR processing allow the detection of basal features in the polar ice sheets.
But the use of these radar systems in alpine terrain is limited (e.g,. airborne radar, snow cat pulled systems).
Devevlop SAR processing techniques for the cheap and lightweight phase sensitive Radio Echo Sounder (pRES).
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 4
Conventional SAR processing techniques are based on the idea of increasing signal strength of point reflectors by summing up the power along their reflection hyperbola recorded over consecutive traces.
For closely-spaced, specular reflectors this approach entails several problems:
Reflection hyperbolas may reach across several layers
Sloping layers cause destructive interference
Resulting radargrams are patchy and can be misinterpreted
→ Need a different approach for SAR processing of internal layers: Summation along the layer
A reflection hyperbola
Radargram after back projection processing
Motivation
  Why do we need layer-optimized SAR processing?
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 5
Radar setup
Tx/Rx antennae:
  Mounted in tractor inner tubes and fixed with wood/bamboos.
GNSS system:
  Used in real time kinematic (RTK) mode to correct the signal of the sled antenna and achieve ~5 cm positioning accuracy.
Computer & pRES:
  Receive GPS coordinates, trigger shots and tell user when to move/stop.
  Because of the 1 s chirp time of the pRES, the data needs to be recorded in Start-Stop mode, making data acquisition slow.
What is the pRES?
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 6
The pRES is a frequency modulated continuous wave (FMCW) radar with:
Bandwidth :
Center frequency :
Chirp time : s
The signal is deramped by subtracting the recorded from the transmitted signal.
After Fourier transforming the deramped signal a frequency spectrum is obtained that translates into an amplitude-depth relation.
A chirp
Recorded signal After Fourier transform
Motivation
  What is the pRES?
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 7
Layer optimized Synthentic Aperture (LoSAR) processing
Idea
  Sum along internal layers to improve their signal strength
Workflow
Find layer slopes
in phase signal
Filter slopes
Coherent
summation along slope line
Shape matching
Phase correction
LoSAR processed radargram
pRES data
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 8
Phase correction
Compared to the power signal, the phase is very coherent
But the raw phase is difficult to interpret. Only after performing a phase correction, as explained by Brennan et al. (2013), the phase response aligns with the layer slopes.
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 9
Shape matching
Before: Raw radar data
After: Shape matched radar data
Convolute input data with a reference reflector to
  Increase strength of good reflections
  Suppress non-reflector type signals/noise
  Relatively increase the strength of weak reflectors
Method following Rahman et al. (2014)
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 10
Find layer slopes in phase signal
Power of raw radar data
Derived layers slopes
The phase is coherent along the layer slope. At every grid point we can find the slope as follows:
Normalize the radargram
Iteratively sum coherently over all possible slope lines (Positive interference when in-phase, otherwise destructive interference)
Take the slope with the maximal return
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 11
Filter layer slopes
In areas with a weak power return the phase is still more noisy and we observe extrema in the slope.
Assuming that internal slopes cannot vary strongly in space , we filter these extrema using a 2D-moving mean filter to
reduce the coherence in the following along slope summation
to avoid an overestimation of the signal power
and let true reflectors become more clear
Before: Layer slopes with maximal phase coherence
After: Filtered layer slopes
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 12
Coherent summation along layer
Before: Power of raw mobile pRES radar data
After: LoSAR processed radargram
By coherently summing up the power along the layer slope lines
the power of true reflectors will add up coherently, become stronger and more uniform
the power signal of noise in reflector free areas will blur out and become indistinct
→ Deep reflectors become clear
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 13
Results: LoSAR processed radargram
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 14
Results: LoSAR processed and shape matched radargram
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 15
Discussion: Spacing requirements
The along track summation of LoSAR processing does not set a general limit on the trace spacing during data acquisition.
But the trace spacing sets a limit on the slope of reflectors that can be traced:
For example, for the pRES with a center frequency of the detection of layers with slopes requires a trace spacing of .
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 16
Discussion: Multi antenna configurations
Multi antenna configurations are needed to:
Solve the left-right ambiguity
Reduce the measurement time by moving in bigger steps
Cover larger profile distances
Difficulties:
Differing phase responses from different antennae and cable
Cable noise from long cable
Using an autonomous Rover, we recorded a profile on Ekström ice shelf to study the feasibility.
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 17
Discussion: Signal stability
Uphill profile after LoSAR processing
In an additional uphill section of the profile, the phase coherence is significantly reduced, decrease the power gain by LoSAR processing
Potentially the signal are noisier as it was more difficult to keep the antenna stable during the chirp times.
Stabilizing the antennae and cable during data acquisition is critical and need to be improved in future deployments.
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 18
Take home messages
There are deep layers at Colle Gnifetti that can continuously be traced and used to intercalibrate ice core records
The pRES can also be used for radar profiling.
LoSAR processing and shape matching can improve the visibility of internal reflection horizons in the ice.
The spacing requirements for LoSAR processing are less strict than for conventional SAR processing. But the spacing sets a limit on the slope of reflectors to be traceable.
LoSAR processed mobile pRES radargram
Take home
Study site
Scientific question
Motivation
Back
Next
Results
Radar setup
LoSAR processing
Discussion

## Slide 19
References
Bell, R.E., K. Tinto, I. Das, M. Wolovick, W. Chu, T.T. Creyts, N. Frearson, A. Abdi, and J. D. Paden. “Deformation, Warming and Softening of Greenland’s Ice by Refreezing Meltwater.” Nature Geoscience 7, no. 7 (2014): 497–502. https://doi.org/10.1038/ngeo2179.
Brennan, P.V., L.B. Lok, K. Nicholls, and H. Corr. “Phase‐sensitive FMCW Radar System for High‐precision Antarctic Ice Shelf Profile Monitoring.” IET Radar, Sonar & Navigation 8, no. 7 (2014): 776–86. https://doi.org/10.1049/iet-rsn.2013.0053.
Konrad, H., P. Bohleber, D. Wagenbach, C. Vincent, and O. Eisen. “Determining the Age Distribution of Colle Gnifetti, Monte Rosa, Swiss Alps, by Combining Ice Cores, Ground-Penetrating Radar and a Simple Flow Model.” Journal of Glaciology 59, no. 213 (2013): 179–89. https://doi.org/10.3189/2013JoG12J072.
Rahman, S., and P.V. Brennan. “Shape Matching Algorithm for Detecting Radar Hidden Targets to Determine Internal Layers in Antarctic Ice Shelves.” In 2014 IEEE Radar Conference, 1430–33. Cincinnati, OH: IEEE, 2014. https://doi.org/10.1109/RADAR.2014.6875824.
Take home
Study site
Scientific question
Motivation
Back
Results
Radar setup
LoSAR processing
Discussion