## Slide 1: Exploring controls on the spatial distribution of bedrock exposure in mixed bedrock and alluvial river systems
Mel Oliveira Guirro, Rebecca Hodge, Fiona Clubb and Laura Turnbull
Durham University
Contact: mel.oliveira-guirro@durham.ac.uk
April 2023

## Slide 2: Rivers and sediment transport: A complex dynamic system
Interaction between sediment, channel morphology and water flow
Alluvial cover is constantly changing
It is not understood well how and when alluvial cover changes
Relevant for :
  Stability of the riverbed, aquatic habitats and water quality
  River management decisions
Introduction
Field analysis
Simulation analysis
Next steps
Summary
Notes: Rivers are dynamic systems that are constantly changing.
Understanding the spatial distribution of sediment cover is crucial in predicting their response to future disturbances.

## Slide 3
Bedrock reach
Mixed reach
Alluvial reach
Introduction
Field analysis
Simulation analysis
Next steps
Summary

## Slide 4
Flow
Bedrock
Alluvial
Introduction
Field analysis
Simulation analysis
Next steps
Summary
River network
Sediment deposition
Spatial distribution of alluvial cover

## Slide 5: Research Aim
To understand how channel and sediment properties affect the spatial distribution of riverbed cover in mixed bedrock and alluvial systems using field data analysis and numerical modelling.
This study is part of a PhD project that aims to understand how sediment connectivity drives the spatial distribution and temporal changes of bedrock and alluvial reaches.
Research questions of PhD project:
How do channel and sediment properties interact with alluvial cover?
How do channel and sediment properties affect the spatial distribution of alluvial cover in equilibrium?
How do temporal variations in sediment supply and flow affect the pattern of alluvial cover?
 Empirical analysis of field data
 Steady state (numerical modelling)
 Perturbations (numerical modelling)
Introduction
Field analysis
Simulation analysis
Next steps
Summary
Notes: Link research questions with sediment connectivity

## Slide 6: Study Area
Carron River network, Scottish Highlands
System with mixed bedrock and alluvial reaches
Datasets:
  Whitbread (2015) – main channel:
    Sediment cover fraction
    Width
    Depth
    Slope
  Field work (2022):
    Sediment cover fraction
    Grain size
Carron Catchment and river network
Introduction
Field analysis
Simulation analysis
Next steps
Summary

## Slide 7: Field work (Sept 2022)
Collected data on:
  Sediment cover
  Grain size
Introduction
Q1 – Empirical
Q2 – Steady state
Q3 - Perturbations
Summary
Data collection sites:

## Slide 8: Field data analysis: sediment cover
Alluvial cover (2022)
PCA for Scottish Highlands
Alluvial
Bedrock
Bedrock-alluvial
Clusters indicates geometric distinction between bedrock and alluvial reaches
Drainage area is the main parameter for PC1 and channel depth is the main for PC2
PC2 – 20%
PC1 – 72%
Results: Spatial distribution
PCA:
Introduction
Field analysis
Simulation analysis
Next steps
Summary

## Slide 9: Field data analysis: grain size data
Grain size distribution:
  Median grain size: D50 = 10 cm
Multiple regression analysis:
  Dependent variable: D50 of each gravel bar
  Drainage area, channel slope, width and riverbed cover have a significant correlation with D50
Field data is noisy. Numerical modelling can isolate parameters.
Independent variable | Coef | Std err | p-value
Drainage area | -0.0005 | < 0.001 | < 0.001
Channel slope | 0.5223 | 0.196 | 0.012
Channel width | 0.0047 | 0.001 | < 0.001
Riverbed cover | 0.0006 | < 0.001 | 0.031
% coarse superficial deposits | 0.0369 | 0.025 | 0.148
Introduction
Field analysis
Simulation analysis
Next steps
Summary
This study site had geological glacial processes that transported sediments and might be affecting the results

## Slide 10: Modelling: Network Sediment Transporter (Pfeiffer et al, 2020)
Tracks sediment parcels on a river network
  River segments are represented by links
Introduction
Field analysis
Simulation analysis
Next steps
Summary
Notes: Based on physical equations of bedload sediment transportation

## Slide 11: Modelling: Network Sediment Transporter
Modifications on the source code:
  Implemented sediment input at every time step
  Modified how sediment parcel moves downstream
  Set up minimum transport capacity to solve bottleneck issue
  Output: sediment cover fraction
Cover fraction | Definition | Type | Diagram
0.0 | 0% cover | Bedrock | 
0.5 | 50% cover | Mixed | 
1.0 | 100% cover | Alluvial | 
2.0 | 200% cover | Alluvial | 
3.0 | 300% cover | Alluvial | 
11/20
Sediment depth relative to grain size
0
1
2
3
4
5
6
0
50
100
150
Days
200
250
Introduction
Field analysis
Simulation analysis
Next steps
Summary
Notes: Based on physical equations of bedload sediment transportation

## Slide 12: Sensitivity Analysis of Network Sediment Transporter
Find the best set of parameters to run scenarios
Modify:
  Initial sediment cover
  Grain size
  Flow depth
  Sediment input
Analyse results when system is in steady state
Latitude
Longitude
Alluvial
Bedrock
Introduction
Field analysis
Simulation analysis
Next steps
Summary
Notes:   Link length
  Flow depth
  Initial sediment over
  Sediment input
  Grain size
  Timestep length

## Slide 13: Sensitivity Analysis of Network Sediment Transporter - Results
  Initial sediment cover
    Increasing initial sediment cover increases final alluvial cover when the simulation finds steady state.
    When alluvial cover increases, it tends to lengthen a continuous alluvial patch.
Fraction of alluvial cover
Introduction
Field analysis
Simulation analysis
Next steps
Summary

## Slide 14: Sensitivity Analysis of Network Sediment Transporter - Results
Results:
  Alluvial cover decreases when flow depth increases.
  Alluvial cover increases com grain size increases.
  The spatial pattern of alluvial cover is similar when changing flow depth and grain variables because channel structure, such as slope, was the main control in alluvial cover.
Fraction of alluvial cover
Introduction
Field analysis
Simulation analysis
Next steps
Summary
Scenario map: Flow depth = 0.5 bankfull depth
Scenario map: Grain size = 3 cm
Flow depth:
Grain size:

## Slide 15: Next steps of bedload sediment transport simulations:
  Create more scenarios by modifying:
    Sediment input
    Flow depth
    Grain size
  Compare model results with field data:
    In a preliminary analysis, they have a Pearson correlation around 0.50, showing a moderate correlation
  Connectivity analysis of results sediment cover at steady state
Introduction
Field analysis
Simulation analysis
Next steps
Summary

## Slide 16: Next step: Perturb the system by adding sediment pulses
Sediment input from hillslope:
  How to choose locations:
    Index of Connectivity (Cavalli et al, 2013)
Introduction
Field analysis
Simulation analysis
Next steps
Summary

## Slide 17: Spatial analysis by clustering river segments with similar time-courses: structural connectivity
Spectral clustering (11 clusters)
Cluster example (red): 72 nodes
Introduction
Field analysis
Simulation analysis
Next steps
Summary
Reach 151
Reach 164
For example, the cluster in red is represented by river segments that loose sediments quickly. They are mainly bedrock reaches. In this case, they have a higher slope than other clusters.

## Slide 18: Temporal analysis and functional connectivity
Time Delayed and Mutual Information (TDMI):
  Example: TDMI identifies similar behaviour between two river segments (nodes) around day 26 with a 5-day time-delay and on day 84 simultaneously.
Introduction
Field analysis
Simulation analysis
Next steps
Summary
Mutual Information (bits)

## Slide 19: Summary
Several parameters affect sediment cover: water flow, sediment and channel characteristics.
From field data analysis:
  Drainage area and depth are the main parameters that make alluvial and bedrock reaches distinct
  Each study site can have specifications: Carron has coarser sediments from glacial source.
From modelling results analysis:
  Channel slope is one of the most important parameters.
Connectivity analysis can further understand controls on alluvial cover
Questions? Contact me: mel.oliveira-guirro@durham.ac.uk
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under the Marie Skłodowska-Curie grant agreement No 859937.
Introduction
Field analysis
Simulation analysis
Next steps
Summary

## Slide 20: References
Pfeiffer, A., Barnhart, K., Czuba, J., & Hutton, E. (2020). NetworkSedimentTransporter: A Landlab component for bed material transport through river networks. Journal of Open Source Software, 5(53).
Wilcock, P. R., & Crowe, J. C. (2003). Surface-based transport model for mixed-size sediment. Journal of Hydraulic Engineering, 129(2), 120-128.
Whitbread, K. 2015. Channel geometry data set for the northwest Scottish Highlands. British Geological Survey Open Report, OR/15/040. 12pp.
Introduction
Field analysis
Simulation analysis
Next steps
Summary
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under the Marie Skłodowska-Curie grant agreement No 859937.
Questions? Contact me: mel.oliveira-guirro@durham.ac.uk