## Slide 1
April 26, 2023
Tengfei Feng1, Yunzhong Shen1*, Qiujie Chen1, Fengwei Wang1, Xingfu Zhang2
1. College of Surveying and Geo-Informatics, Tongji University (https://gteam.tongji.edu.cn/)
2. Department of Surveying and Mapping, Guangdong University of Technology
Spatiotemporal Characteristics and Drivers of Groundwater Change in North China Revealed by GRACE
Time-Variable Gravity
Session HS8.2.9

## Slide 2
GWSA Change and Decomposition
Driving Factors
Introduction
Data and Methodology
Outline
Ⅰ
Ⅱ
Ⅲ
Ⅳ
Summary
Ⅲ

## Slide 3: Introduction: Background
Focus on Groundwater change Based on GRACE + Hydrological models
India
Central Valley
Great Plains
North China
salinization
subsidence
GRACE/GRACE-FO

## Slide 4: Introduction: Motivation
Current
GRACE models with higher spatial resolution.
Hidden spatiotemporal features.
Quantitative identification of drivers.
Further
Tang et al., 2013, GRL
Feng et al., 2013, WRR
water footprint (Su et al., 2020, JOH)

## Slide 5: Introduction: Research object
Estimate terrestrial water storage anomaly (TWSA) and groundwater storage anomaly (GWSA) with high resolution model Tongji-RegGRACE2019.
Implement spatiotemporal decomposition for GWSA with ICA, explore the periodic characteristics of source signals.
Identify the driving factor and driving mechanism for GWSA source signals.

## Slide 6
Data sets (2004-2015)
Variable | Source | Temporal resolution | Spatial resolution | Annotation
Terrestrial water storage (TWS) | GRACE (Tongji-RegGrace2019) | monthly | 0.5º×0.5º | Chen et al., 2021, JGR
Soil moisture (SM), snow water equivalent (SWE) | GLDAS | monthly | 0.25º×0.25º | Rodell, 2004, AMS
Surface water (SW), groundwater storage (GWS) | WGHM | monthly | 0.5º×0.5º | Döll et al., 2003, JOH
Evaporation | GLEAM | daily | 0.25º×0.25º | Martens et al., 2017, GMD
Precipitation | TCH Weighted product | monthly | 0.5º×0.5º | Xu et al., 2020, WRR
Groundwater level | Observation wells (2005-2014) | monthly | / | 
Water consumption of agricultural irrigation, industrial development | Yearbooks, bulletins | yearly | / | /
Coal mining | Yearbooks, bulletins | monthly and yearly | / | 
Normalized difference vegetation index (NDVI) | SPOT satellite | monthly | 1 km | 

## Slide 7
Decomposition-ICA
Correlation-GACD
Normalized GWS matrix (m : epoch, n : gridpoint number):
P, principal component (PC) matrix; E, eigenvector matrix
S, temporal component; A, spatial pattern
W, rotation matrix, estimated with Joint approximate diagonalization of eigenmatrices (JADE) algorithm (Cardoso 1993; Forootan and Kusche 2012; 2014)
Factor time series y and GWS time series u:
S, A
Initialization and first-order differential
Correlation
Absolute correlation degree
PCA
ICA
Decomposing GWS with independent component analysis (ICA) to derive the spatial pattern (SP) and temporal component (TC)
Calculating grey absolute correlation degree (GACD) for each GWS component and drivers
GACD can analyze multiple factors simultaneously and rank the importance.
Method: Drivers identification

## Slide 8: Results: TWSA and GWSA estimates
Trend (cm/yr) | 2004.01-2009.12 | 2010.01-2013.12 | 2014.01-2015.12 | 2004.01-2015.12 | 2005.01-2013.12
TWSA-GRACE | -1.96±0.12 | 0.72±0.27 | -4.64±0.54 | -1.00 ± 0.06 | 
GWSA-GRACE |  |  | -3.71±0.49 | -0.87±0.04 | -0.85±0.06
GWSA-WGHM |  |  | -2.11±0.07 | -1.51±0.01 | -1.43±0.01
GWSA-Well |  |  |  |  | -0.80±0.03
GWSA from GRACE and hydrologic model: GWSA=TWSA-SMA-SWEA-SWA

## Slide 9: Results: Spatiotemporal decomposition for GWSA
Cumulative variance：89%
Contribution ratios：36，32，18，14%
TC is generally less clustered by different time cycles
SP shows distinct localized characterstics
Arctic Oscillation
and La Niña
Slepian localization analysis method (Han et al., 2021, CJG)

## Slide 10: Results: Spatiotemporal decomposition for P and Et
Precipitation
Evaporation

## Slide 11: Results: Driving factors identification
Potential factors: irrigation, coal mining, industry, precipitation, evaporation

## Slide 12: Results: Driving factors identification
Natural factors: precipitation, evaporation
Anthropogenic factors: agricultural irrigation, coal mining

## Slide 13: Results: Intra-annual distributions
GWS declines throughout the first half of the year and reaches the annual low in July (-4.07 cm) before increasing rapidly during July to August, following by a gradual reduction again.
NDVI highlights a bimodal distribution, which matches with the growing season (annual double-cropping system) of crops.

## Slide 14: Summary
GWS derived from Tongji-RegGRACE2019 in North China is depleted with a rate of -0.87±0.04 cm/yr from Jan. 2004 to Dec. 2015, which is basically consistent with that from monitoring well.
By ICA decomposition, the temporal components of GWSA present significant annual or intra-annual cycles, and the spatial pattern has distinct localized characteristics, which is helpful for identificating source signal.
The driving factors, including uneven spatiotemporal distribution of precipitation, intense seasonal evaporation, severe loss by coal mining, coupled with exhaustive exploitation for irrigation, jointly restrict the GWS rise and fall at different time nodes.
Feng, T., Shen, Y., Chen, Q., Wang, F., Zhang, X. (2022). Groundwater storage change and driving factor analysis in North China using independent component decomposition. J. Hydrol., 609, 127708, doi: 10.1016/j.jhydrol.2022.127708.

## Slide 15: Major references
Feng, W., Zhong, M., Lemoine, J. M., Biancale, R., Hsu, H. T., Xia, J., 2013. Evaluation of groundwater depletion in North China using the gravity recovery and climate experiment (GRACE) data and ground-based measurements. Water Resour. Res. 49(4), 2110-2118.
Forootan, E., Kusche, J., 2012. Separation of global time-variable gravity signals into maximally independent components. J. Geod. 86(7), 477-497.
Forootan, E., Kusche, J., Loth, I., Schuh, W. D., 2014. Multivariate prediction of total water storage changes over west Africa from multi-satellite data. Surv. Geophys. 35(4), 913-940.
Han, J., Chen, S., Lu, H., Xu, W., 2021. Time-variable gravity field determination using Slepian functions and terrestrial measurements: A case study in North China with data from 2011 to 2013. Chin. J. Geophys. (in Chinese) 64(5), 1542-1557.
Liu, B., Dai, W., Liu, N., 2017. Extracting seasonal deformations of the Nepal Himalaya region from vertical GPS position time series using independent component analysis. Adv. Space Res., 60, 2910-2917.
Mei, Z. G., 1992. The concept and computation method of grey absolute correlation degree. Systems Engineering (in Chinese) 10, 43-44.
Tang, Q., Zhang, X., Yin, T., 2013. Anthropogenic impacts on mass change in North China. Geophs. Res. Lett. 40, 3924-3928.

## Slide 16
April 26, 2023
https://gteam.tongji.edu.cn/
Tengfei Feng1, Yunzhong Shen1, Qiujie Chen1, Fengwei Wang1, Xingfu Zhang2
1. College of Surveying and Geo-Informatics, Tongji University
2. Department of Surveying and Mapping, Guangdong University of Technology
Thank you for your attention !
Spatiotemporal Characteristics and Drivers of Groundwater Change in North China Revealed by GRACE Time-Variable Gravity Field