## Slide 1
Christian Marx | Dörthe Tetzlaff | Reinhard Hinkelmann | Chris Soulsby
c.marx@tu-berllin.de
Photo: Marx, privat
Effects of 66 years of water management and hydroclimatic change on the urban hydrology and water quality of the Panke catchment, Berlin, Germany, Science of The Total Environment, 900, 165764.
Water management is a success story:
How water quality changed based on historical development and mid-term hydroclimate

## Slide 2
Marx, C., 2023. Insights from stable water isotopes and long-term water quality data on urban hydrology. TU Berlin PhD Thesis. https://doi.org/10.14279/depositonce-18518
Motivation
Motivation | Study site & development | Methods | Results | Discussion
Understanding the urban hydrological cycle, pathways and their consequences
Influence of hydroclimate on urban water quality

## Slide 3
Study site: Berlin & the Panke catchment
Motivation | Study site & development | Methods | Results | Discussion
Upstream
Sewage Irrigation farm
until 1985
Site | Urban + Streets [%] | Forest[%] | Agriculture [%]
UP1 | 30.3 | 9.0 | 55.9
UP2 | 41.5 | 7.5 | 47.1
Buch | 42.4 | 7.7 | 45.7
OL | 34.1 | 22.8 | 34.6
Upstream
Those values are cumulative based on the nested catchment
Waste water treatment plant (WWTP, 1985+)
Area: ~220 km²
Upstream:
Groundwater dominated
Downstream :
Waste water dominated
Marx C., Tetzlaff D., Hinkelmann R., Soulsby C. (2021). Isotope hydrology and water sources in a heavily urbanized stream. Hydrological Processes, 35(10). https://doi.org/10.1002/hyp.14377

## Slide 4
Methods & Data
Motivation | Study site & development | Methods | Results | Discussion
>+2
SPI
(Standard Precipitation Index)
<-2
0
-1
1
Long term
trend
Saisonal and
random effects
Hydroclimate:
Standard Precipitation Index (SPI):
  < -2 extreme drought, +1 - -1 „average years“,
  >+2 extreme wet years
Stream Quality: NH4-N, NO3-N, oPO4-P, Cl
Multiplicative trend decomposition
Multiple breakpoint analysis (trend stability)
Classification after German standards (LAWA)
Longterm data: Water quality 66 years; fertilizer 70 years, 66 years of hydroclimate,
30 years water quantity and 20 years of groundwater quality, changes in water management
Ø
Extr. drought
Extr. wet
Time Series
Marx et al, 2023, STOTEN

## Slide 5
Wasserwirtschaftliche Entwicklung
Rieselfelder (bis 1985)
Rieselanlagen bis 10,000 mm/a (Ende 1960er -1985)
Kläranlage
(1985 - Mitte 90er)
Kläranlage
(2015 - heute)
Gewässer-renaturierung
(2015 - heute)
Mech. Reinigung (1985)
Chem. P Eliminierung (1986)
BioP (1993)
Komb. Nitri + Denitri (1999-2000)
Motivation | Methods | Study site & hydroclimate | Results | Discussion
13 Jahre: übergreifende Dürren
Feuchte- periode
1964-1967
Trocken-periode
1970-1976
Trocken-periode
1996-2001
Feuchte- periode
2007-2013
Trocken-periode
2018-2021
8 Jahre: übergreifende Feuchte-perioden

## Slide 6
Düngemittelausbringung (Ost- und wiedervereinigtes Deutschland)
(Datensatz als Supplementary tables): https://doi.org/10.1016/j.scitotenv.2023.165764
Statistics could be created differently
Only mineral fertilizer
Statistic after 1990 is biased towards West-Germanys fertilization practices (Areal normalisation)
P2O5 Plateau 1970-1980
Since 1990: P2O5 -33%/Decade reduction
Nitrogen: except after reunification no major decline (~6%/Decade)
Nitrogen only since 2015/17 reduced application
Strong increase N:P-ratio (from 2.5:1 to 15:1)
Data sources:
DDR: (1950–1989): Statistisches Amt der DDR, 1990; BRD: (1989–2021): BMEL, 2022; Statistisches Bundesamt (Destatis) 2022a; Ackerfläche: Statistisches Bundesamt (Destatis), 2022b
Motivation | Methods | Study site & hydroclimate | Results | Discussion
-6%/Decade
15:1
-33%/Decade
5:1
2.5:1

## Slide 7
Generally decreasing nutrient concentration
  particular after abandonment of the SIF (1985) at all sites
Similar dynamics between UP1,UP2, Buch and Outlet
Dynamics in upstream sites stabilized in late 1990ies/early 2000
Upstream sites reached “good” to “very good” water quality in the following decades
The urban UP2 has the best water quality
Motivation | Study site & development | Methods | Results | Discussion
Water quality & influence of water management
SIF
WWTP
SIF
WWTP
SIF
WWTP
SIF
WWTP
SIF
WWTP
Marx et al, 2023, STOTEN

## Slide 8
Motivation | Study site & development | Methods | Results | Discussion
Better hydrologic connectivity of the agricultural dominated areas during wet periods
Under circumstances: accumulation of fertilizer during droughts, because of less infiltration/bio-production?
Normalized concentration (0 = low, 4 = high)
Nitrogen as a function of hydroclimate (upstream sites)
Ø
Extr. drought
Extr.
wet
Normalized concentration (0 = low, 4 = high)
Marx et al, 2023, STOTEN

## Slide 9
WWTP concentration independent of hydroclimate (as it is threshold controlled)
Outlet concentration is statistically significant impacted by hydroclimate in terms of seasonal and random effects
Ammonium concentration is low.
Motivation | Study site & development | Methods | Results | Discussion
Normalized concentration (0 = low, 4 = high)
Nitrogen as a function of hydroclimate (downstream sites)
Ø
Extr. drought
Extr.
wet
Normalized concentration (0 = low, 4 = high)
Marx et al, 2023, STOTEN

## Slide 10
Only minimal hydroclimatic impact of oPO4-P & Cl in the upstream sites
Motivation | Study site & development | Methods | Results | Discussion
Normalized concentration (0 = low, 4 = high)
Ortho-phosphate & chloride as a function of hydroclima (upstream sites)
Ø
Extr. drought
Extr.
wet
Normalized concentration (0 = low, 4 = high)
Marx et al, 2023, STOTEN

## Slide 11
oPO4-P: increase during droughts, in particular with increasing urbanization
Chloride is usually independent of hydroclimate (“conservative tracer”); snow rich winter have an impact, due to de-icing of streets
Motivation | Study site & development | Methods | Results | Discussion
Normalized concentration (0 = low, 4 = high)
Ø
Extr. drought
Extr.
wet
Ortho-phosphate & chloride as a function of hydroclimate (downstream sites)
Normalized concentration (0 = low, 4 = high)
Marx et al, 2023, STOTEN

## Slide 12
Historically: Ammonium is “the greatest issue”, within the catchment
Indirect influence of the former sewage irrigation farm on upstream sites?
Since 2000: upstream sites between “good” and “very good”
The urban site UP2 has even the “best water quality
Only since the reintroduction of effluents to the Outlet (2015), deminshed water quality
  But: enough flows to avoid intermittency
Water quality classes
Motivation | Methods | Study site & hydroclimate | Results | Discussion

## Slide 13
NH4-N: Increase during drought conditions, lower during wet periods
NO3-N: Decrease during drought conditions, higher during wet periods
  Potential source limitation (wet)
oPO4-P: Increase for dry and wet periods in upstream sites, higher during droughts (Outlet)
Summary: Hydroclimate
Motivation | Study site & development | Methods | Results | Discussion
Chloride, no midterm influence
  Snow rich winter have a significant, short-term effect
Influence of hydroclimate on water quality is significantly increasing with urbanization, independently of WWTP
Hydrologic connectivity is probably causing relation between hydroclimate and water quality changes
Marx et al, 2023, STOTEN

## Slide 14
Take home messages:
Water quantity & -quality:
  Improving due to active water management
  Urban water quality is depending on hydroclimate
  Hydrologic connectivity as well as urban influence are relevant
  Ecology is returning (bird-, beaver- & otter habitat)
Resilience is increased
  No exceedance beyond good water quality classes in the upstream sites during hydroclimatic extremes
  Flow in downstream sites is maintained by WWTP effluents during droughts
Motivation | Study site & development | Methods | Results | Discussion
Beaver dam, former SIF
Beaver dam, former SIF
River restoration
Marx et al, 2023, STOTEN

## Slide 15
Thank you very much!
Marx C., Tetzlaff D., Hinkelmann R., Soulsby C. 2023. Effects of 66 years of water management and hydroclimatic change on the urban hydrology and water quality of the Panke catchment, Berlin, Germany, Science of The Total Environment, 900, 165764. https://doi.org/10.1016/j.scitotenv.2023.165764
Contact:
Dr. Christian Marx
c.marx@tu-berlin.de
Gustav-Meyer-Allee 25
13355 Berlin, Germany
Building 13b,
Room 517
Original Publication
+++ Call for Papers: Special Issue +++
Hydrological processes in urban systems
In: Hydrological Processes (HP)
https://onlinelibrary.wiley.com/page/journal/10991085/homepage/call-for-papers/si-2024-000191
Funding:
Other exciting upcoming talks from our group:
Motivation | Study site & development | Methods | Results | Discussion
Prof. Dr. Dörthe Tetzlaff
HS2.2.1/EGU24-4416 (Fri 15:25-15:35) Room B
Zhengtao Ying,
HS8.2/EGU24-602 (Wed, 17 Apr, 16:25-16:35) Room 2.44
Dr. Maria Magdalena Warter
HS10.8/EGU24-383 (Thur, 18 Apr, 14:25–14:35) Room 2.15
Famin Wang
PICO (Fri, 19 Apr, 08:53-08:55) PICO Spot A
Hanwu Zheng
GM6.3/SSP3.8/EGU24-140 (Fri, 19 Apr, 16:20–16:30) Room 2.91
Hyekyeng Jung
HS3.4/EGU24-811 (Fri, 19 Apr, 17:38–17:48) Room 2.31
Prof. Soulsby
Prof. Tetzlaff
Prof. Hinkelmann