## Slide 1
An Integrated Hydrological Modeling Framework for Enhancing Water-Energy Nexus in the Godavari River Basin, India
Prof. Kasiviswanathan KS
Associate Professor, IIT Roorkee, India
Mobile: +91 9952 199 196
Email: k.kasiviswanathan@wr.iitr.ac.in
Kasiviswanathan KS, Chandni Thakur

## Slide 2: Background

## Slide 3: Water-Energy-Food Nexus
How does El Niño impact India’s water resources, agricultural output and energy production???
Food for Water
Agricultural runoff and water quality
6

## Slide 4: Water-Energy Nexus

## Slide 5: Introduction
Enhanced Calibration
Hydrological models:
    Strengthen the accuracy of hydrological modelling
    Decrease the uncertainty in El Niño impact assessment on water-energy nexus
El Niño
El Niño:
Impacts Indian summer monsoon rainfall
Historical droughts and rainfall deficits
Implications on streamflow and hydropower
Affects water resources, economy and stakeholders
Hydrological Modelling
  Hydrological models:
  To assess the impacts of El Niño on water-energy nexus
  Limitations:
  Uncertainty in the model simulations
  Single site calibration
  Equifinality
  Local optimization
Water-Energy Nexus
  El Niño Impacts:
  On ISMR are bound to affect water-energy nexus
  Water and energy security during El Niño
  Mitigating El Niño impacts on hydro-energy vulnerability
  Resilient run-of-river small hydropower sites

## Slide 6: Godavari River Basin (GRB)
Geographical Location: covers approximately 9.5% of the country’s geographical area i.e. 312,812 km2
Climate: experiences a tropical climate and ISMR accounts for approximately 85% of the annual rainfall
Water Infrastructures: More than 15 major dams and reservoirs, with a combined storage capacity exceeding 21 billion m3 and installed hydropower generation capacity exceeds 2.7 GW
Vulnerability: A significant reduction in annual water discharge due to declining annual rainfall, leading to frequent agricultural and hydrological droughts
Future Projections: An increase in the frequency of droughts from 2053 to 2099

## Slide 7: Introduction to the VIC Model
The Variable Infiltration Capacity Model
A large-scale, semi-distributed hydrological model (Liang et al.1994)
Sub-grid heterogeneity (e.g. elevation, land cover) is handled via statistical distributions
Developed for coupled Land Surface Model (LSM) – Global Circulation Model (GCM) simulations
Open-source development

## Slide 8: Workflow of the VIC Model
Note: The VIC model has been developed for use on Linux platforms and requires pre-processing of input data in an ASCII format at each grid level: a time consuming process

## Slide 9: Need to Improve VIC Calibration Process?
Manual Calibration (Hengade et al. 2018;Shah and Mishra 2016; Mishra et al. 2020)
  Time-consuming
  Subjectivity
  Automatic optimization algorithms (Downhill simplex method, Genetic algorithm)
    Poor parametrization: unable to handle high dimensionality
    Computationally inefficient: large number of model runs required
    Equifinality: various parameter sets reproducing identical output
    Need of an automatic calibration framework providing more realistic model parameter estimates and is computationally more efficient

## Slide 10: Calibration Framework
Chandni Thakur, Venkatesh Budamala, KS Kasiviswanathan, Claudia Teuschbein, Bankaru-Swamy Soundharajan (2024). Advancing the Calibration of Macroscale Hydrological Models by Integrating Sensitivity Analysis, Adaptive Pseudo-modeling Optimization and Multi-site Calibration. (Revision is under review, Water Resources Research)

## Slide 11: Datasets
Data Parameter | Source/Product Name | Spatial Resolution | Temporal Resolution | VIC Requirement
Precipitation | IMD | 0.25° × 0.25° | Daily | Daily
Minimum and Maximum Temperature | IMD | 1° × 1° | Daily | Daily
Elevation Data | SRTM DEM | 30 m | - | -
Soil Data | FAO-HWSD | 30 arc-second (~1 km) | - | -
LULC Data | NASA’s ORNL DAAC Portal | 100 m | - | Annual
Leaf Area Index (LAI) | MCD15A3H (MODIS Terra + Aqua Combined) | 500 m | 4 Days | Monthly
Shortwave Albedo | MCD43A3 | 500 m | Daily | Monthly
Observed Streamflow | CWC | PG Bridge, Konta, Tekra and Polavaram | Daily | Daily
Oceanic Niño Index | NOAA | - | 3 Months | -

## Slide 12: Methodological Framework

## Slide 13: El Niño Years
El Niño events were classified based on the mean monthly ONI values from National Oceanic and Atmospheric Administration (NOAA) during 1950-2020.
Source: http://www.cpc.noaa.gov/data/indices/
Event | Years
El Niño (19) | 1951, 1953, 1957, 1958, 1963, 1965, 1969, 1972, 1982, 1983, 1987, 1991, 1992, 1997, 2002, 2004, 2009, 2015, 2019
Normal (8) | 1960, 1961, 1962, 1967, 1981, 1990, 1993, 2013

## Slide 14: Model Performance
Calibration
Validation
Comparison of daily observed (red) and the VIC simulated (blue) streamflow (m3/s) for the (a) Calibration (2003-2012), (b) Validation (2013-2017) periods at the selected gauge stations Polavaram, Konta, Tekra and PG Bridge

## Slide 15: GIS Analysis for Head Assessment
Stream Network Generation:
Utilized SRTM 30 m x 30 m resolution DEM
Hydraulic Head and Waterway Length Determination:
Points densified at 500 m intervals (Backwater from downstream)
Maximum waterway length set at 3000 m (minimize the overall cost of penstock)
Additional point layers generated at intervals of 1000 m to 3000 m
500m point layer was prioritized to select/remove any intersecting points with other layers
Criteria for Technical Potential Assessment:
POSH meeting head threshold equal to or greater than 10 m
Spatial distribution of potential RoR-SHP sites that satisfied the criteria for head (H ≥10m)

## Slide 16: Selected Run-of-river Small Hydropower Sites
Site | Head (m) | Waterway Length(m) | Flow (m3/s) |  |  | Power (MW) |  |  | Energy (TWh/yr) |  | 
 |  |  | Q30 | Q75 | Q90 | P30 | P75 | P90 | E30 | E75 | E90
POSH,MW1 | 10 | 3000 | 338 | 36 | 26 | 26 | 3 | 2 | 0.10 | 0.01 | 0.01
POSH,MW2 | 40 | 2500 | 115 | 15 | 12 | 36 | 5 | 4 | 0.12 | 0.02 | 0.02
POSH,MW3 | 27 | 2500 | 326 | 35 | 25 | 69 | 7 | 5 | 0.25 | 0.03 | 0.02
POSH,MW4 | 26 | 2000 | 130 | 17 | 14 | 27 | 3 | 3 | 0.09 | 0.02 | 0.01
POSH,MW5 | 11 | 2000 | 338 | 36 | 26 | 29 | 3 | 2 | 0.11 | 0.01 | 0.01
POSH,MW6 | 16 | 2000 | 260 | 32 | 23 | 33 | 4 | 3 | 0.10 | 0.02 | 0.01
POSH,MW7 | 10 | 1500 | 338 | 36 | 26 | 26 | 3 | 2 | 0.10 | 0.01 | 0.01
POSH,MW8 | 11 | 1500 | 1530 | 181 | 144 | 132 | 16 | 12 | 0.46 | 0.07 | 0.05
POSH,MW9 | 15 | 1000 | 338 | 36 | 26 | 40 | 4 | 3 | 0.15 | 0.02 | 0.01
POSH,MW10 | 29 | 500 | 115 | 15 | 12 | 26 | 3 | 3 | 0.22 | 0.02 | 0.01
POSH,MW11 | 24 | 500 | 326 | 35 | 25 | 61 | 7 | 5 | 0.06 | 0.03 | 0.02

## Slide 17: El Niño Impacts
Energy
Flow
Power
Flow, Power and Energy during El Niño, normal and all years for 11 filtered sites

## Slide 18: Resilient Hydropower Sites during El Niño
Power
Energy
Annual technical hydropower potential and annual energy (GWh/yr) for potential sites under El Niño

## Slide 19: Conclusions
The GRB demonstrated the significant collective technical potential (226 POSH) for RoR-SHP hydropower generation, capable of producing approximately 4.09 TWh/yr, 0.53 TWh/yr, and 0.4 TWh/yr with 30%, 75%, and 90% flow dependability
11 potential sites for Run-of-river small hydropower (RoR-SHP) were identified based on the threshold for annual technical power (2-25 MW) with 90% flow dependability (computed across the period 1951-2020, considering all years)
A decline of 46%, 38%, and 18% in annual energy at 30%, 75%, and 90% flow dependability in El Niño years compared to normal years
Potential sites maintaining the firm power (90% flow dependability) even during El Niño years (computed across the period 1951-2020, considering El Niño years only) were proposed
The integration of the VIC model and GIS provided a thorough assessment of the potential of RoR-SHP in the GRB, particularly in mitigating energy vulnerability during El Niño events
The finding underscored the increased risk of power shortages during El Niño years and emphasized the need to develop appropriate strategies to cope with the risks associated with El Niño events

## Slide 20: Acknowledgement
Chandni Thakur
Ph.D. Scholar
WRD&M Department
IIT Roorkee
Mobile: +91 8894 046 468
Email: chandnithakur2@gmail.com
The authors are thankful to Swedish Research Council (Vetenskapsrådet, VR) for providing financial support for carrying out this study (Grant Number: 2018-05848)

## Slide 21
Suggestions/Feedback
THANK YOU!