## Slide 1
Funded by the European Union. Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union or the European Climate, Infrastructure and Environment Executive Agency (CINEA). Neither the European Union nor the granting authority can be held responsible for them. This project has received funding under grant agreement No 101112879 (INSPIRE).
www.inspire-europe.org / Inspire Europe (LinkedIn) / Inspire Europe (Facebook) / inspire_eu (Instagram) / INSPIRE_EUROPE (X)
Large-scale remote monitoring of riverine litter to evaluate effectiveness of clean-up technologies
Robrecht Moelans, Liesbeth De Keukelaere, Els Knaeps, Marian-Daniel Iordache, Klaas Pauly, Ils Reusen
ITS3.24/HS12.9: Advances in plastic pollution monitoring across the Geosphere

## Slide 2: Introduction
Litter on Land
Target: hot spots & densities
Scene = more static
=> mobile camera (UAV)
More variation in background
Floating Litter
Target: number of floating items per time (flux)
Scene = very dynamic
=> fixed camera (bridge)
Camera set-up & installation
Only high-resolution RGB data (camera on bridge or UAV)
Only macro-litter on rivers & riverbanks

## Slide 3: Floating Macro-Litter on Rivers

## Slide 4: Test & Development Set-up
View of test set-up at bridge over canal (width 35m) close to VITO HQ (Mol – Belgium)
Test set-up useful for:
Generate training data, e.g. via release-and-catch experiments
Concept testing
Protocols developed and defined in Horizon Europe Project “INSPIRE”
  www.inspire-europe.org / Inspire Europe (LinkedIn) / Inspire Europe (Facebook) / inspire_eu (Instagram) / @INSPIRE_EUROPE (X)
Example of image taken with RGB camera during release & catch experiment with litter received from the port of Antwerp
RGB
Multispectral VNIR
Multispectral SWIR

## Slide 5: Operational Set-up
Development => Operational
Equipment
  Cost
  Water resistant
  Robust
Power supply
Remote connection & control
Recording schedule, storage & transfer
Specific site conditions
Auxiliary sensors
Rhine
Scheldt
Po
Source: Google Earth
Example image taken with Reolink camera installed on bridge close to VITO HQ (Mol – Belgium)

## Slide 6: Detect Floating Macro-Litter Objects
Faster RCNN (Region-Based Convolutional Neural Network)
Detectron 2 platform of Meta AI
  https://github.com/facebookresearch/detectron2
In general, very good results
Some false positives if water surface is less homogeneous:
  Reflection at water surface (sun or sky)
  Bottom visible (link with tide)
  Waves
  Shadows
  Turbidity plumes
  White caps / foam
=> Annotate more data
Image from RGB camera on bridge over canal close to VITO HQ
(Mol – Belgium)

## Slide 7: From Detecting Objects to Plastic Flux
Plastic Flux = how many plastic objects pass per unit time on a river
Camera on bridge: only objects at or close to water surface (floating)
Procedure
  Install enough cameras to cover complete cross-section of river (tide!)
  Detect plastic objects in individual images
  Recognize same object in different images (frame rate, current, wind, etc.)
  Add only new objects to object counter

## Slide 8: Plastic Flux: Example
Images from RGB camera on bridge over canal close to VITO HQ (Mol – Belgium)

## Slide 9: Personalize Segment Anything
https://arxiv.org/pdf/2305.03048.pdf
(1) User provides
One Image
One Mask
(2) One-shot Tuning
(3) Personalized Segmentation
Results generated based on tutorial Niels Rogge:
https://github.com/NielsRogge/Transformers-Tutorials/tree/master/PerSAM

## Slide 10: Macro-Litter on Riverbank

## Slide 11: Data Acquisition on Land
Image taken with DJI Phantom 4 Pro at an altitude of 50 meter above the ground (Vietnam)

## Slide 12: Detect Macro-Litter Objects
Image classification
Resnet-50 model trained with equal number of patches with and without litter
  Prediction accuracy of 91.6%
Benefits of approach include:
  Fast and simple to train
  Can easily include more labelled data
  End product easy to look at (binary map)
Litter patches
No litter patches

## Slide 13: Detect Macro-Litter Objects
Blue = Litter detected in patch
Red = No litter detected in patch
Image taken with DJI Mini 3 Pro at an altitude of 15 meter above the ground (Bocholt-Herentals Canal in Belgium)