## Slide 1
Soil erosion & sediment transport  global environmental issues  degradation of land, deterioration of ecological balance
Eroded material in high elevated mountains  gravel-bed channels  downstream reaches  morphology of downstream reaches and alluvial plains (Johnson and Whipple, 2007)
Monitoring coarse grain transport  traps, acoustic sensors, grain tracking (RFIDs)  challenging during floods, expensive
Global perspective
Painted tracers – cost effective alternate
© JPPVL, Uttarakhand
Role of ISM in annual transport?
Implications of using local vs c/s averaged hydraulic forcing?
Role of partial vs full transport conditions?
Himalayan perspective
Huge transport of coarse material particularly during Indian Summer Monsoon (ISM)
Relatively lesser investigated
No known scientific observatory in Himalayas
Objectives
EGU General Assembly 2024
Estimating bed material transport in Himalayan streams using the virtual velocity approach
Anshul Yadav*, Sumit Sen, Luca Mao, Marwan A. Hassan

## Slide 2
Study Area
Measurements on flood specific tracer mobility, virtual velocity, active layer depth, GSD, flow depth
Using local shear stresses, annual bed material transport  37600 m3 (± 11500 m3), and 11000 m3 (±3600 m3) in Aglar and Paligad, respectively (~60 % during monsoon).
Using c/s averaged shear stresses, annual transport  42300 t (±15800 t) and 12200 t (±4700 t), in Aglar and Paligad respectively, (~79 % and 68 % during monsoon respectively).
Break in transport curves (abrupt increase in transport rates)
Virtual velocity approach (VVA)

## Slide 3: Proposal of a unified function for smoother transition from PT to FT
Partial transport
Original Mi in VVA
Modified Mi
Full transport
Original Mi in VVA
Modified Mi
Major Conclusions:
Significant transport during long-term low magnitude non-monsoon flows (~40 %).
Using local vs c/s averaged shear stresses results in rather different transport estimates.
Proposed unified function seems to better capture the transport dynamics retaining the physics of VVA.

## Slide 4: Part b – Detailed presentation

## Slide 5: Virtual velocity approach
The unit mass fractional transport rate (qi, in kg.m-1.s-1) (Wilcock, 1997)
Mi - mass of sediments of i-size entrained from a certain surface area over a certain time (in kg. m-2)
Vi - virtual velocity of the i-size sediments (m.s-1) (Stelczer, 1971)
The total unit mass transport rate (kg.m-1.s-1) for the transported sediment.
Virtual velocity (Vi)=
Duration of competent flow – duration for which Shield’s stress exceeds the mobility thresholds
For partial transport (PT), =
For full transport (FT) (sub-surface material also gets transported), =
    mi - mass of an individual grain of fraction i (kg)
    Fi - proportion of fraction i in the surface GSD
    Di - diameter of fraction i (m),
    Yi - percentage of surface grains of fraction i entrained during the transport event
    -thickness of the active sediment layer

## Slide 6: Workflow of calculations

## Slide 7: Field observations

## Slide 8: Bed proportion mobility, active layer, and virtual velocity
Parameters | Site | Equations | Statistics
Y | Aglar |  | R2 = 0.97, RMSE = 0.068, p < 0.001
 | Paligad |  | R2 = 0.98, RMSE = 0.044, p < 0.001
ds | Aglar |  | R2 = 0.67, RMSE = 0.05 m, p < 0.001
 | Paligad |  | R2 = 0.77, RMSE = 0.06 m, p < 0.001
Vi | Aglar |  | R2 = 0.45, RMSE = 2.10 m/hr, p < 0.001
 | Paligad |  | (R2 = 0.40, RMSE = 1.39 m/hr, p < 0.001)
Parameters | Site | Equations | Statistics
Y | Aglar |  | R2 = 0.97, RMSE = 0.068, p < 0.001
 | Paligad |  | R2 = 0.98, RMSE = 0.044, p < 0.001
ds | Aglar |  | R2 = 0.67, RMSE = 0.05 m, p < 0.001
 | Paligad |  | R2 = 0.77, RMSE = 0.06 m, p < 0.001
Vi | Aglar |  | R2 = 0.45, RMSE = 2.10 m/hr, p < 0.001
 | Paligad |  | (R2 = 0.40, RMSE = 1.39 m/hr, p < 0.001)
Overall, 1346 and 966 tracers were recovered in Aglar and Paligad, respectively

## Slide 9: Transport curves and active sediment layer

## Slide 10
Intra cross-sectional variability of bed material transport and key input parameters

## Slide 11
Bed material loads

## Slide 12: Unified function for smoother transition from PT to FT
Partial transport
Original Mi in VVA
Modified Mi
Full transport
Original Mi in VVA
Modified Mi

## Slide 13: How modified flow resistance equations improves bed material transport estimated using conventional equations?
Increased flow resistance
  Either use increased mobility thresholds (evolves with space and time- difficult to measure)
  Use reduced/effective shear stress
  Slope decomposition approach
  Reduced/effective shear stress
Total loads – July 2021 – June 2022

## Slide 14: Major findings
    High energetic floods  Huge mobilization of coarse sediments during the monsoon  still significant transport during long-term low-magnitude (non-monsoon) flows
    Long-term low-magnitude flows (non-monsoonal contribution) (~ 40 % using local shear stress, ~ 20 using cross-sectional average shear stress)
    The overall annual contribution of PT (~ 5 % local shear stress, ~ 20% using cross-sectional average shear stress)
    The different formulations of active layer results in different transport estimates (differing nearly one order of magnitude)  need more research on the characterization of the active layer
    Bed elevation was assumed constant throughout the event  need of technology for continuous spatiotemporal monitoring of bed elevation changes and active layer depth
Yadav, A., Sen, S., Mao, L., & Hassan, A. M. (2023). Estimation of bed material transport in gravel-bed streams using the virtual velocity approach: Insights from the North-western Himalayas, India. Earth Surface Processes and Landforms (under review)

## Slide 15: Scope for future research
Need for better characterization of flow resistance and its incorporation in bedload equations/models
Technological advancements for continuous spatiotemporal measurements on bed elevation and active layer depth
Impacts of flood sequencing on tracer dispersion
Exploring the explicit effects of flow regulation and sediment mining on observed flow, sediment and morphological regime

## Slide 16: References
Recking, A., Liébault, F., Peteuil, C., Jolimet, T., 2012. Testing bedload transport equations with consideration of time scales. Earth Surf. Process. Landforms 37, 774–789.
Recking, A., 2012a. Influence of sediment supply on mountain streams bedload transport. Geomorphology 175, 139–150.
Yager, E.M., Turowski, J.M., Rickenmann, D., McArdell, B.W., 2012. Sediment supply, grain protrusion, and bedload transport in mountain streams. Geophys. Res. Lett. 39.
Wilcox, A.C., Wohl, E.E., 2006. Flow resistance dynamics in step‐pool stream channels: 1. Large woody debris and controls on total resistance. Water Resour. Res. 42.
Mao, L., Toro, M., Carrillo, R., Brardinoni, F., Fraccarollo, L., 2020. Controls over particle motion and resting times of coarse bed load transport in a glacier‐fed mountain stream. J. Geophys. Res. Earth Surf. 125, e2019JF005253.
Recking, A., Frey, P., Paquier, A., Belleudy, P., Champagne, J.Y., 2008. Feedback between bed load transport and flow resistance in gravel and cobble bed rivers. Water Resour. Res. https://doi.org/10.1029/2007WR006219
Bonilla-Porras, J.A., Armanini, A., Crosato, A., 2021. Extended Einstein’s parameters to include vegetation in existing bedload predictors. Adv. Water Resour. 103928.
Kothyari, U.C., Hashimoto, H., Hayashi, K., 2009. Effect of tall vegetation on sediment transport by channel flows. J. Hydraul. Res. 47, 700–710.
Wilcock, P.R., 1992. Flow competence: A criticism of a classic concept. Earth Surf. Process. Landforms 17, 289–298.
Ancey, C., Pascal, I., 2020. Estimating mean bedload transport rates and their uncertainty. J. Geophys. Res. Earth Surf. 125, e2020JF005534.
Campbell, F.B., Bauder, H.A., 1940. A rating‐curve method for determining silt‐discharge of streams. Eos, Trans. Am. Geophys. Union 21, 603–607.
Jain, M.K., Kothyari, U.C., 2000. Estimation of soil erosion and sediment yield using GIS. Hydrol. Sci. J. 45, 771–786.
Pandey, A., Himanshu, S.K., Mishra, S.K., Singh, V.P., 2016. Physically based soil erosion and sediment yield models revisited. Catena 147, 595–620.
Turowski, J.M., Rickenmann, D., Dadson, S.J., 2010. The partitioning of the total sediment load of a river into suspended load and bedload: a review of empirical data. Sedimentology 57, 1126–1146.

## Slide 17: Thanks