## Slide 1: Observing the Ammonia Daily Cycle over Agricultural Areas in Asia Using Combined Satellite Measurements
Iorga, A.1,2, Harrison, J.J.1,2 and Moore, D.P.1,2
1 School of Physics and Astronomy, University of Leicester, UK, 2National Centre for Earth Observation, Leicester, UK

## Slide 2: Agriculture and Air Quality
The Threat: Big Agriculture and Ecological Collapse
    The agricultural sector emits NH3 into the atmosphere that contributes to environmental degradation (soil, water, air) and respiratory diseases
    Largest NH3 hotspots: agricultural areas in South and East Asia
    NH3 concentrations are expected to rise with average global temperatures due to climate change
The Challenge: Rapid Changes and Sparse Measurements
    NH3 is difficult to monitor due to its short atmospheric life-time (a few hours)
    Ground observations are sparse and not many countries have networks that monitor NH3 (particularly over Asia, Africa and South America)
The Solution: Combined Global Satellite Observations
    Combined satellite observations can give information on the evolution of NH3 concentrations over large areas throughout a day where no ground observations are available

## Slide 3: Preliminary results
We want to produce one OE-based NH3 retrieval scheme for the IASI and CrIS instruments
Using the same retrieval setup and a-priori profiles would remove any possible biases
First attempts observing the NH3 diurnal cycle over selected regions in the Indo-Gangetic Plain (IGP) for spring, autumn and winter
IASI and CrIS have higher signal-to-noise ratios than current geostationary satellites observing Asia
NH3 total columns over South East Asia, 3rd April 2022, IASI day time observations.

## Slide 4: Summary – Quick links
Effects on the environment
Chemistry and spectroscopy
Challenges of retrieving NH3
Satellite instruments
Retrieval scheme
Fast detection scheme
Satellite observations
Seasonal cycle
Daily cycles
BACKGROUND
METHOD
RESULTS
CONCLUSIONS
ABOUT ME

## Slide 5: Ammonia (NH3)
Most NH3 (>70%) is produced from agriculture through the usage of N-based fertilisers and animal husbandry
Current budget highly uncertain ~50-130 TgN
Higher surface temperatures promote faster volatilisation rates of NH3 from soils
Contributes to the acidification and eutrophication of soils and water bodies (1) through deposition leading to vegetation damage and biodiversity loss
Reacts with acids in the atmosphere to form PM2.5 leading to smog (2) and poor air quality
1
2
Harmful algae bloom causing “dead zones” in water bodies
NH3-derived PM2.5 decreases visibility in cities near agricultural areas

## Slide 6: NH3 Spectroscopy and Atmospheric Chemistry
NH3 reacts with atmospheric acids to form aerosol (ammonium salt)
Strongest signal at Q–branch features ν2 band

## Slide 7: The Challenges of Retrieving Ammonia
Concentrations vary rapidly over space and time (highly reactive gas)
IR satellite measurements require high thermal contrast near the surface (most NH3 is found ~ 0-2 km)
High thermal contrast results in a better NH3 signal
More difficult to monitor ammonia at night

## Slide 8: Satellite Instruments
IASI
Operated by EUMETSAT
MetOp –A, -B, -C satellites
Polar orbiting, nadir viewing
Local overpass 9:30 AM/PM
Swath 2200 km
12 km diameter footprint
50 x 50 km FOV (4 pixels, 2 x 2)
Spectral range 645 – 2760 cm-1
Spectral resolution 0.5 cm-1
CrIS
Operated by NOAA
Suomi-NPP, NOAA-20, NOAA-21 satellites
Polar orbiting, nadir viewing
Local overpass 1:30 AM/PM
Swath 2200 km
14 km diameter footprint
50 x 50 km FOV (9 pixels, 3 x 3)
Spectral range 650 – 2550 cm-1
Spectral resolution 0.625 cm-1

## Slide 9: University of Leicester IASI Retrieval Scheme – (ULIRS)
Mixing ratio (ppmv)
Altitude (km)
NH3 a-priori
NH3 averaging kernel
Altitude (km)
Uses the Levenberg-Marquardt method -Optimal Estimation-based (OE)
NH3 active in the IR range (920-940 cm-1 and 960-980 cm-1 Q-branches give the strongest signal)
Cloud free observations only
11 levels equidistant pressure grid
Produces averaging kernels
Uses the Reference Forward Model (RFM) – line-by-line radiative transfer model developed at the University of Oxford
NH3, H2O, CO2, O3, and temperature profile co-retrieved with N2O, CFC-12 also in the microwindow
Uses 3 different NH3 a-priori profiles depending on NH3 pollution level (low, moderate, high) – Fast Detection Scheme
The CrIS Algorithm For Trace gases (CRAFT) is used as the retrieval scheme for the CrIS instrument. It is based on ULIRS and uses the same set of parameters, but currently is optimised for the high NH3 case only.
Notes: What other information to include? DOFS? Residuals? Fast Linear Retrieval Scheme – HRI?

## Slide 10: Quick detection as input to ULIRS
NH3 a-priori
A scaling factor x is retrieved using a one-step linear process
K is the difference between a calculated IASI spectrum with target gas (for a fixed atmospheric profile), and one without
y is a measured IASI spectrum in the region of interest (cloud fraction 0-20 %)
y̅ is an averaged climatological background spectrum (cloud fraction 0-20 %) over the Asia region for each month in 2022:
Sy is the corresponding variance-covariance matrix:
K is calculated using the RFM and an assumed target gas profile
  Assumes a typical surface emissivity
  Assumes climatological pressure, temperature, humidity profiles
  Cloud-free scene
x scales the target gas profile, before conversion to a total column
J.C. Walker et al. (2012), J. Geophys. Res., 117, D00U16
Notes: What other information to include? DOFS? Residuals? Fast Linear Retrieval Scheme – HRI?

## Slide 11: Fast Detection Scheme Day Time Observations
The Fast Detection Scheme (used by ULIRS) is used to determine 3 different NH3 a-priori profiles depending on the pollution case.
Fast detection 3rd April 2022
ULIRS 3rd April 2022
NH3 detection index

## Slide 12: Fast Detection Scheme Night Time Observations
Negative thermal contrast (the surface temperature is lower than the temperature of the atmospheric layer where NH3 peaks) can be observed in the fast detection for values smaller than -5
We are still trying to implement this correctly in the retrieval.
Fast detection 3rd April 2022
ULIRS 3rd April 2022
NH3 detection index

## Slide 13: NH3 Satellite Observations - Spring
Top left: CrIS night time (1:30)
Top right: IASI day time (9:30)
Bottom left: CrIS day time (13:30)
Bottom right: IASI day time (21:30)
Date: 8th April 2022
CrIS NH3 night time total columns are higher than IASI night time over much of the Indo-Gangetic Plain. We are still investigating the IASI retrieval.
CrIS retrieval is only optimised over the Indo-Gangetic Plain.
CrIS night
CrIS day
IASI night
IASI day

## Slide 14: NH3 Satellite Observations - Summer
Top left: CrIS night time (1:30)
Top right: IASI day time (9:30)
Bottom left: CrIS day time (13:30)
Bottom right: IASI day time (21:30)
Date: 30th July 2022
The monsoon season takes place between late June and early September in India.
This makes is more difficult to observe NH3 during summer.
CrIS day
CrIS night
IASI day
IASI night

## Slide 15: NH3 Satellite Observations - Autumn
Top left: CrIS night time (1:30)
Top right: IASI day time (9:30)
Bottom left: CrIS day time (13:30)
Bottom right: IASI day time (21:30)
Date: 26th October 2022
CrIS NH3 night time total columns are higher than IASI night time over much of the Indo-Gangetic Plain. We are still investigating the IASI retrieval.
NH3 peaks during spring (main fertilisation period) followed by smaller increases in autumn (second fertilisation period).
CrIS day
CrIS night
IASI day
IASI night

## Slide 16: NH3 Satellite Observations - Winter
Top left: CrIS night time (1:30)
Top right: IASI day time (9:30)
Bottom left: CrIS day time (13:30)
Bottom right: IASI day time (21:30)
Date: 26th January 2022
The NH3 daily cycle is much weaker during winter, although small increases in the total column can still be observed during the day.
Generally lower thermal contrast is seen during the day.
CrIS day
CrIS night
IASI day
IASI night

## Slide 17: Ammonia Seasonal Cycle India 2015-2022
Region: Northern India (25-30N 70-88E)
NH3 concentrations peak between late March and early July.
The peaks coincide with the agricultural season (when fertiliser is spread) and with raising temperatures.
NH3 concentrations decline during monsoon season (late July to Sep) as the gas is “washed out” of the atmosphere.
NH3 concentrations are at their minimum during winter.
Time series showing the NH3 seasonal cycle over the Indo-Gangetic Plain between 2015 and 2022 using IASI day time observations.

## Slide 18: NH3 Diurnal Cycle Study Areas - Indo-Gangetic Plain
Geographical and administrative map of the Indo-Gangetic Plain (IGP), including Pakistan, India and Bangladesh.
The mean NH3 total column was calculated inside the following grid box locations for each satellite overpass:
30-31N 73-74E (Punjab, Pakistan)
29-30N 76-77E (Haryana, India)
26-27N 81-82E (Uttar Pradesh, India)
The NH3 daily cycle is over-plotted with the thermal contrast from ERA5 data, defined as the difference between the surface and the atmosphere at 900 hPa.
Study area

## Slide 19: Punjab, Pakistan (30-31N 73-74E) - Spring
Legend
IASI data
CrIS data
- - - ERA5 TC

## Slide 20: Haryana, India (29-30N 76-77E) - Spring

## Slide 21: Uttar Pradesh, India (26-27N 81-82E) - Spring

## Slide 22: Punjab, Pakistan (30-31N 73-74E) - Autumn

## Slide 23: Haryana, India (29-30N 76-77E) - Autumn

## Slide 24: Uttar Pradesh, India (26-27N 81-82E ) - Autumn

## Slide 25: Punjab, Pakistan (30-31N 73-74E) - Winter

## Slide 26: Haryana, India (29-30N 76-77E) - Winter

## Slide 27: Uttar Pradesh, India (26-27N 81-82E ) - Winter

## Slide 28
Conclusions
An OE-based retrieval scheme for NH3 has been implemented for IASI and CrIS
A Fast Detection Scheme has been introduced for the IASI NH3 product
The NH3 seasonal and diurnal cycles have been studied over the IGP region
There are issues with small thermal contrasts suppressing IASI signals
Further work
Check consistency of IASI and CrIS night time observations
Implement Fast Detection Scheme into CRAFT
Extend study to include the North China Plain
Utilise new spectroscopic data in the retrieval
Compare satellite NH3 measurements to modelled NH3
Acknowledgements

## Slide 29: About me
3rd year PhD Candidate
Monitoring Air Quality from Space: IASI and CrIS retrievals of Ammonia over SE Asia
Based at Space Park Leicester, University of Leicester, UK
Contact: ai184@leicester.ac.uk