## Slide 1
Determination of the solubility, diffusion coefficient and hydrate stability of hydrogen sulfide in water and brine
Jiang Lei, Ph.D.
Institute of Deep-sea Science and Engineering,
Chinese Academy of Sciences
April 17, 2024
EGU General Assembly 2024

## Slide 2
cold-seeps
hydrothermal area
Background
The high-sulfur natural gas fields are widely distributed in western China.
H2S is prone to hydrate formation at low temperatures and high pressures, resulting in pipeline plugging, and subsequent pressure drop during natural gas production and transportation.
H2S gas is often detected in deep-sea cold seeps and hydrothermal regions, exerting significant influences on mineralization and biological activities.

## Slide 3
Experimental platform
Hydrate phase equilibrium conditions of gas-water system.
Growth dynamics of gas hydrate by measuring the consumption of gas over time.
Experimental platform of high-pressure optical cell
Hydrate research

## Slide 4
Experimental platform
Combined with laser Raman spectroscopy , HPOC can be used to measure the concentration and diffusion coefficient of gas in water across a wide range of temperatures and pressures
Heating-cooling stage
Thermocouple
273-603K
Pressurize
10-120MPa
Mercury
H2S-H2O
Principle

## Slide 5
Jiang L*, Xin Y, Chou IM, Sun R. Raman spectroscopic measurements of H2S solubility in pure water over a wide range of pressure and temperature and a refined thermodynamic model. Chem Geol. 2020;555:119816.
H2S solubility decreases with increasing temperature when the pressure is below 3 MPa. However, when pressure above 5 MPa, solubility first increases and then decreases with increasing temperature. A similar solubility change trend has been observed for other gases, such as CO2 and CH4
Solubility of H2S in water
H2S solubility in water at various temperature and pressure

## Slide 6
Huang Y, Wu C, Chen Y, Chou IM, Jiang L*. Measurement of diffusion coefficients of hydrogen sulfide in water and brine using in-situ Raman spectroscopy. Fluid Phase Equilib. 2022;556:113381.
Diffusion coefficient of H2S in water and brine
Diffusion coefficient of H2S is mainly controlled by temperature, and is inhibited by salinity.
Match well at low temperatures but show wide deviations at high temperatures ( > 350 K)
Compared with previous experiments

## Slide 7
Sun J, Xin Y, Chou IM, Sun R, Jiang L*. Hydrate Stability in the H2S–H2O system—Visual Observations and Measurements in a High-Pressure Optical Cell and Thermodynamic Models. J Chem Eng Data. 2020;65:3884-92.
Stability of H2S hydrate
1. Phase equilibrium conditions in water
H-I-Lw-H2S(g)
H-Lw-H2S(g)-H2S(l)
We extended the experimental pressure to 66.128 MPa for the H−Lw−H2S (l) phase boundary,
The upper quadruple point (Q2) was located at 302.7 K and 2.2407 MPa and the lower quadruple point (Q1) was located at 272.4 K and 0.0986 MPa.

## Slide 8
Sun J, Sun R, Ming Chou I, Nguyen AV, Jiang L*. Experimental measurement and thermodynamic modeling of dissociation conditions of hydrogen sulfide hydrate in the presence of electrolyte solutions. Chem Eng J. 2022;431:133821.
Stability of H2S hydrate
1. Phase equilibrium conditions in electrolyte solutions
LHV equilibrium curves shift more and more toward low temperatures and high pressures as the concentration of the electrolyte solutions increases.
The inhibitory effect of six electrolytes on H2S hydrate formation is in the order of MgCl2 > NH4Cl > NaCl > KCl > Na2SO4 = K2SO4.
The inhibitory effect of different electrolytes
Np - experimental data
T0eq / Tsalt eq - H2S hydrate dissociation temperature in pure water and salt solutions at the same pressure

## Slide 9
Stability of H2S hydrate
The electrolytes disturb the network of hydrogen bonds in water.
The more the water activity is affected, the stronger the inhibition effect of salt on hydrate equilibrium conditions will be
Why does electrolyte have an inhibitory effect on the stability of hydrates?

## Slide 10
Wu C, Chen J, Sun J, Chou IM, Mei S, Lin J, Jiang L*. Experimental determination and thermodynamic modeling of the hydrogen sulfide hydrate solubility in water. Chem Eng Sci. 2023:119474.
Stability of H2S hydrate
2. Solubility of H2S hydrate
The solubility of hydrogen sulfide (H2S) hydrate, which determines the minimum concentration required for hydrate stability.
The solubility of H2S hydrate in water was determined at temperatures ranging from 273.15 to 301.15 K with a 4 K increase and pressures ranging from the H–Lw–V three-phase equilibrium pressure for each temperature to 100 MPa.

## Slide 11
Thanks
EGU General Assembly 2024
Sun J, Xin Y, Chou IM, Sun R, Jiang L*. Hydrate Stability in the H2S–H2O system—Visual Observations and Measurements in a High-Pressure Optical Cell and Thermodynamic Models. J Chem Eng Data. 2020;65:3884-92.
Sun J, Sun R, Ming Chou I, Nguyen AV, Jiang L*. Experimental measurement and thermodynamic modeling of dissociation conditions of hydrogen sulfide hydrate in the presence of electrolyte solutions. Chem Eng J. 2022;431:133821.