## Slide 1
Issa Leye, Andrew Ogilvie, Soussou Sambou and Didier Martin
Vienna, Austria : HS6.9, Thu 01 May, 08:45-08:47 | PICO4.6 | EGU25-11344
Improved floodplain modelling with FABDEM and Sentinel-2 earth observations in the middle valley of the Senegal River

## Slide 2
Study area and objectives
1900 km2 floodplain
Bakel
Floodplain of Senegal river basin
Annual inundation
Limited knowledge (sparse observations, flat topography)
Supports flood-recession agriculture & associated ecosystem services
Map surface water dynamics through
  - 2D hydraulic modelling (HEC-RAS)
  Combining advances in remote sensing - DEM (Fabdem, Copdem),
  Sentinel-2 inundation maps, and field data
Matam
Podor

## Slide 3
HEC-RAS
Simulation
( Flood area)
Calibration
(Input parameters)
SENTINEL-2
MNDWI (Water-Bodies)
KGE,
F1-score
No
Yes
Flood mapping
Validation (model)
Yes
Methods
DEM Accuracy
Elevation
(FABDEM, TanDEM, COPDEM…)
Ground control points

## Slide 4
HEC-RAS: 2D Models
The 2D diffusion wave equations
2D flow area mesh in RAS Mapper (500m x 500m)
Methods

## Slide 5
Methods
Land use/land cover and Manning's Roughness Coefficient (n)
Land use | n
water | 0.028
Trees | 0.137
Flooded Vegetation | 0.068
Crops | 0.035
Built Area | 0.103
Bare ground | 0.027
Rangeland | 0.038
HEC-RAS: 2D Models

## Slide 6
HEC-RAS: Boundary conditions
Upstream: Flow Hydrograph
Downstream: Normal Depth
Methods
HEC-RAS: Meteorological Data
Precipitation
Evapotranspiration
HEC-RAS: 2D Models

## Slide 7
The Normalized Difference Water Index (NDWI).
Modified Normalized Difference Water Index (MNDWI).
Green: Band 3 ; NIR: Band 8 ; MIR: Band 11
Remote Sensing: Sentinel-2 (Water-Bodies)
Methods

## Slide 8
HEC-RAS and Sentinel-2: Comparison (Flooded areas/ Water-Bodies)
The harmonic mean of precision and recall (F1-score).
Precision is the ratio of true positive (TP) to the sum of true positive and false positive (FP), while recall is the ratio of true positive to the sum of true positive and false negative (FN).
value ranges from 0 to 1
Methods

## Slide 9
Results
Comparison of 6 DEMs with ground control points and river profiles
Best results with COPDEM, FABDEM and TANDEM
FABDEM has the lowest errors
126 ground control points
4 river profiles

## Slide 10
Results
Parameters |  | AW3D | COP | FABDEM | NASADEM | SRTM | TanDEM
MAE | Min. | 3,67 | 0,58 | 0,46 | 1,93 | 3,37 | 0,57
 | Median | 4,64 | 1,35 | 1,24 | 2,38 | 4,51 | 1,38
 | Max. | 10,39 | 9,1 | 9,24 | 7,62 | 11,62 | 6,09
RMSE | Min. | 3,9 | 0,72 | 0,58 | 2,63 | 4,03 | 0,72
 | Median | 4,86 | 2,28 | 1,66 | 3 | 5 | 1,9
 | Max. | 10,81 | 10,01 | 10,15 | 9,52 | 13,11 | 7,24
NSE | Min. | -5,42 | -1,7 | -2,13 | -1,79 | -4,87 | -0,69
 | Median | 0,35 | 0,89 | 0,92 | 0,8 | 0,34 | 0,91
 | Max. | 0,74 | 0,99 | 0,99 | 0,87 | 0,7 | 0,99
KGE | Min. | -2,8 | -1,53 | -1,57 | -1,48 | -2,68 | -0,53
 | Median | 0,5 | 0,86 | 0,84 | 0,79 | 0,52 | 0,87
 | Max. | 0,8 | 0,97 | 0,96 | 0,9 | 0,82 | 0,98
Best results with COPDEM, FABDEM and TANDEM

## Slide 11
Results
Lowering the altitudes of the minor bed of the main channel
HEC-RAS terrain reconditioning

## Slide 12
Simulation (water level)
Calibration (water level)
Simulation: KGE (0.80) Overestimate water level
Calibration: KGE (0.84) Better representation of water level
Results

## Slide 13
Simulation (water level)
Calibration (water level)
Simulation: KGE (0.84) Overestimate peak
Calibration: KGE (0.47) Overestimate recession
Results

## Slide 14
Simulation (Flooded area)
Calibration (Flooded area)
Results
Simulation: F1-Score (0.81), HEC-RAS overestimates flooded areas.
Calibration: F1-Score (0.86), Flooded area matches better SENTINEL-2.

## Slide 15
Results
Simulation (Flooded area)
Calibration (Flooded area)
Simulation: F1-Score (0.88), HEC-RAS overestimates flooded areas.
Calibration: F1-Score (0.91), Flooded area matches better SENTINEL-2.

## Slide 16
Results
Validation (Flooded area)
Podor: F1-Score (0.81), Flooded area matches better SENTINEL-2.
Ouoloum Néné: F1-Score (0.55), HEC-RAS overestimates flooded areas.

## Slide 17
Results
Flood mapping
Results for mapping flooded areas are very encouraging.

## Slide 18
Thank you for your attention