## Slide 1
Geochemical Assessment and Preliminary Source Tracing of
Sediment and Water Pollution in Major Korean Rivers
* Korea Institute of Geoscience and Mineral Resources (dwcho@kigam.re.kr)
Hyeop-Jo Han, Seon Yong Lee, Dong-Wan Cho*

## Slide 2
Previous National-scale Sedimnet Survey
Since 1990s, over 20,000 sediment samples have been collected across Korea.
Geochemical maps for major and toxic elements were created for environmental monitoring.
Foundation for pollution status and regional background levels.

## Slide 3
We collected 28 sediment and 28 water samples from six major rivers.(Currently, the number of sediment samples has increased to ~50.)
Over 50 major&trace elements were analyzed in each sample.
Some sediment samples showed high concentrations of As, Cd, Ni and Pb.
SMG River
Geum River
Yeongsan River
Nakdong River
Han River
Cheongyang
Current Study on Major Rivers (2024-2027)

## Slide 4
Geochemical indices (EF, Igeo) confirmed the pollution levels.
REE distribution was dominated by LREEs, reflecting granite influence.
Current Study on Major Rivers (2024-2027)

## Slide 5
Extra Slides
(Supplementary Information)

## Slide 6
Previous National-scale Sedimnet Survey
Since 1990s, over 20,000 sediment samples have been collected across Korea.
Geochemical maps for major and toxic elements were created for environmental monitoring.
Foundation for pollution status and regional background levels.

## Slide 7
Provision of a scientific basis for pollution management and source control
Comprehensive assessment was conducted using both river water and sediment samples.
Concentrations of heavy metals were analyzed alongside geochemical indicators (EF, Igeo).
Pollution levels were evaluated relative to background values to identify contamination.
Isotopic analyses of Cu, Pb, Zn, and Cs are used to trace pollution sources with high precision.
Rare earth element distributions provide additional insight into sediment origin and transport.
Geochemical indices such as Igeo help distinguish anthropogenic impacts from natural background.
Comprehensive Assessment of Heavy Metal Contamination
Integrated Geochemical Approach to Pollution Source Identification
Geochemical Investigation and Tracing of Sediment Pollution
Objectives

## Slide 8
Selected six key river systems for initial investigation, including Korea’s four major rivers (Han, Nakdong, Geum, Yeongsan)
Included additional sites near the Saemangeum reclaimed area and a mining-affected region
Collected 28 sediment samples and 28 water samples from these areas
Currently, the number of sediment samples has increased to approximately 50
SMG River
Geum River
Yeongsan River
Nakdong River
Han River
Cheongyang
Han River (HT)
Cheongyang (CY)
Yeongsan River (YS)
Geum River (KK)
SMG River (SMG)
Nakdong River (ND)
Sediment Sampling Sites in Korea

## Slide 9
Sediment samples were wet-sieved on-site using a 100-mesh sieve (<0.15 mm).
Background soils were collected from nearby hills at depths of less than 50 cm.
Trace elements in sediments were digested after 4-acid digestion (HF, HCl, HNO₃, HClO₄).
Instrumental analysis was conducted using ICP-OES and ICP-MS.
Sediment Sampling and Geochemical Analysis

## Slide 10
Contamination levels of each metal were assessed for every sample point.
Arsenic (As) concentrations were notably high in the CY sample.
→ This is likely due to the presence of a historical gold mine in the region.
Elevated As levels in other regions were observed only in samples 1 and 2. These samples are located near headwater areas of the river system.
→ Elevated As in these cases is interpreted as a result of geological background influence.
 | Grade I | Grade II | Grade III | Grade IV
As | 0 ~ 15 | 15 ~ 44.7 | 44.7 ~ 92.1 | ≥ 92.1
Cd | 0 ~ 0.4 | 0.4 ~ 1.87 | 1.87 ~ 6.09 | ≥ 6.09
Cr | 0 ~ 112 | 112 ~ 224 | 224 ~ 991 | ≥ 991
Cu | 0 ~ 48 | 48 ~ 228 | 228 ~ 1,890 | ≥ 1,890
Ni | 0 ~ 40 | 40 ~ 87.5 | 87.5 ~ 330 | ≥ 330
Pb | 0 ~ 59 | 59 ~ 154 | 154 ~ 459 | ≥ 459
Zn | 0 ~ 363 | 363 ~ 1,170 | 1,170 ~ 13,000 | ≥ 13,000
Korean Sediment Quality Standards for Individual Heavy Metals
Metal-Specific Sediment Pollution Evaluation

## Slide 11
Cd was notably elevated in sample HT-1, along with high concentrations of Cu, Pb, and Zn.
→ These multi-element patterns suggest a hydrothermal origin influenced by local geology
Cr&Ni were elevated in CY-4, the most downstream site near a former gold mine
→ Likely influenced by nearby industrial activity rather than geology
Cu and Zn were elevated in ND-4 and ND-5, collected from an urban area.
→ Being downstream sites (3rd–5th order streams), they are likely influenced by urban runoff.
Metal-Specific Sediment Pollution Evaluation

## Slide 12
Grade | Condition
Unpolluted | All element concentrations are below the threshold for Grade 1
Slightly Polluted | At least one element exceeds the threshold for Grade 1 but none exceed that for Grade 2
Moderately Polluted | The index based on Metal Grade II criteria is equal to or greater than 0.34.
Heavily Polluted | At least one element exceeds the threshold for Grade 3
Korean Criteria for Integrated Sediment Contamination Grading
Metal Grade II Index =
ECi: Measured concentration of metal i in sediment PELki: Metal I - specific Threshold Value for Grade II
Integrated Site-Based Contamination Classification

## Slide 13
Enrichment Factor (EF)
EF =
(Cx/Cref)
(Bx/Bref)
Cx: Concentration of element i in the sample Bx: Background concentration of element i Cref: Concentration of reference element in the sample Bref: Background concentration of the reference element
In the ND region, EF values for Zn, Cd, Cu, and Pb fall within the moderate to significant enrichment range (EF levels 2–3).
Zn and Cd show higher enrichment in mid- to downstream sites, Cu in the downstream area, and Pb in the midstream area.
Class | EF Value | Soil quality
1 | EF < 2 | Deficiency to minimal enrichment
2 | 2 ≤ EF < 5 | Moderate enrichment
3 | 5 ≤ EF < 20 | Significant enrichment
4 | 20 ≤ EF < 40 | Very high enrichment
5 | EF ≥ 40 | Extremely high enrichment
Sediment Contamination Assessment Using EF and Igeo

## Slide 14
Geoaccumulation Index (Igeo)
In the ND region, Igeo values for Zn, Cd, Cu, and Pb fall within Class 2–3, indicating moderate to considerable contamination.
Zn and Cd show higher Igeo values in mid- to downstream sites, Cu in the downstream area, and Pb in the midstream area.
Cn: Metal Contents in Sediments Bn: Average Background Values in Shale Cd 0.13, Cu 45, Hg 0.45, Ni 68, Pb 22, Zn 95
Class | Igeo Value | Soil quality
0 | Igeo ≤ 0 | Practically uncontaminated
1 | 0 < Igeo < 1 | Uncontaminated to moderately contaminated
2 | 1 ≤ Igeo < 2 | Moderately contaminated
3 | 2 ≤ Igeo < 3 | Moderately to heavily contaminated
4 | 3 ≤ Igeo < 4 | Heavily contaminated
5 | 4 ≤ Igeo < 5 | Heavily to extremely contaminated
6 | Igeo ≥ 5 | Extremely contaminated
Sediment Contamination Assessment Using EF and Igeo

## Slide 15
Rare earth element (REE) concentrations were normalized to CI chondrite values.
Elements are arranged from light REEs (LREEs) on the left to heavy REEs (HREEs) on the right.
Due to Korea’s predominantly granitic bedrock, REE distribution patterns appear broadly similar across samples.
Most patterns show enrichment in light REEs (left side) and depletion in heavy REEs (right side).
Distribution Pattern of Rare Earth Elements in Sediment

## Slide 16
Application of Korean Waste Leaching Procedure to Sediment Samples
Parameter | Condition
Sample Amount | 5 g of solids per 100 mL of extract
Extractant | HCl + Deionized water
Extractants pH | 5.8-6.3
Reaction | Shaking speed: 200 rpm Shaking time: 6 hours
Centrifugation | 3,000 rpm, 20 minutes
Filtration | 0.45 μm
All heavy metals were below regulatory limits, except for arsenic.
Arsenic exceeded the standard at CY-1 and CY-2.
However, the concentrations are not considered high, as the area is a former gold mining site where arsenic levels in sediments have historically reached several hundred mg/kg.
Mobility Evaluation of Heavy Metals in Sediments

## Slide 17
Potential Ecological Risk Index (PERI) for Toxic Elements
Minimal contamination was observed based on the Korean waste leaching test method.
Several samples showed potential ecological risk in the PERI assessment.
CY-1, CY-2 and HT-1, HT-2 exhibited high risk due to geogenic contamination.
All ND samples showed elevated risk levels, likely due to their urban location.
Eri = Tri
×
Ci
Cni
( )
PERI =
Mobility Evaluation of Heavy Metals in Sediments
Eri Element-specific Potential Ecological Risk Index Tri Toxic Response Factor for Each Element Ci Measured Concentration of the Element Cni Background Concentration of the Element

## Slide 18
Isotopic analysis of Cu, Pb, Zn for tracing pollution
Isotopic analysis is typically conducted using only one or two elements.
However, overlapping signatures often make it difficult to distinguish contamination sources clearly.
To improve source discrimination, isotopic ratios of Cu, Pb, and Zn will be analyzed simultaneously.
Re-analysis of Rare Earth Elements
Rare earth elements (REEs) are not fully dissolved by the standard 4-acid digestion method.
Complete dissolution often requires high-temperature fusion prior to leaching.
Re-analysis is planned using an improved method to ensure accurate REE quantification.
Jeong&Ra (2021) J. Anal. Sci. Technol., v.12, article n.39.
Further Study

## Slide 19
Comparison of Enrichment Factors Using Fe and Sc as Reference Elements

## Slide 20
Comparison of PERI Results Based on Reference vs. Site-Specific Background Values
A comparison of PERI results based on literature reference values and locally measured background concentrations revealed an almost perfect correlation (R² = 0.9987), confirming the robustness of the background assessment.

## Slide 21
Correlation Analysis Among Rare Earth Elements (REEs)

## Slide 22
Enrichment Factor

## Slide 23
Enrichment Factor