## Slide 1: Stochastic modeling of contrail formation
Roberto Paoli and Justin Rigal
Polytechnique Montreal

## Slide 2: Problem statement and motivations
Spatial simulations of contrail formation in the jet phase are computationally expensive especially when the geometry of the aircraft and the engine are considered
Classical 2-eqs RANS models are doable but RSM 6-eqs RANS models can still be challenging
RANS provide mean flow solution possibly missing unsteady effects, turbulence (dynamics, mixing, microphysics); Spatial LES are just too expensive to run routinely in sensitivity analysis
Spatial LES of passive particles (Kolomesnky & Paoli, 2018) ~700M grid-points + stats convergence
Near-field RANS initialization for temporal LES in far-filed (Bouhafid et al., 2024)
Why not trying to combine the two in some way…
Notes: Example of design studies : chevron on engine nozzle by Cantin et al.

## Slide 3: Overall objectives
Model turbulence effects on jet-regime contrail formation while maintaining computational efficiency
  Develop a hybrid Stochastic Lagrangian-Eulerian model for ice particle growth
  Demonstrate the model ability to capture key microphysical processes
  Evaluate the model ability to assess sensitivity to varying physical conditions

## Slide 4: Eulerian Finite Volume Solver – CHApel Multi-Physics Simulation
Chapel language
Cell-centered finite-volume solver
Compressible
Second order convective Roe Scheme
Weighted Least Squares gradient
Implicit Symmetric Gauss-Seidel (SGS)
Multi-node, multi-core
Species transport
Upwind with gradient based interpolation
Example of flow simulation using CHAMPS

## Slide 5: Stochastic Differential Equation – Simplified Langevin Model
Lagrangian form of velocity equation
The unknowns from Stochastic form are time dependent random processes
Langevin model replaces the fluctuating force by a Stochastic process : random perturbation/mean relaxation
Simplified Langevin Model (Pope, 2011)
Wiener process
consistency calibration
Autocorrelation function
at high Re
Kolmorogorv constant
Follow the approach proposed
for stochastic condensation of
clouds (Paoli & Shariff, 2009)

## Slide 6: Stochastic Differential Equation – SLM Calibration
Generated mean flow
The Langevin Model yield the correct Navier Stokes mean flow equation
Turbulent kinetic energy equation is used to calibrate the relaxation rate to yield the expected velocity variance
Generated turbulent kinetic energy
Homogeneous turbulence (Pope, 2011)
Stationary
Decaying

## Slide 7: Stochastic Differential Equation – SLM Calibration
The relaxation rate compatible with k- SST model was derived
Solving the model in the Eulerian framework allows for non-homogeneous turbulence
k- SST turbulent kinetic energy
Relaxation rate : Non-homogenous
Generated turbulent kinetic energy
Pressure transport is neglected as in many Reynolds transport models (Pope, 2000)
Notes: Riotta

## Slide 8: Stochastic Differential Equation – Interaction with the Mean IEM
Stochastic form of scalar transport equation
The unknown from Stochastic form is a random diffusion term
IEM model replaces the fluctuating diffusion by a relaxation to the mean
Interaction by Exchange with the Mean model (Pope, 1985)
: species mass fraction

## Slide 9: Stochastic Differential Equation – Microphysical system
Complete microphysical system
Equations for particle temperature, vapour mass fraction and ice mass evolution are added
Vapor depletion is coupled to ice growth with the initial definition of a fluid mass
Ice-Vapor Coupling
Diagram of Lagrangian particle composition
Ice mass of represented particles
Fluid mass
Temperature
Vapor mass fraction

## Slide 10: Numerical Setup – Geometry
CFM56-5B3 rear body geometry was redrawn from a scaled cut view provided by Safran
Reconstructed aerodynamic profiles of the bypass and core nozzles from the CFM56-5B3
Aerodynamic lines of a real aircraft engine, the CFM56-5B3, were reconstructed

## Slide 11: Numerical Setup – Computational Domain
The computational domain consists of a 30° sector of the exhaust geometry
237m axially; 24m radially, allowing to catch 1s at cruise speed
Buffer zones have been incorporated
Overview of the computational domain
The domain is a 30° periodic sector of 24m radially, spanning 237m downstream of the exhaust

## Slide 12: Numerical Setup – Conditions
Freestream conditions at 35,000 feet (ISA)
Turbofan boundary conditions
Freestream conditions are defined from Internation Standard Atmosphere (ISA)
Engine operation point was provided by a thermodynamic model by Safran
Engine operating point (Safran)

## Slide 13: Airflow Results – Shock And Expansions
L2 norm of density residual was reduced by 8 orders of magnitude
Total pressure loss agrees within 1% with the operating conditions provided by Safran
Mean flow contours of a) axial velocity, b) pressure, c) temperature
Both nozzle are sonic. Airflow at the engine exhaust present shock and expansion waves
Notes: SFD
Jacobian definition at boundary
Boundary condition ramping
L2 norm of density residual : 8 order of magnitude

## Slide 14: Airflow Results – Potential Cores
Normalized axial velocity profiles highlight :
Diffusion in turbulent shear layers
The primary potential core
Coaxial secondary potential core
Normalized axial velocity excess profiles at x
The potential cores establishment and diffusion are as expected
The obtained aerodynamic flow field serves as the basis for subsequent computations in this study

## Slide 15: Stochastic Trajectories
Mean velocity streamtraces
Stochastic model qualitatively produces expected dispersion and turbulent vortices
Stochastic velocity trajectories

## Slide 16: Stochastic Trajectories – Statistics
Axial velocity
The Lagrangian statistics produced by the Langevin model reproduced very accurately the inputted RANS fields
Comparison between RANS quantities and Langevin model generated statistics
Velocity variance

## Slide 17: Numerical Setup – Contrail
Average chemical formula of Jet-A1 fuel : C10.8H21.6 was considered (Xu et al., 2018)
Assuming perfect combustion, water vapor mass emission index is : EIH20,m = 1.284 kg kg-1
Safran provided extrapolated soot emission indices :
Vapor and particle emission were defined using emission indices and fuel to air ratio
In-flight exhaust composition
Freestream vapor mass fraction
EIsoot,m = 14.486 mg kg-1
EIsoot,n = 2.755 x 1014 # kg-1
Notes: Radius was derived from mass using a power law calibrated on experimental data since soot aggregates have a variable effective density (depending on the proportion of air stuck in the structure)

## Slide 18: First Results – Thermodynamic evolution
Particles effectively mix with ambient air
Microphysics behaves as expected
  Particles first reach liquid saturation
  Then they evolve to ice sat equilibrium
5s with ~25000 particles in domain was computed allowing mean fields convergence
10000 trajectories were extracted for post processing
The model behaves as expected, generating dispersion and effectively simulating microphysics
Notes: 2 order of mag for L2 of mean radius time fluctuations

## Slide 19: Alternative Models Comparison – Spatial Distributions of Particles
Langevin effectively disperse particles
Mean composition exhibit a larger, less uniform, radii distribution
Spatial distribution of particles, colored by crystal radius, cross-sectional distribution at x=220m
While Langevin model exhibit proper dispersion, it seems to overpredict radii if not associated with IEM
RANS+Langevin
RANS
Notes: SFD
Jacobian definition at boundary
Boundary condition ramping
L2 norm of density residual : 8 order of magnitude

## Slide 20: Alternative Models Comparison – Axial Evolution
Turbulence dispersion broaden the activation range
IEM model delay the last particle activation and limit ice growth
Comparison of the number of activated particles
Turbulence model effectively affect growth activation and IEM model limit ice growth by limiting mixing
Comparison of the mean particle radius
Effect of turbulent mixing
Notes: SFD
Jacobian definition at boundary
Boundary condition ramping
L2 norm of density residual : 8 order of magnitude

## Slide 21: Summary of Work
Developed a hybrid Stochastic Lagrangian–Eulerian model for contrail formation
  RANS equations for mean flow
  Time-accurate Lagrangian framework for particles
    Simplified Langevin Model for trajectories
    Interaction by Exchange with the Mean for compositions
    Microphysical model of ice growth
  Coupling between Eulerian and Lagrangian by mean depletion term
Cheap alternative to LES for parametric analysis while retaining turbulence features of the flow

## Slide 22: Limitations and Future Research
Assumption of constant particle density within computational particles
  Excessive depletion of vapor within the fluid particle
  Add particle density as an IEM composition variable to compute Lagrangian depletion term
The stochastic model presents several constraints
  Instantaneous gas density is approximated by mean density, but it can have significant fluctuations near nozzle exit where temperature gradient are high
  Future work could focus on improving the RANS-Lagrangian trajectory model
The microphysical model is simplified
  Include volatile particle and particle-chemistry interactions
  Add initial freezing phase
Include interaction with the aircraft wake

## Slide 23
Thank you!

## Slide 24: Research Framework – Regimes of evolution
Wide range of time and space scales
  Evolution classified in four distinct regimes
Classification of aircraft wake evolution into four regimes (Paoli & Shariff, 2016)
Contrail evolution study is split under four regimes
This work focuses on the Jet regime
Notes: Jet regime : first few seconds, micro, nucleation, complex aero
Vortex regime : seconds to minutes, vortices interact with jet plume, complex flow structure
Dissipation regime : minutes to hours, vortex disintegration, release of ice crystals in atmosphere, sublimation or not
Diffusion regime : hours, up to global scales, atmospheric turbulence, radiative processes, wind shear -> Cirrus

## Slide 25: Contrail Simulation Procedure
After population of the domain, coupled iterations occur until mean vapor field reach steadiness
Notes: Interpolation of quantities linearly and weighting using fraction of traj spent in cell computed during tracking

## Slide 26: Numerical Setup – Conditions
Freestream conditions at 35,000 feet (ISA)
Turbofan boundary conditions
Freestream conditions are defined from Internation Standard Atmosphere (ISA)
Engine operation point was provided by a thermodynamic model by Safran
Engine operating point (Safran)

## Slide 27: Numerical Setup – Mesh
Overview of the computational mesh
Hybrid structured/unstructured mesh was produced on Fidelity Pointwise
Diamond like axis
10-cell rotation
Wall thickness : 2µm
y+<1
7 884 125 elements
A 3D, 30° periodic, mesh was generated on Fidelity Pointwise. Freestream is unstructured. Jet plume is structured

## Slide 28: Radiative forcing from global aviation emissions. (Lee et al., 2023)

## Slide 29: Reynolds Averaged Navier Stokes – Mean Flow Equations
Momentum equation
Navier Stokes equations are solved under their Favre averaged form
Boussinesq Eddy-Viscosity requires a turbulence model to close the equations
Species transport equation
Boussinesq Eddy-Viscosity assumption (Blazek, 2001)

## Slide 30: Reynolds Averaged Navier Stokes – Turbulence model : k- SST
Versatile to treat mixed internal-external flows configurations such as nozzle-jet flows
Blends between k- near wall and k- away (Menter, 1993)
Provides necessary turbulence information for stochastic trajectories
k- SST combines k- and k- advantages and performs well for mixed flows
The model provides cell-centered k and  for later stochastic modeling
Equations (Menter, 1993)

## Slide 31: Stochastic Differential Equation – Generalized Langevin Model

## Slide 32: Ice Growth Rate
Ice crystals grow by water deposition on their surface
Rate of growth is related to pressure difference between its surface and ambient air
Corrections for Kelvin effect, collision geometry, sticking probability, and ventilation
Ice growth rate is computed from local gas properties around the particle (Jacobson, 1999)
Crystal radius
Local vapor pressure
Vapor saturation pressure over ice
Molecular diffusion coefficient
Thermal conductivity of air
Latent heat of sublimation
Local gas temperature
Vapor specific gas constant
Notes: Kelvin's curvature correction

## Slide 33: Lagrangian Implementation – Numerical Integration : Discretization

## Slide 34: Parallel Processing
Parallel data structure

## Slide 35: Verification Tests – CHAMPS Internal/External : Near-sonic jet
Axisymmetric Near-Sonic Jet case from Nasa Langley Research Center Turbulence Modeling Resource

## Slide 36: Verification Tests – CHAMPS Internal/External : Near-sonic jet
Comparison of CHAMPS and WIND (Bush et al., 1998)

## Slide 37: Particle Motion
Inertial particle velocity equation
Particles velocity in the jet regime is approximated by gas velocity
For particles with a radius lower than 1µm, the relaxation timescale is lower than 2x10-5 s.
 We consider particles to have the velocity of the carrier phase (Cantin et al., 2022; Paoli et al., 2008; Khou, 2018)
Small Reynolds value relaxation timescale
=

## Slide 38: Airflow Governing Equations – RANS/SDE Approaches Comparison
Velocity equation
RANS approach requires modeling the statistics associated with fluctuation to compute the averaged terms
SDE approach requires modeling the spatial variations of the fluctuation to compute the instantaneous terms
Scalar transport equation
Convective transport by fluctuating velocity
Effects of the spatial variation of fluctuating terms (undefined since we only solve realizations)
Fluctuation effects on source terms

## Slide 39: Airflow Governing Equations – Important notes
Focus on source term
SDE approach allows to account for non-linearities on source terms
Example of non-linear source term

## Slide 40: Airflow Governing Equations – Important notes
In this work the RANS computation provides all statistics and inputs required for the Langevin model
This allows to only compute the trajectories emanating from core nozzle
Difference with usual SDE implementations
Usual implementation
  (Cao et al., 2005; Zhou et al., 2017; Wang & Pope, 2008)
  Mean fields are derived from particles statistics
   is added as a particle property
This work
  Mean fields are provided by RANS calculation
  Turbulence statistics by RANS turbulence model
  Mean mass fractions by RANS calculation
    Particles originate only from core nozzle
Mean fields (velocity, vapor,…) ?
Mean fields (velocity, vapor,…) ?
Sketch of this work implementation of Lagrangian/Eulerian
Sketch of usual implementation of Lagrangian/Eulerian

## Slide 41: First contrail results
Numerical Setup
Alternative Models Comparison
Sensitivity Analyses

## Slide 42: First Results – Average evolution
Contrail downstream evolution, mean radius, saturation ratios
5s with ~25000 particles in domain was computed allowing mean fields convergence
10000 trajectories were extracted for post processing
Particles activation is spread out. Average crystal radius evolves smoothly, ultimately reaching a steady value
Particles activate between 25m and 75m
Mean radius evolves smoothly
At the end it slows around 500nm
Ice saturation converges to 1
Notes: 2 order of mag for L2 of mean radius time fluctuations

## Slide 43: Alternative Models Comparison – Spatial Distributions of Particles
Langevin effectively disperse particles
Mean composition exhibit a larger, less uniform, radii distribution
Spatial distribution of particles, colored by crystal radius, cross-sectional distribution at x=220m
While Langevin model exhibit proper dispersion, it seems to overpredict radii if not associated with IEM
Notes: SFD
Jacobian definition at boundary
Boundary condition ramping
L2 norm of density residual : 8 order of magnitude

## Slide 44: Sensitivity Analyses – Soot Particles Emission Rate
More particles increase total ice mass while decreasing mean particle radius
Dependence of a) contrail particle mean radius, b) total ice mass flux, on soot particle emission rate
Because vapor is shared among more particles, mean radius decreases but more total ice if formed

## Slide 45: Sensitivity Analyses – Atmospheric Relative Humidity
Atmospheric saturation increases mean bigger cristals and more total ice mass
Dependence of a) contrail particle mean radius, b) total ice mass flux, on atmospheric relative humidity
Because more vapor is available in the freestream, particles grow bigger

## Slide 46: Sensitivity Analyses – Atmospheric Temperature
Hotter atmospheric temperature induces small crystals and lower total ice mass
Dependence of a) contrail particle mean radius, b) total ice mass flux, on atmospheric temperature
Because particles final equilibrium temperature is higher, ice growth is slower

## Slide 47: Sensitivity Analyses – Cases Properties
6 additional cases were defined to study soot emission, ambient saturation and ambient temperature effects
Because the engine adapt, additional parameters varies for the temperature cases
Ssoot / Ssoot,ref | S1 80% | Ref 100% | S2 120%
RHI∞ | R1 100% | Ref 110% | R2 130%
T∞ | T1 210K | Ref 215K | T2 220K
Six cases are defined as variations from the reference
Engine operating point to ambient conditions induces variations for additional parameters for temperature cases

## Slide 48: Sensitivity Analyses – Side-by-Side Comparison
The jet regime is most sensible to ambient temperature
Soot particle number have a non-neglectable impact on crystal radius
Mean radius
Total ice mass

## Slide 49: Alternative Models Comparison – Thermodynamic evolutions
Intermediate model underestimate local vapor depletion
Scatter plot of particles in the thermodynamic diagram, left : mean velocity, center :, right : stochastic model
Vapor depletion equilibrium is not achieved by the turbulent velocity model if not associated with IEM
Notes: SFD
Jacobian definition at boundary
Boundary condition ramping
L2 norm of density residual : 8 order of magnitude

## Slide 50: Stochastic Trajectories – C0 Reynolds Dependence
Contour plot of C0

## Slide 51: Proposed Multi-Phase Framework
Workflow of the proposed contrail model
RANS precomputation provides mean flow fields to the coupled section of the model
Coupled section : Lagrangian and Eulerian solvers interact through statistics computation and interpolation

## Slide 52: Coupling – Lagrangian/Eulerian
The mean vapor depletion term is computed from particles
  Opposite of total ice mass captured in the cell
  Divided by the time of the simulation and the cell volume
Residence time is computed while tracking
Example of residence time computing
Mean vapor transport is coupled with Lagrangian vapor transport by computation of the average depletion term
Notes: Interpolation of quantities linearly and weighting using fraction of traj spent in cell computed during tracking

## Slide 53: Sensitivity Analyses – Cases Properties – Additional parameters