## Slide 1: Enhancing PPP Performance with Multi-GNSS Satellite Products and Integer Ambiguity Resolution
marcus.glaner@geo.tuwien.ac.at
Marcus Franz Wareyka-Glaner1, Gregor Möller1
1 Department of Geodesy and Geoinformation, Technische Universität Wien, Austria
29 April 2025

## Slide 2: Precise Point Positioning
PPP requires precise satellite products and complex models and algorithms
position accuracy: cm, or even mm
major drawback: convergence time
satellite products
Wareyka-Glaner, 29/04/2025
PPP with integer ambiguity resolution → PPP-AR

## Slide 3: improve PPP
multi-GNSS
multi-frequency
integer ambiguity fixing
accurate error models
innovative PPP models
modern satellite products
Wareyka-Glaner, 29/04/2025

## Slide 4: Satellite products
Analysis Center |  | GNSS | Source
COD | Center of Orbit Determination Europe | GRECJ | ftp.aiub.unibe.ch/CODE_MGEX/CODE
GRG | Centre National d’Études Spatiales | GREC | https://cddis.nasa.gov/archive/gnss/products/
HUS | Huazhong University of Science and Technology | GREC | ftp://ggda.ac.cn/pub/mgex/products/
WUM | Wuhan University | GRECJ | https://cddis.nasa.gov/archive/gnss/products/
WMC | Combined product | GRECJ | ftp://igs.gnsswhu.cn/pub/whu/phasebias/
G…GPS R…GLONASS E…Galileo C…BeiDou J…QZSS
Wareyka-Glaner, 29/04/2025
operational final MGEX products
with phase biases
latency: ∼ 9 days

## Slide 5: Test case
Software | (https://github.com/TUW-VieVS/raPPPid)
Data | 21 IGS MGEX stations, January 1, 2025
Observations | GPS: L1+L2, GLONASS: G1+G2, Galileo: E1+E5a 30 sec interval, reset of solution: every 20 min
Satellite products | COD or GRG or HUS or WUM or combined product
Wareyka-Glaner, 29/04/2025

## Slide 6
Software raPPPid (VieVS PPP) [Glaner & Weber, 2023]
Data 21 globally distributed IGS MGEX stations (January 1, 2025)
Observations GPS: L1+L2, GLONASS: G1+G2, Galileo: E1+E5a
Observation ranking GPS: WCLQ, GLONASS: PCQX, Galileo: CQX
Observation interval 30 sec, reset of solution: every 20 min
Processing mode Post-processing, ionosphere-free LC, static
Raw observation noise Code 30cm, phase 2mm
Observation weighting Elevation weighted, sin²(elev), cutoff angle 5°
Correction models Phase Wind-Up, solid Earth tides, relativistic effects, PCO + PCV, ocean loading
Troposphere model VMF3 + GRAD, residual zenith wet delay is estimated, process noise 5mm /√h
Adjustment Filter (float solution) and Least-Squares-Adjustment (fixed solution)
Float ambiguities Constant, zero-difference, cycle-slip detection: dL1-dL2
PPP-AR Fixing cutoff 10°, reference satellite = highest satellite, fixing start after 120s
Fixing WL with HMW LC of the last 5minutes, NL with LAMBDA 4.0
Orbits, Clocks, Biases COD or GRG or HUS or WUM or combined product
Satellite attitude From ORBEX
Wareyka-Glaner, 29/04/2025

## Slide 7: Results
fixed position | COD | GRG | HUS | WUM | WMC
Ø TTCF [min] | 3.56 | 3.66 | 3.28 (*) | 4.17 | 4.40
median 2D error [cm] | 0.90 | 0.92 | 0.78 (*) | 1.46 | 0.90
Ø 3D error after 20 min [cm] | 3.28 | 3.50 | 3.25 (*) | 3.91 | 3.54
TTCF is achieved when 2D < 5 cm for the complete remaining period
TTCF … time to correct fix
(*) only stations tracking Galileo CQ-signals (no X code biases)

## Slide 8: Results
fixed position | COD | GRG | HUS | WUM | WMC
Ø TTCF [min] | 3.24 | 3.28 | 3.28 | 3.76 | 3.96
median 2D error [cm] | 0.84 | 0.84 | 0.78 | 1.40 | 0.85
Ø 3D error after 20 min [cm] | 3.19 | 3.56 | 3.25 | 3.87 | 3.45
TTCF is achieved when 2D < 5 cm for the complete remaining period
TTCF … time to correct fix
stations tracking Galileo CQ-signals

## Slide 9: Ø TTCF / station
TTCF is achieved when 2D < 5 cm for the complete remaining period
TTCF … time to correct fix
Wareyka-Glaner, 29/04/2025
… station tracks Galileo X signals

## Slide 10: 3+ Frequencies
all tested products enable PPP-AR with IF LC
only WUM allows multi-frequency fixing
for example: Decoupled Clock Model 1
WUM MGEX rapid, GrEC, 3 frequencies
UNB3 2024/001, fixed UTM
1 Naciri & Bisnath, 2021
→ improves convergence
Wareyka-Glaner, 29/04/2025

## Slide 11: igs20.atx
PCO/PCVs of some satellites changed in week 2345
backward compatibility is lost, for example:
  satellite products were generated with old values
  PPP user applies latest igs20.atx file
igs20_2356.atx, https://files.igs.org/pub/station/general/
AREG, GRG products
correct igs20.atx
latest igs20.atx

## Slide 12: Summary
several high-quality satellite products
only WUM endorses 3+ frequencies
rapid ∼ final products
igs20.atx: ”valid from” / “valid to” tags?

## Slide 13: References
Naciri, N., & Bisnath, S. (2021). An uncombined triple-frequency user implementation of the decoupled clock model for PPP-AR. Journal of Geodesy, 95(5), 60. https://doi.org/10.1007/s00190-021-01510-y
Glaner, M. F., & Weber, R. (2023). An open-source software package for Precise Point Positioning: raPPPid. GPS Solutions, 27(4), 174. https://doi.org/10.1007/s10291-023-01488-4

## Slide 14: Thank you for your attention!
© Thomas Fabian (flickr)

## Slide 15: Supplementary

## Slide 16: raPPPid
open-source PPP software
GitHub: https://github.com/TUW-VieVS/raPPPid
Documentation: https://vievswiki.geo.tuwien.ac.at/en/raPPPid
Wareyka-Glaner, 29/04/2025

## Slide 17: Results
2D, 95% Quantile
3D, 95% Quantile
HUS: only stations tracking Galileo CQ-signals (no X code biases)

## Slide 18: 2D error / station
Wareyka-Glaner, 29/04/2025
… station tracking Galileo X signals

## Slide 19: Results: ZTD

## Slide 20: CODr vs CODf (GrE)
fixed results | rapid | final
Ø TTCF [min] | 3.52 | 3.56
median 2D error [cm] | 0.89 | 0.90
Ø 3D error after 20 min [cm] | 3.30 | 3.28
TTCF is achieved when 2D < 5 cm for the complete remaining period
TTCF … time to correct fix
float
float
fixed
fixed

## Slide 21: Results: GrEC
fixed position | COD | GRG | HUS | WUM | WMC
Ø TTCF [min] | 3.54 | 3.92 | 3.34 (*) | 4.65 | 4.47
median 2D error [cm] | 0.90 | 0.92 | 0.78 (*) | 1.51 | 0.91
Ø 3D error after 20 min [cm] | 3.21 | 3.52 | 3.22 (*) | 4.14 | 3.53
TTCF is achieved when 2D < 5 cm for the complete remaining period
TTCF … time to correct fix
(*) only stations tracking Galileo CQ-signals (no X code biases)

## Slide 22: Results: GrEC
Ø TTCF
2D error

## Slide 23: Another Day (032/2025)
fixed position | COD | GRG | HUS | WUM | WMC
Ø TTCF [min] | 3.66 | 3.66 | 3.61 (*) | 4.23 | 4.55
median 2D error [cm] | 0.90 | 0.89 | 0.80 (*) | 1.13 | 0.88
Ø 3D error after 20 min [cm] | 4.00 | 3.78 | 3.34 (*) | 4.32 | 3.88
TTCF is achieved when 2D < 5 cm for the complete remaining period
TTCF … time to correct fix
(*) only stations tracking Galileo CQ-signals (no X code biases)

## Slide 24: Another Day (032/2025)
fixed position | COD | GRG | HUS | WUM | WMC
Ø TTCF [min] | 3.29 | 3.34 | 3.61 | 3.90 | 4.31
median 2D error [cm] | 0.82 | 0.81 | 0.80 | 1.05 | 0.82
Ø 3D error after 20 min [cm] | 3.72 | 3.35 | 3.34 | 3.87 | 3.40
TTCF is achieved when 2D < 5 cm for the complete remaining period
TTCF … time to correct fix
only stations tracking Galileo CQ-signals