## Slide 1
1 Agroscope Reckenholz, Water Protection and Substance Flows , Zürich, Switzerland
2 Oeschger Centre for Climate Change Research , University of Bern, Switzerland
3 Institute of Geography, University of Bern, Switzerland
4 Hydrosystem modeling, UFZ Helmholtz-Centre for Environmental Research Leipzig, Germany
From Field to Catchment: Evaluating the Hydrological Effects of Soil Organic Carbon Increases
, , ,
PICO
A.13
Expectation: Impact on states, fluxes, discharge and water balance
Assumption: Management adaptation leads to change in soil hydraulic properties
Soil organic carbon
Bulk density
Sat. hydraulic conductivity
Plant available water
Notes: Agricultural management can be adapted to increase resilience towards the increasing droughts, organic amendment, cover cropping or conservational tillage can lead to changes in soil hydraulic properties that can increase water retention to make more water longer available for crops. Given that such measures would be taken up on a large scale, we wanted to investigate the impacts on catchment scale hydrological processes.

## Slide 2
Results: Impacts on states, fluxes, discharge and water balance:
PICO
A.13
Assumption: Management adaptation leads to change in soil hydraulic properties
Actual evapotranspiration
Soil water content
Groundwater storage
Total runoff & discharge
Peak flows
Low flows
Soil organic carbon
Bulk density
Sat. hydraulic conductivity
Plant available water
1 Agroscope Reckenholz, Water Protection and Substance Flows , Zürich, Switzerland
2 Oeschger Centre for Climate Change Research , University of Bern, Switzerland
3 Institute of Geography, University of Bern, Switzerland
4 Hydrosystem modeling, UFZ Helmholtz-Centre for Environmental Research Leipzig, Germany
From Field to Catchment: Evaluating the Hydrological Effects of Soil Organic Carbon Increases
, , ,
Notes: We therefore implemented the changes in the mesoscale hydrologic model and first results indicate, that water retention is increased, also actual Evapotranspiration is, and that percolation, groundwater recharge and overall total runoff are decreased, leading to a generally mildly decreased discharge aner therefore affected peak and low flows. Please come to Pico spot A13 to discuss further.

## Slide 3
Context
Increasing duration and magnitude of agricultural and hydrological droughts
Declining yields and reduced irrigation possibilities
Management measures increasing soil organic carbon (SOC) can
enhance soil water retention
@Agroscope
@FOEN
How would a large scale implementation of such measures affect hydrological processes at catchment scale ?

## Slide 4
Broye catchment: lowland, mid-sized (~600) with large share of agricultural use (~70%)
Case study and model
Mesoscale hydrological model mHM (Samaniego et al. 2010)
Open-source, process-based distributed, rainfall-runoff model.
Arbogne Avenches
Petit Glane
Broye Payerne
Flon Aval
1482m
429m
pervious
impervious
forest
KGE: 0.87 NSE: 0.84 pbias: -6.1
gauging station

## Slide 5
+ 0.65 to 1 % mass Soil organic carbon SOC or increase by 7 to 220%
(Haruna et al. 2020, Hao et la. 2023, Blanco-Canqui et al 2009 , Blanco-Canqui et al 2023 & Shi et al. 2016)
10 to 20 % decrease in bulk density BD
(Haruna et al. 2020, Veetil et al. 2024, Hao et al. 2023, Blanco-Canqui et al 2009 , Blanco-Canqui et al 2023 & Shi et al. 2016)
40 to 360 % increase in saturated hydraulic conductivity Ksat
(Rawls et al. 2004, Haruna et al. 2020, Veetil et al. 2024, Hao et al. 2023, Blanco-Canqui et al 2009 , Blanco-Canqui et al 2023)
4 to 65 % increase in plant available water PAW
(Haruna et al. 2020, Hao et al. 2023, Blanco-Canqui et al 2009 , Blanco-Canqui et al 2023 & Shi et al. 2016)
Literature review: management
Management adaptations such as cover crops or organic amendments can lead to changes in soil hydraulic properties:

## Slide 6
Management scenario run: +1% SOC (mass) for all pervious landcover cells
Implementation of management in the model (mHM)
SOC
BD
PTF: Manrique & Jones 1991
Required input for each cell: soil texture and bulk density
„pervious“ landcover cells (e.g. cropland)
Δ SOC
Δ BD
PTF: Manrique & Jones 1991
Default model run (no management)

## Slide 7
Impact of +1% SOC (mass) on key parameters:
Implementation of management in the model (mHM)
Δ SOC
Δ BD
PTF: Manrique & Jones 1991
PTF: Vereecken et al. 1990
Sand
Clay
Δ SOC
Δ BD
(cm/day)
BD (g/)
simulated (scenario)
simulated (default)
simulated (scenario)
simulated (default)
~
-10%
~
+115%
 Magnitude of changes is consistent with reported changes from literature
PAW (%)
+5%
~
simulated (default)
simulated (scenario)
Assuming an inital range of 0-5% SOC for an example soil (loam)

## Slide 8
Impact on states and fluxes
% difference in states and fluxes of
management scenario run relative to default run
( positive: increased under management)
Seasonal pattern, larger effect in summer
increased aET
higher soil water content
lower groundwater storage
decreased total runoff
actual ET
Soil water content (0-30cm)
Soil water storage total
Groundwater storage
Total runoff (interflow + baseflow)
Average temperature (°C)
Precipitation (mm)
(weekly aggregation for example cropland cell)
Notes: Overall: seasonal differences: in winter soils are anyway more saturated and there is less ET, less room for differences.
Increased water content at layer 1= wegen soil conditions. Overall soil water storage: eher increased, aber auch limited wegen aET, im winter teilweise decreased: higher ksat : more percolation = infiltration from last layer ? Overall groundwater is reduced, but in summer the difference is almost 0, because there is a bit more percolation

## Slide 9
Impact on discharge
Overall slightly reduced
Seasonal pattern: biggest impact in winter
Peak flows are reduced
Arbogne Avenches
Petit Glane
Broye Payerne
Flon Aval
% difference of simulated scenario relative to default scenario
simulated (default)
simulated (scenario)

## Slide 10
Impact on peak and low flows
Low flows
Peak flows
Days with flow < percentile are mostly increasing under the management scenario
Yearly and peak flows are mostly reduced under management scenario
observed
simulated (default)
simulated (scenario)
Petit Glane 2019
Broye Payerne 2022

## Slide 11
Impact on water balance:
Absolute impacts are in general quite marginal, water partitioning is changed:
aET is increased
discharge is reduced
simulated (scenario)
simulated (default)

## Slide 12
Summary & Conclusion
Actual evapotranspiration
Soil water content
Groundwater storage
Total runoff & discharge
Peak flows
Low flows
Soil organic carbon
Bulk density
Sat. hydraulic conductivity
Plant available water
Results: Impacts on states, fluxes, discharge and water balance:
Assumption: Management adaptation leads to change in soil hydraulic properties
Overall: rather minor impacts although assumption is optimistic
Positive side effect: reduced peak flows
Tradeoff: even more low flows in water scarce summer month