## Slide 1: Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
Mohammad Rajabi1, Mohsen Hajibabaei1 and Robert Sitzenfrei1*
1Department of Infrastructure Engineering, University of Innsbruck, Innsbruck, Austria

## Slide 2
Application of the proposed graph-based urban drainage network model
Optimization of flood mitigation projects by calculating objective functions in different scenarios, such as:
  LID (Low Impact Development) placement
  Network design
  Network Rehabilitation
Calculation of reward values in reinforcement learning methods
Global resilience analysis
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
1
3
Results
2
Application
Flow routing

## Slide 3
2
1
3
4
5
Subcatchment 1
Subcatchment 4
Subcatchment 3
Subcatchment 2
Subcatchment 5
Hydrologic Model
Nonlinear Reservoir Model
Hydraulic Model
Hydrodynamic Model
Physics-Informed Graph Network
Legend
Inlet
Outlet
Conduit
Flow routing in urban drainage network
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
1
3
Results
2
Application
Flow routing

## Slide 4
Flow routing in urban drainage network
Legend
Inlet
Outlet
Flow
Conduit
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
1
3
Results
2
Application
Flow routing
0.7
Q (m³/s)
t (s)
0.5
Q (m³/s)
t (s)
2
3
1
4
5
Max flow1
Max flow3
Max flow4
Max flow5
Max flow2
0.5
Q (m³/s)
0.5
Q (m³/s)
0.5
Q (m³/s)
2
3
1
4
5
Max flow3
Max flow4
Max flow5
Max flow2
Max flow2

## Slide 5
Results
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
Maximum Flow of Pipes Based on the SWMM and graph-based model
Q (
Q (
1
3
Results
2
Application
Flow routing

## Slide 6
Contact
Mohammad Rajabi
PICOA.12 University of Innsbruck, Austria E-Mail: Mohammad.Rajabi@uibk.ac.at
Acknowledgments
This research is part of the ‘RESTORE’ project and is funded by the Austrian Science Fund (FWF) P 36737-N.

## Slide 7
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
Mohammad Rajabi1, Mohsen Hajibabaei1 and Robert Sitzenfrei1*
1Department of Infrastructure Engineering, University of Innsbruck, Innsbruck, Austria

## Slide 8
1
3
Application
2
Research gaps
Research gaps
Research aims
Paper | Failure | Model | Research aim
(Mugume and Butler, 2017) | Global functional failures | SWMM | Resilience assessment
(Li and Burian, 2023) | Functional failure | SWMM | Real-time flood control
(Haghbin and Mahjouri, 2023) | Functional failure | SWMM | Resilience enhancement with LID location
(Xu et al. 2024) | Global functional failures | SWMM | Resilience assessment
(Zhang et al., 2025) | Functional failures | SWMM | Resilience enhancement with LID location
(Mugume et al., 2015) | Global structural failures | SWMM | Resilience assessment
(Osheen et al., 2023) | Structural and functional failures | SWMM | Resilience assessment
(Dastgir et al., 2023) | Structural failures | Graph-based method | Critical pipe analysis
(Valizadeh et al., 2023) | Structural failures | Graph-based method | Resilience assessment
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria

## Slide 9
Paper | Failure | Model | Research aim
(Mugume and Butler, 2017) | Global functional failures | SWMM | Resilience assessment
(Li and Burian, 2023) | Functional failure | SWMM | Real-time flood control
(Haghbin and Mahjouri, 2023) | Functional failure | SWMM | Resilience enhancement with LID location
(Xu et al. 2024) | Global functional failures | SWMM | Resilience assessment
(Zhang et al., 2025) | Functional failures | SWMM | Resilience enhancement with LID location
(Mugume et al., 2015) | Global structural failures | SWMM | Resilience assessment
(Osheen et al., 2023) | Structural and functional failures | SWMM | Resilience assessment
(Dastgir et al., 2023) | Structural failures | Graph-based method | Critical pipe analysis
(Valizadeh et al., 2023) | Structural failures | Graph-based method | Resilience assessment
Current paper | Functional and structural | Graph-based method | Resilience assessment
Research gaps
1
3
Application
2
Research gaps
Research aims
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria

## Slide 10
A novel physics-informed graph theory model for flow routing under normal and failure conditions is developed and validated using the Storm Water Management Model (SWMM).
Hydraulically informed graph metrics are developed using weighted shortest path results to enhance the accuracy of flow estimation.
Research aims
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
1
3
Application
2
Research gaps
Research aims

## Slide 11
Application of the proposed graph-based urban drainage network model
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
1
3
Application
2
Research gaps
Research aims
Optimization of flood mitigation projects by calculating objective functions in different scenarios, such as:
  LID (Low Impact Development) placement
  Network design
  Network Rehabilitation
Calculation of reward values in reinforcement learning methods
Global resilience analysis

## Slide 12
2
1
3
4
5
Subcatchment 1
Subcatchment 4
Subcatchment 3
Subcatchment 2
Subcatchment 5
Legend
Inlet
Outlet
Conduit
Graph-based Model of Urban Drainage Network
4
6
Results
5
Graph analysis
Case study
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria

## Slide 13
1
4
2
3
Capacity: 0.4m³/s
Travel Time: 2.5 min
Capacity: 0.4m³/s
Travel Time: 2 min
Capacity: 0.2m³/s
Travel Time: 1 min
Capacity: 0.6m³/s
Travel Time: 1.5 min
Capacity: 1 m³/s
Travel Time: 2 min
5
Graph-based Model of Urban Drainage Network
Legend
Inlet
Outlet
Conduite
4
6
Results
5
Graph analysis
Case study
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria

## Slide 14
Graph-based Model of Urban Drainage Network
4
2
3
5
0.5
Q (m³/s)
t (s)
0.7
Q (m³/s)
t (s)
0.5
Q (m³/s)
t (s)
0.3
Q (m³/s)
t (s)
0.8
Q (m³/s)
t (s)
1
Legend
Inlet
Outlet
Conduite
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 15
Graph-based Model of Urban Drainage Network
Legend
Inlet
Outlet
Flow
Runoff edge betweenness centrality (REBC): inflows from upstream nodes that accumulated because they go through the same edge
2
3
1
4
5
Max flow1
Max flow3
Max flow4
Max flow5
Max flow2
Conduite
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 16
4
2
3
5
1
REBC: 0.5 m³/s
REBC: 0.5 m³/s
REBC: 2 m³/s
REBC: 0.3 m³/s
REBC: 2.8 m³/s
Legend
Inlet
Outlet
Conduit
Graph-based Model of Urban Drainage Network
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 17
Legend
Inlet
Outlet
Conduit
4
2
3
5
1
REBC*: 0.4 m³/s
REBC*: 0.5 m³/s
REBC*: 1.9 m³/s
REBC*: 0.3 m³/s
REBC*: 2.8 m³/s
0.1 m³/s
2
4
5
Graph-based Model of Urban Drainage Network
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study
4
2
3
5
1
REBC: 0.5 m³/s
REBC: 0.5 m³/s
REBC: 2 m³/s
REBC: 0.3 m³/s
REBC: 2.8 m³/s
Capacity: 0.4m³/s
Travel Time: 2.5 min
Capacity: 0.4m³/s
Travel Time: 2 min
Capacity: 0.2m³/s
Travel Time: 1 min
Capacity: 0.6m³/s
Travel Time: 1.5 min
Capacity: 1 m³/s
Travel Time: 2 min

## Slide 18
Graph-based Model of Urban Drainage Network
4
2
3
5
1
REBC*: 0.4 m³/s
REBC*: 0.4 m³/s
REBC*: 1.8 m³/s
REBC*: 0.3 m³/s
REBC*: 2.8 m³/s
0.1 m³/s
1
4
5
0.1 m³/s
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study
4
2
3
5
1
REBC*: 0.4 m³/s
REBC*: 0.5 m³/s
REBC*: 1.9 m³/s
REBC*: 0.3 m³/s
REBC*: 2.8 m³/s
0.1 m³/s
2
4
5
Capacity: 0.4m³/s
Travel Time: 2.5 min
Capacity: 0.4m³/s
Travel Time: 2 min
Capacity: 0.2m³/s
Travel Time: 1 min
Capacity: 0.6m³/s
Travel Time: 1.5 min
Capacity: 1 m³/s
Travel Time: 2 min
Legend
Inlet
Outlet
Conduit

## Slide 19
4
2
3
5
1
REBC*: 0.4 m³/s
REBC*: 0.4 m³/s
REBC*: 0.6 m³/s
REBC*: 0.2 m³/s
REBC*: 1 m³/s
0.1 m³/s
1
4
5
0.1 m³/s
2
3
0.1 m³/s
0.6 m³/s
0.1 m³/s
Graph-based Model of Urban Drainage Network
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study
Notes: Model-Based → Simulates water network behavior and compares with real sensor data to find leaks.

## Slide 20
Case Studies
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 21
Case Studies
Maximum flow of the pipes for the case study (a) with the damping effect (FSMI=0.2* Rainfall duration)
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 22
Case Studies
Maximum flow of the pipes for the case study (a) with the damping effect (FSMI=0.2* Rainfall duration)
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 23
Case Studies
Maximum flow of the pipes for the case study (a) with the damping effect (FSMI=0.2* Rainfall duration)
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 24
Case Studies
Maximum flow of the pipes for the case study (a) with the damping effect (FSMI=0.2* Rainfall duration)
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 25
Case Studies
Maximum flow of the pipes for the case study (a) with the damping effect (FSMI=0.2* Rainfall duration)
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 26
Case Studies
Maximum flow of the pipes for the case study (a) with the damping effect (FSMI=0.2* Rainfall duration)
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 27
Case Studies
Maximum flow of the pipes for the case study (a) with the damping effect (FSMI=0.2* Rainfall duration)
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 28
Case Studies
Maximum flow of the pipes for the case study (a) with the damping effect (FSMI=0.2* Rainfall duration)
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 29
Case Studies
Maximum flow of the pipes for the case study (a) with the damping effect (FSMI=0.2* Rainfall duration)
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 30
Case Studies
Maximum flow of the pipes for the case study (a) with the damping effect (FSMI=0.2* Rainfall duration)
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 31
Case Studies
Heat map of values for pipe flow in real-world case studies (FSMI=0.2*duration)
Case study (c)
Case study (b)
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 32
Case Studies
Heat map of values for pipe flow in real-world case studies (FSMI=∞)
Case study (c)
Case study (b)
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 33
Case Studies
Heat map of values for pipe flow in real-world case studies (FSMI=0)
Case study (c)
Case study (b)
Urban Drainage Network Modeling Based on Physics-Informed Graph Analysis
EGU General Assembly, May 2025, Vienna, Austria
4
6
Results
5
Graph analysis
Case study

## Slide 34
Contact
Mohammad Rajabi
PICOA.12 University of Innsbruck, Austria E-Mail: Mohammad.Rajabi@uibk.ac.at
Acknowledgments
This research is part of the ‘RESTORE’ project and is funded by the Austrian Science Fund (FWF) P 36737-N.