## Slide 1
Adsorption Dynamics of Atrazine on realistic Polystyrene Nanoplastics: Insights into Co-Contamination Risks
Thasleema k1, Seetha Narayanan2 and Sudha Goel1
1Department of Civil Engineering, Indian Institute of Technology Kharagpur, West Bengal–721302, India
2Department of Civil Engineering, Indian Institute of Technology Hyderabad, Telengana- 502284, India
Background and Motivation
Environmental Concern: Fragmented plastics like micro- and nanoplastics are increasingly detected in water, soil, and even the human body, posing serious health and ecological risks.
Most studies use idealised, spherical plastic beads; this study uses realistic polystyrene nanoplastics to better understand atrazine adsorption.
Materials and Methods
Source of Polystyrene: Single-use Polystyrene (PS) bowls and plates were sourced from local markets. These items, commonly discarded after one-time use, were selected to simulate environmentally realistic PS nanoplastics (PSNPs)
Material Confirmation: The plastic type was confirmed as Polystyrene using Fourier Transform Infrared Spectroscopy (FTIR) analysis.
Particle Size Analysis: The lab produced suspension showed consistent particle sizes below 1 µm, with good colloidal stability.
Results and Discussion
Conclusions
References
.
Objective
Effect of Salinity
To investigate the adsorption behavior of atrazine on realistic, irregularly shaped polystyrene nanoplastics (PSNPs) under environmentally relevant conditions.
Acknowledgements
Thasleema k is thankful to her close friends, supervisors , and Ministry of Education, Govt. of India for providing Doctoral Fellowship.
Atrazine shows significant adsorption onto PS nanoparticles (PSNPs), with maximum adsorption capacity observed at an initial concentration of 2 mg/L, beyond which saturation occurs.
Higher PSNP concentrations (244–266 mg/L) increased the overall adsorption efficiency of atrazine, especially over a 24-hour contact period, highlighting the importance of adsorbent dose in pesticide removal.
Contact time significantly affects adsorption, with equilibrium reached around 24 hours, showing gradual stabilization of atrazine concentration in the solution.
Salinity negatively impacts atrazine adsorption, indicating competitive interactions between salt ions and atrazine molecules for binding sites on PSNPs.
These results suggest that PSNPs can act as carriers or sinks for hydrophobic pesticides like atrazine, potentially affecting their fate and transport in aquatic environments
Schwaferts, C., Niessner, R., Elsner, M., & Ivleva, N. P. (2019). Methods for the analysis of submicrometer- and nanoplastic particles in the environment. TrAC Trends in Analytical Chemistry, 112, 52–65. https://doi.org/10.1016/J.TRAC.2018.12.014
Wang, L., Wu, W.-M., Bolan, N. S., Tsang, D. C. W., Li, Y., Qin, M., & Hou, D. (2020). Environmental fate, toxicity and risk management strategies of nanoplastics in the environment: Current status and future perspectives. https://doi.org/10.1016/j.jhazmat.2020.123415
Distribution of micro/nano plastic shapes (spherical vs. non-spherical) used in adsorption and transport experiments.
PS Bowls
Effect of initial concentration of atrazine
Chart: Adsorption of atrazine by 244mg/L PSNP suspension
| 0.4 | 0.8 | 1 | 2 | 3 | 4 | 5 | 6
244mg/L-0hr | 0.0081967 | 0.3878 | 0.3995 | 2.5105 | 4.6867 | 6.3611 | 8.281 | 10.5745
244mg/L-24hr | 0.54684 | 1.4065 | 1.6506 | 3.9136 | 5.7661 | 7.5601 | 9.6906 | 11.7864
Chart: Adsorption of atrazine by 250mg/L PSNP suspension
| 0.4 | 0.8 | 1 | 2 | 3 | 4 | 5 | 6
250mg/L-0hr | 0.2327 | 0.89997 | 1.0089 | 3.171 | 5.0639 | 7.0394 | 8.803 | 10.946
250mg/L-24hr | 0.54856 | 1.4151 | 1.6809 | 3.8388 | 5.596 | 7.6627 | 9.4559 | 11.7007
Chart: Adsorption of atrazine by 266mg/L PSNP suspension
| 0.4 | 0.8 | 1 | 2 | 3 | 4 | 5 | 6
266mg/L-0hr | 0.47173 | 1.1706 | 1.3825 | 3.4524 | 5.1199 | 6.7654 | 8.6859 | 10.5048
266mg/L-24hr | 0.55143 | 1.3658 | 1.6196 | 3.6118 | 5.3889 | 7.134 | 8.915 | 10.7877
Effect of Adsorbent dose
Chart: At the beginning of adsorption study
| 0.4 | 0.8 | 1 | 2 | 3 | 4 | 5 | 6
244mg/L-0hr | 0.995 | 0.88172 | 0.90252 | 0.69372 | 0.61882 | 0.61197 | 0.59589 | 0.56997
250mg/L-0hr | 0.85456 | 0.71876 | 0.74777 | 0.60362 | 0.57801 | 0.56004 | 0.55985 | 0.54392
266mg/L-0hr | 0.6863 | 0.61078 | 0.63224 | 0.54082 | 0.54604 | 0.5501 | 0.53791 | 0.53429
Chart: At the enD of adsoRption study(24hr
| 0.4 | 0.8 | 1 | 2 | 3 | 4 | 5 | 6
244mg/L-24hr | 0.66642 | 0.57103 | 0.59726 | 0.52254 | 0.53102 | 0.53884 | 0.5271 | 0.52069
250mg/L-24hr | 0.65715 | 0.55778 | 0.57978 | 0.52016 | 0.53367 | 0.52108 | 0.5272 | 0.51247
266mg/L-24hr | 0.6333 | 0.54586 | 0.56918 | 0.51963 | 0.52219 | 0.52559 | 0.52572 | 0.52175
Effect of contact Time
Chart: Time(Hour)
| 0 | 0.5 | 1 | 3 | 5 | 8 | 12 | 18 | 24
266mg/L | 1 | 0.66502 | 0.65514 | 0.64987 | 0.64526 | 0.63867 | 0.63834 | 0.62385 | 0.62055
244mg/L | 1 | 0.92193 | 0.92193 | 0.90588 | 0.8984 | 0.8861 | 0.86364 | 0.8631 | 0.85615
Chart: Adsorption Efficiency
| 0.4 | 0.8 | 2 | 3 | 4 | 5 | 6
244mg/L | 33.3575 | 42.8968 | 47.7459 | 46.898 | 46.1163 | 47.2902 | 47.9314
250mg/L | 34.285 | 44.2217 | 47.9844 | 46.633 | 47.8917 | 47.2796 | 48.7529
266mg/L | 36.6698 | 45.4141 | 48.0374 | 47.7813 | 47.4412 | 47.428 | 47.8254
Chart: 
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35
244mg/L | 0.6333 | 0.36902 | 0.29752 | 0.15421 | 0.083773 | 0.076031 | 0.062376 | 0.050963
Chart: 
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35
266mg/L | 0.65718 | 0.38903 | 0.32261 | 0.15734 | 0.087899 | 0.080115 | 0.062904 | 0.053245
Chart: 
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35
250mg/L | 0.63861 | 0.40161 | 0.31601 | 0.059571 | 0.088889 | 0.077558 | 0.063993 | 0.054125
Chart: Number of Reserach papers
| PS | PP | PMMA | PET | PVC | PA | PLA | PTFE | PBAT
Spherical | 40 | 6 | 0 | 2 | 1 | 1 | 1 | 1 | 0
Non-Spherical | 4 | 6 | 4 | 3 | 4 | 0 | 0 | 1 | 1
Chart: 
| PS | PP | PMMA | PET | PVC | PA | PLA | PTFE | PBAT
 | 42 | 9 | 3 | 3 | 2 | 1 | 1 | 1 | 1
A chart representing different types
of plastics used for adsorption/transport studies
Polystyrene (PS)
Polypropylene (PP)
Polyethylene Terephthalate (PET)
Polyamide (PA)
Polylactic Acid (PLA)
Polyvinyl Chloride (PVC)
Polytetrafluoroethylene (PTFE)
Polymethyl Methacrylate (PMMA)