## Slide 1: Development and Validation of a GIS-Based Tool for Disinfection Byproduct Formation Prediction in Water Distribution Systems
Stelios Vrachimis, Senior Research Associate
Pavlos Pavlou, Research Engineer II
Marios Kyriakou, Research Software Engineer II
Demetrios Eliades, Research Assistant Professor
KIOS Research and Innovation Center of Excellence University of Cyprus
Session HS1.1.4, EGU2025
Thursday, 01 May, 10:05–10:15 (CEST) Room 2.15
https://doi.org/10.5194/egusphere-egu25-19192

## Slide 2: Overview of presentation
The challenge of disinfection by-products
Towards a DBP modelling tool
Demonstration
Conclusions & Discussion

## Slide 3: Disinfection By-Products
Disinfection for public health is linked with the unintended formation of >700 disinfection by-products.
Several DBPs (THMs, HAAs, …) are regulated, due to association with carcinogenic and mutagenic risks.
DBP concentrations fluctuate spatiotemporally inside Drinking Water Distribution Networks (DWDNs).
Real-time assessment is limited by expensive, sparse sensing.
Few sensors measure DBP directly, surrogate sensors can have uncertainties.
Background & Motivation

## Slide 4: Modelling DBP Formation
Complex reaction dynamics
Dependence on hydraulics, water age, temperature, pH, NOM, etc…
Use Digital Twins to capture dynamics make decisions.
A Digital Twin (DT) is a high-fidelity, computational representation of a physical system, enriched with real-time data, that enables the “what-if” analysis, prediction, and optimisation across its life-cycle.

## Slide 5: Developing a GIS-based Digital Twin for DBPs
GIS and assets model
Hydraulic modelling and calibration using sensors
Development of a multi-species water quality model based on literature
Quality sensor calibration using sampling data
Quality model calibration using sensor data and DBP formation potential
Spatial model calibration using additional sampling locations
Development of a multi-parameter model for improved predictions
From QGIS to EPANET Models
Calibrating EPANET Models with real data
Managing real sensor data and sampling results
Calibrating models for simulations

## Slide 6
Adapted from (Evlampidou, 2020)
CS1-LIMASSOL (CYPRUS)
high variability of source water and quality and high formation of THMs.
CS2- BARCELONA (SPAIN)
high THMs formation potential in distributed water and changing conditions in the source reservoirs. High concentration of bromide in drinking water sources.
CS3- MADRID (SPAIN)
possible formation of Nitrogenous-DBPs from generation of chloramines
CS4- Co. MAYO (IRELAND)
high formation of THMs from peatland dominated catchments. EU infringement for unsafe drinking water.

## Slide 7
1
1
2
3
4
2
4
3
DWTP
1
2
Zone 2 Tank
3
DMA Inlet
4
DMA DP 3
Limassol Pilot
Desalinated
water input

## Slide 8: Optimal sensor placement and manual sampling plan
1
2
3
4
Define optimization problem
Nodes that are not affected by reverse flows in the network
Cover as much of the network as possible with minimum overlaps with the other sensors

## Slide 9
DWTP
1

## Slide 10: Modeling tool to predict DBP formation
Pavlou P, Kyriakou M, Vrachimis SG, Eliades DG. “A Comprehensive Virtual Testbed for Modeling Disinfection Byproduct Formation in Water Distribution Networks”. Engineering Proceedings. 2024; 69(1):33. https://doi.org/10.3390/engproc2024069033
Researchers/practitioners/operators can evaluate variations in:
Reaction models
  Multiple species
  Reaction coefficients
Hydraulic conditions
  Demands
  Sources
Control actions and mitigation strategies:
  Valve/pump
  Network reconfiguration
  Booster station disinfection scheduling

## Slide 11
Multi-species model:
Chlorine (Cl)
Total organic carbon (TOC)
  Slow reducing agent
  Fast reducing agent
Trihalomethanes (THM)
Halo-acetic Acids (HAA)
Example application scenario
Scenario uncertainty considered:
Ratio of water acquired from each source (affecting TOC)
Chlorine inserted to the system
THM Yield coefficient - YTHM
HAA Yield coefficient - YHAA
Scenario configuration (set as in real system):
7- day simulation period
Chlorination input at sources (desalination, DWTP) and re-chlorination tank

## Slide 12
THM and HAA prediction
Scenario uncertainty bounds:
CTOC [0.8 - 1.2] mg/L
CCl [0.2 - 0.5] mg/L
YTHM [30 – 180] μg-HAA/mg-CL
YHAA [15 – 35] μg-HAA/mg-CL
THM
HAA
THM and HAA prediction

## Slide 13
Maximum concentration per node
Maximum concentration per node

## Slide 14
Plugin
Mechanistic models and data
Scenario builder
Scenario simulator
Interactive map
Results explorer

## Slide 16
10 20 30
Effect of temperature variations

## Slide 17
*Model mismatch possibly due to hydraulics

## Slide 18: Conclusions & Discussion
The risk DBP is increasing, and there are many unknowns
Accurate data for online monitoring of DBPs is a challenge
Digital Twins, coupled with GIS and Sensor/Sampling data, can help answer operational and policy questions
Model calibration requires good sampling data
Intervals are suitable for handling uncertainties

## Slide 19: Demetrios Eliades
eldemet@ucy.ac.cy