## Slide 1
Precise Estimation of Snow Water Equivalent with GPS and Galileo measurements
Patrick Henkel, Markus Lamm and Franziska Koch

## Slide 2
Snow Monitoring Applications

## Slide 3
GNSS-based Snow Monitoring at Zugspitzplatt (2420 m)
GPS + Galileo

## Slide 4
GNSS-based SWE estimates at Zugspitzplatt (2420 m) in winter 2024/ 2025
3 months without almost any precipitation
early snowfall event in September

## Slide 5
Continuous monitoring through Kalman filter
Single epoch float solution
Kalman filter
based fixed solution
Fast convergence

## Slide 6
snow
GNSS antenna below snow
 Signal attenuation due to snow, mainly due to Liquid Water Content (LWC)
 Snow-induced time delay due to reduced speed of signal propagation in snow
 Refraction at air-snow interface according to Snell‘s law
GNSS reference antenna
Physical Effects of Snow on GPS + Galileo Signals

## Slide 7
Double differenced carrier phase measurement between two GNSS receivers and two satellites:
Relative position („baseline“) between both GNSS receivers
Snow Water Equivalent (SWE)
Integer Ambiguity
Modeling of GNSS measurements

## Slide 8
Stacking measurements from all satellites gives:
Double differenced carrier phase measurement between two GNSS receivers and two satellites:
Rank-defect by 1. Consideration of time series of measurements needed to obtain full-rank system of equations.
Modeling of GNSS measurements

## Slide 9
Snow-free day
Measurement basis – GNSS carrier phases

## Slide 10
Snow-free day
Measurement basis – GNSS carrier phases

## Slide 11
Snow Parameter Estimation
Kalman filter based estimation of SWE and float ambiguities
Integer ambiguity fixing with LAMBDA method
Least-squares adjustment of SWE estimates
Determination of snow height/ depth and LWC
Calibration: RTK positioning at a snow-free time.
Joint estimation of relative position between both GNSS antennas and carrier phase double difference ambiguities
GNSS-based Snow Parameter Estimation

## Slide 12
Consideration of both dry and wet snow conditions
References: Henkel et al., 2018 (IEEE Transactions on Geoscience and Remote Sensing) and Koch et al., 2019 (Water Resources Research)

## Slide 13
ANavS Snow Monitoring Station
GPS + Galileo
- Easy to carry and install by a single person
- Completely autonomous operation with solar power & satellite communication
- No foundation required
- No flat ground required

## Slide 14: Contact data
Advanced Navigation Solutions
ANavS GmbH Gotthardstraße 40 80686 München Germany
Managing directors: Dr.-Ing. habil. Patrick Henkel and Andreas Sperl Phone number: +49 - (0)89 - 890567 - 21 Emails: patrick.henkel@anavs.de patrick.henkel@anavs-sensor-tech.at Web: www.anavs.com
We are the Collaborative Change Makers.
ANavS Sensor Technologies GmbH Weißstraße 9 6112 Wattens Austria