## Slide 1
Department of Environmental Engineering, Anyang University, Anyang, Gyeonggi, Republic of Korea
Hui-Jeong Lim
A Study on the Seasonal Correlation between O₃ and PM2.5 in Seoul

## Slide 2
Ⅰ Introduction
Table of Contents
Ⅱ Theoretical Background
Ⅳ Results and Discussion
Ⅴ Conclusion
Ⅲ Data and Methods

## Slide 3
Ⅰ. Introduction
Using Python for data processing and correlation analysis, we analyze the relationship between O₃ and fine particulate matter (PM2.5)
The results are compared seasonally.
Investigate the seasonal correlation
between O₃ and PM2.5
in Seoul from 2015 to 2023.
2. Research Purpose
Enhance the understanding of air quality changes.
Contribute to environmental policy-making.
3. Introduction to methodology
1. Background
Air pollution significantly impacts human health and the environment.
O₃ and fine particulate matter (PM2.5) in Seoul have considerable effects on health and the environment, with their concentrations varying by season.
Understanding seasonal air quality variations in Seoul is crucial.

## Slide 4
Ⅱ. Theoretical Background
1. PM2.5
Definition: PM2.5 refers to ultrafine particulate matter with a diameter of 2.5 µm or less.
Composition
            Primary particles: Naturally occurring elemental components, fuel combustion emissions, primary organic matter (POM), and elemental carbon (EC).
            Secondary particles: Ionic components (SO₄²⁻, NO₃⁻, NH₄⁺), secondary organic matter (SOM).
            Health Effects: WHO Group 1 Carcinogen, Causes Respiratory and Cardiovascular Diseases.
Role of O₃: Facilitates the mechanism by which NOx and VOCs convert into PM2.5.
Oxidation reaction: Plays a crucial role in the formation of secondary organic aerosols (SOA).
3. Effect of PM2.5 on O₃
Surface heterogeneous reaction: Influences tropospheric O₃ formation.
Suppression effects
Summer: PM2.5 absorbs radicals, suppressing O₃ formation (Li et al., 2019)
High aerosol concentrations: Weaken light transmittance, reducing O₃ production
(Feng et al., 2016; Li et al., 2011)
Winter: High concentrations of PM2.5 block solar radiation, decreasing O₃ (Jia et al., 2017)
Current status: Limitations of managing O₃ and PM2.5 separately (Seoul Institute, 2018)
Necessity: Integrated management strategy and control of VOCs and Nox
Research objective: To analyze the seasonal correlation between O₃ and PM₂.₅ concentrations in Seoul (2015–2023)
2. Chemical behavior of O₃ and PM2.5
in the atmosphere
4. Seasonal Management Strategies

## Slide 5
Ⅲ. Data and Methodology
1. Data source
Urban air monitoring network data from 25 districts in Seoul
Hourly data from January 1, 2015, 01:00 to December 31, 2023, 24:00
Analysis of concentrations of O₃, PM2.5, and NO₂
PM2.5 and NO₂: Hourly average data for each district, used as daily average concentrations
O₃: 8-hour average (MDA8) used as daily average concentration
Monthly average concentrations and correlation coefficients among O₃, PM2.5, and NO₂: Calculated monthly using daily average data by district
KMA Automated Synoptic Observing System (ASOS)
2015–2023, Seoul (37°57′N, 126°97′E) Solar radiation and cloud cover data
Air pollutant measurement
data
2. Methodology
Conducting Pearson bivariate correlation analysis using Python
Analysis of the correlation between O₃ and fine dust using Pearson correlation analysis or multiple regression analysis
Research period: Seasonal data (spring, summer, autumn, and winter) from 2015 to 2023 were used(Each measurement was included in the analysis only if the proportion of valid data exceeded 75%)
Cloud cover: Expressed as the percentage (%) of the sky covered by clouds, based on the entire sky being 100% at the observation site.
Hourly solar radiation data: The total amount of radiation energy received per unit area over one hour (MJ/m²).
Meteorological
Data

## Slide 6
Ⅳ. Results and Discussion
T
1. Seasonal Distribution and Correlation of O₃ and PM2.5 Concentrations
Monthly Distribution of O₃ and PM2.5 Concentrations
  Concentrations increase during spring and summer when sunlight is strong,
Tend to decrease in winter
  Increased fuel consumption and prevailing northwesterly winds lead to higher concentrations in spring and winter.
  Increased precipitation causes a decrease in summer concentrations.
  (Both O₃ and PM2.5 drop sharply in August due to rainfall.)
O₃
PM2.5
[Figure 1] Monthly variation of averaged maximum daily 8-hour O₃ and PM2.5 in Seoul during from 2015 to 2023.

## Slide 7
Ⅳ. Results and Discussion
2. Correlation between PM2.5 and O₃ in Seoul
Positive correlations in all districts from March to September
Strong correlations in summer (Jun–Aug): 0.50–0.69 with low variability
Negative correlations in winter (Jan, Feb, Dec): –0.32 to 0.04
  This analysis identifies key factors driving seasonal differences in O₃–PM2.5 correlation between summer (June–August) and winter (January, February, December)
O₃–PM2.5 Correlation Analysis
Seasonal patterns are distinct
Winter: Negative correlation (O₃↓, PM2.5↑)
Summer: Strong positive correlation (Both ↑)
Potential for photochemical smog in summer
Uncertainty in Feb & Oct
→ high correlation variability
[Figure 1] Monthly Pearson correlation coefficients (p < 0.01) between PM2.5 and O₃_MDA8 in Seoul

## Slide 8
Ⅳ. Results and Discussion
4. Correlation Characteristics Between O₃ and PM2.5 During Summer
To assess the impact of secondary formation, we analyzed the relationship between Ox (O₃ + NO₂) and PM2.5 during summer in Seoul.
Monthly Correlations (O₃ vs PM2.5):
            june: r = 0.50
            July: r = 0.69 (strongest)
            August: r = 0.60
The scatter plot shows a strong positive correlation between Ox and PM2.5 in July (r = 0.69).
Conclusion:→ Atmospheric oxidative capacity has a significant influence on the secondary formation of PM2.5 during summer.
[Figure 3] Scatter plot and correlation (p < 0.01) between PM2.5 and Ox in Seoul (June–August, all years)

## Slide 9
Ⅳ. Results and Discussion
5. Characteristics of the Correlation Between O₃ and PM2.5 in Winter
In winter, High PM2.5 → Less solar radiation, more cloud cover
Leads to reduced O₃ formation
In Seoul winter:
→ Peak solar radiation drops sharply with higher PM2.5
→ Cloud cover increases throughout the day
O₃ suppression is strongest during midday hours
1) Assessment of PM2.5's Suppressive Effect on O₃ Production
[그림4] Diurnal change of (a) Solar radiation and (b) Cloud cover under three PM2.5 levels over 16~36 µg/m3, 36~75 µg/m3 and exceeding 76 µg/m3 during winter in Seoul, from 2015 to 2023.
Chart: (b) Cloud cover
| 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
16 µg/m3≤PM2.5<36 µg/m3 | 36.0247 | 37.1845 | 40.4712 | 36.9192 | 38.209 | 39.2822 | 42.6385 | 44.9215 | 41.7277 | 39.675 | 39.359
36 µg/m3≤ PM2.5<76 µg/m3 | 49.5376 | 46.1053 | 44.3814 | 45.2857 | 47.7941 | 54.7739 | 53.8122 | 50.8876 | 51.871 | 51.3014 | 52.4476
76 µg/m3≤PM2.5 | 64.6154 | 71.25 | 66.8421 | 56.5517 | 65.8333 | 72.1053 | 61.4286 | 55.625 | 59.4118 | 63 | 61.25
Chart: (a) Solar radiation
| 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
16 µg/m3≤PM2.5<36 µg/m3 | 0.021838 | 0.28555 | 0.70865 | 1.1463 | 1.414 | 1.5314 | 1.4195 | 1.1427 | 0.80249 | 0.40879 | 0.084721
36 µg/m3≤ PM2.5<76 µg/m3 | 0.017371 | 0.24819 | 0.65675 | 1.039 | 1.3095 | 1.3312 | 1.2385 | 1.0516 | 0.70667 | 0.35726 | 0.078472
76 µg/m3≤PM2.5 | 0.01 | 0.15937 | 0.51895 | 0.99552 | 1.0562 | 1.1168 | 1.0705 | 0.83625 | 0.53059 | 0.2655 | 0.026875

## Slide 10
Ⅳ. Results and Discussion
5. Wintertime Correlation Between O₃ and PM2.5 (Jan, Feb, Dec)
O₃ Formation, Destruction
O₃ is formed and destroyed through the
photolysis cycle of NO₂.
In the presence of VOCs, O₃ concentration
increases.
The response of O₃ depends
on the VOC/NOx ratio:
NOx-limited regime (high VOCs/NOx):
→ O₃ increases with NO, little effect from VOCs.
VOCs-limited regime (low VOCs/NOx):
→ O₃ increases with VOCs, decreases with NOx.
→ The Seoul Metropolitan Area tends toward a
VOCs-limited regime, so increasing NOx can reduce
O₃ production efficiency.
NOx and PM2.5:
→ NOx contributes to PM2.5 formation.
→ Due to limited NO data, NO₂ is used as a proxy.
Winter 2015~2023 Observations (Seoul):
NO₂ and O₃: Strong negative correlation (r = -0.81).
NO₂ and PM2.5: Positive correlation(r = 0.59).
High NO₂ concentrations → lower O₃,
higher PM2.5
O₃fect of NOx on O₃ Suppression
Correlation of
daily averaged
concentration of
NO2 with
(a) O₃ and
(b) PM2.5
during winter
in Seoul, from 2015 to 2023
(confidence
level of 99%).

## Slide 11
Ⅳ. Results and Discussion
5. Wintertime Correlation Between O₃ and PM2.5 (Jan, Feb, Dec)
Key Factors: NOx and PM2.5
Correlation Analysis
O₃ vs NO₂: Strong negative correlation (r = -0.56 to -0.69)
O₃ vs PM2.5: Weak negative correlation (r = -0.05 to -0.31)
In winter, NOx has a greater impact on O₃ reduction than PM2.5.
Compared to findings from China, the influence of PM2.5 on O₃ formation in Seoul appears to be relatively minor.
The O₃-suppressing effect of NOx plays a more significant role.
3) Comparative Influence of NOx and PM2.5 on O₃ During Winter
In Seoul’s winter, NOx is a key factor in O₃ reduction.
Correlation coefficient of O₃ with PM2.5 and NO2
(confidence level of 99%) during winter in Seoul, 2015~2023.
 | Jan | Feb | Dec
O₃-PM2.5 | -0.25 | -0. 19 | -0.36
O₃-NO2 | -0.84 | -0.81 | -0.83

## Slide 12
Ⅴ. Conclusion
Seasonal Correlation Between O₃ and PM2.5
Study Overview
  Analysis of O₃ and PM2.5 concentrations in 25 districts of Seoul from 2015 to 2023
  Period : 2015.01.01 ~ 2023.12.31
Correlation Coefficients
  Summer: Strong positive correlation between O₃ and PM2.5 (average r = 0.60)
  Winter: Negative correlation between O₃ and PM2.5 (average r = -0.37)
Cause Analysis
  Summer: High solar radiation → More O₃ → Enhanced atmospheric oxidation → Promotes secondary PM2.5 formation
  Winter: O₃ suppression by NOx > Solar radiation blocking effect by PM2.5
Conclusion
  The interaction between O₃ and PM2.5 varies by season due to different meteorological conditions
  Seasonal strategies are needed for effective air quality management