## Slide 1: Modeling Seismic Hazard and Landslide Occurrence Probabilities in Northwestern Yunnan, China: Exploring Complex Fault Systems with multi-segment rupturing in a Block Rotational Tectonic Zone
Jia Cheng, Chong Xu, Xiwei Xu
China University of Geosciences, Beijing
Vienna, 2025-04-28

## Slide 2
Gan et al., 2007
The Northwestern Yunnan Region, is characterized by a combination of low-crustal flow and gravitational collapse, giving rise to a complex network of active faults.
NE- and SW- trending faults coexist
Clockwise rotation and SE extrusion of the crust
Introduction
NE-trending faults
SW-trending faults

## Slide 3
Strong Historical earthquakes frequently ruptured in this region.
Introduction
1996-02-03 Ms7.0 Earthquake occurred near Lijiang Area

## Slide 4
Seismic landslide hazard:
Huang et al., 2021, Earth Science Frontiers
Landslide accomplice with the seismogenic fault of the 1515 Yongsheng M7.8 EQ
Introduction
This area also has frequent landslides, with high mountains, steep slopes, abundant water and loose soil.
Active crustal movement
Unique monsoon climate with heavy rainfall
Complex geological structure
fragile ecological environment
diverse local climate background

## Slide 5
Seismic Source Model: we applied the method of SHERIFs (Chartier et al. 2017) to simulate the occurrence rate of multi-segment rupturing, align with the fault slip rate, fault segmentation, historical earthquake occurrence rates, and the recurrence intervals of historical and paleo-earthquake events.
Chartier et al., 2017,NHESS
Multi-segment Seismic Hazard Modeling
Cheng et al., 2017, BSSA
SW Yunnan Region

## Slide 6
Introduction
Geological data and Slip rates
Rupture combination considering Quaternary Basins
A fault segmentation and rupture combination model to characterize seismic sources.

## Slide 7
Harris and Day, 1993
Harris and Day, 1999
Numerical simulations: A 5+ km width step-over could stop rupture process
Multi-segment Seismic Hazard Modeling
Strike-difference of > 30° can stop the multi-segment rupture.
historical rupture data: >30° can stop the rupture
Stress field study : similar results, but should also consider the background stress field
Mignan et al., 2015
Biasi and Wesnousky, 2017
Two factors can stop the rupture to be a multi-segment event.

## Slide 8
Simulation of the seismicity rates
Multi-segment in individual fault
Normal slip of the YLF
(F15-F16)
F30-F35, the strike-slip of LQ-Fault
F4-F10 with F11-F14
(2023 M7.8 Turkey EQ)
Chartier et al., 2019
NMS (non-mainshock slip) ratio ≤30–40%
was used for judging the reasonableness of the rupture combination models
Comparison of modeled and historical seismicity rates
Multi-segment Seismic Hazard Modeling
Four multi-segment rupture combination model

## Slide 9
Calculation of the PGA values, considering the amplification effect of site conditions.
Multi-segment Seismic Hazard Modeling
Chen et al., 2021
PGA distribution with selected GMPEs
(10% PE in 50 yr)
Site amplification of rock types

## Slide 10
Our results
National Seismic Hazard Map of China
Comparison with our PGA distribution of Nation Seismic Hazard Map
(10% probability of exceedance in 50 years)
Multi-segment Seismic Hazard Modeling

## Slide 11
历史
历史
11
Xu et al., 2012
The 15 types of sample densities are randomly selected in the study area, and each repeated calculation 200 times to ensure that there is no abnormal impact of sample selection.
Probabilistic Seismic Landslide Hazard Assessment
Machine Learning - Logistic Regression
Landslides
Slope angle
Slope aspect
TWI
PGA
Epicenter
River Network
Road
Lithology
Precipitation
Notes: We use Machine learning – logistic regression to do probabilistic seismic landslide hazard assessment. The parameters includes topography, geology ,earthquake, hydrology and other factors.

## Slide 12
Landslide occurrence probabilities under PGA distribution.
Probabilistic Seismic Landslide Hazard Assessment
PGA distribution
Landslide Occurrence Probabilities

## Slide 13
Our multi-segment rupture source model is consistent with the microplate rotational model.
Wang et al., 1998,
GSA Special Paper
Tectonic and strata
data
Multi-segment rupture combination
Microplate rotational model
Conclusion

## Slide 14
Rangin et al., 2013, JAES
This Micro-plate rotation is driven by the gravitational collapse, causing the upper crust to move westward faster than the lower crust.
Micro-plate rotation model
Conclusion
Dynamic sources

## Slide 15
We used the simulation method in the SHERIFS code to calculate seismicity rates for both single-segment and multi-segment ruptures. Our results show that multi-segment ruptures occur only within individual faults in the NW Yunnan Region.
We also provided valuable insights into the seismic hazards present in the NWYR, and generated a more comprehensive assessment of seismic hazards and landslide probabilities, considering both the fault slip behavior and site condition map.
Our multi-segment rupture source model aligns with the rotational motion of regional micro-blocks, driven by lower crustal flow and gravitational collapse along the southeastern margin of the Tibetan Plateau, reflecting both tectonic implications and fault activities.
Conclusion

## Slide 16
Reference：
Cheng et al. 2025. Modeling seismic hazard and landslide occurrence probabilities in northwestern Yunnan,
China: exploring complex fault systems with multi-segment rupturing in a block rotational tectonic
zone. Natural Hazards and Earth System Sciences, 25, 857-877, doi:10.5194/nhess-25-857-2025.
Cheng et al. 2023. From Active Fault Segmentation to Risks of Earthquake Hazards and Property and Life
Losses – A Case Study from the Xianshuihe-Xiaojiang Fault Zone. Science China Earth Sciences,
66(6): 1345-1364.
Cheng and Chartier, et al. 2021. Multisegment Rupture Hazard Modeling along the Xianshuihe Fault Zone,
Southeastern Tibetan Plateau. Seismological Research Letters, 92(2A), 951-964.
Cheng et al. 2021. Probabilistic multi-segment rupture seismic hazard along the Xiaojiang fault zone,
southeastern Tibetan Plateau. Journal of Asian Earth Sciences, 221, doi: 10.1016/j.jseaes.2021.104940.
Chartier T, Scotti O, Lyon-Caen H, Boiselet A. 2017. Methodology for earthquake rupture rate estimates of
fault networks: example for the western Corinth rift, Greece. Nat Hazards Earth Syst Sci, 17:1857-1869.
Chartier T, Scotti O, Lyon-Caen H. 2019. SHERIFS: Open-Source code for computing earthquake rates in
fault systems and constructing hazard models. Seismol Res Lett, 90:1678-1688.

## Slide 17
Thanks for your attention!

## Slide 18
Cheng et al., 2012, Chinese J. Geophys
GPS velocity observations and S-wave velocity imaging both indicate that this region may be a lower crustal flow channel.
Introduction
Zhang et al., 2021, Science China
GPS velocity field after removing overall (block) motion
Vs velocity field
Extensional
Crustal
deformation
Low
Crustal
flow

## Slide 19
GMPEs的选取
Dangkua, et al., 2017, BSSA
Abrahamson, Silva, and Kamai (2014)
Chiou and Youngs (2014)
Campbell and Bozorgnia (2014)
Boore et al. (2014) branches.
Each branch was assigned the same weight of 0.25
We used logic Tree model of 4 branches.
PGA calculation with GMPEs
Multi-segment Seismic Hazard Modeling