## Slide 1: Landslide topography interpretation technology using deep learning research on improvement
Research & Development Center NIPPON KOEI CO.,LTD
Hirokazu FURUKI
Presentation materials for my doctoral thesis.
The repository for the thesis can be accessed using the QR code below.
Prior studies for the 2025 EGU publication

## Slide 2
Chapter1
Conception, first try, and verification

## Slide 3: Introduction to AI (deep learning)
type | Data | method | Advantages/disadvantages
Supervised learning | With Label (with correct answer) | ◆Automatically analyze data with correct answers to the machine ◆Learning the relationship between the features captured by the machine and the features of the correct data | ◆Efficient for classification problems. ◆It takes time to prepare a huge amount of labeled data
Unsupervised learning | No label | ◆ Automatically analyze a huge amount of data ◆ Since there is no correct answer, we derive structures, laws, trends, classifications, definitions, etc. from the calculated features. | ◆ Since the machine itself discovers characteristics and definitions, if there is a huge amount of data, there is no need or effort to prepare labeled data.
Reinforcement learning | none※ | updates its own actions and evaluations ◆ Maximizes the results and value of a continuous series of actions | * There is no correct answer, but it is necessary to set rewards (points and wins). "Examples: Go, Shogi, Autonomous Driving"
■Types of machine learning
◆Use supervised learning*
*In this presentation, supervised deep learning will be referred to as "AI"

## Slide 4: Idea of ​​applying AI (deep learning) to interpretation technology
Generate photos from mosaics with Pix2pix
Generate maps from aerial photos
※Isola, P., Zhu, JT., Zhou, T. and Efros, AA. （2017）： Image-To-Image Translation With Conditional Adversarial Networks, Proceedings of the IEEE conference on computer vision and pattern recognition. pp. 5967-5976.
■What I want AI to remember
⇒Learn the tacit knowledge of civil engineers
*Using deep learning to learn how to diagnose and interpret intuitively by looking at “photos” and “diagrams”
Ex. “pix2pix” *
◆Input as an image ⇒ Output as an image ⇒ Intuitive to use
◆You can learn the results that technicians are seeing and diagnosing
■Machine learning environment (implemented on a general PC)
Framework: Tensorflow (google)*
OS: Windows10
GPU: NVIDIA RTX2080
Frameworks required for deep learning
Use freely available libraries (programs) (from the perspective of versatility)

## Slide 5: Flow of applying terrain interpretation to deep learning
Flow of research in this thesis
The idea of applying AI for image generation to decipherment
application
Advantages of AI: Output is several tens of seconds - minutes
Application example for general images
Input
Output
Correct image
mosaic image
Example of application to landslide topography interpretation
■Generate photos from mosaic images with pix2pix ⇒ Application to landslide topography interpretation
topographic map
Generate (convert) images
AI generated image
real photo
Landslide topographic image generation using AI = Interpretation map
Landslide topography interpretation map
3D topographic information(DEM)
Deep learning
Train Data
Test Data
Unidentified
Data Input
Expert decipherment
(tacit knowledge)
Test and Evaluation
CS 3D map etc.
Landslide predicted by AI
Inference
Terrain information
(color tone/pattern)

## Slide 6: Survey location and creation of CS map
5km
◆Uses the digital elevation model (5m mesh) of Geospatial Information Authority of Japan basic map information
◆Created with GIS software plug-in
◆The coloring has been changed to a color tone that is easier to see in three dimensions from the reader's perspective
Nara Pref.
Study area
1km
37km
23km
Test data area
3/4 Off Set
Train data area

## Slide 7: Creation of multiple types of topographic representation maps
Contour map
Inclination map
CS 3D map
※Scale Bar = 500ｍ
1bit
8bit
24bit
Amount of color
information
△
○
◎
Legibility
◆Differences in the amount of information and landslide representation for each topographic map
(Top: topographic map, bottom: image with landslide topographic distribution map superimposed on the topographic map)
◆The more color information there is, the easier it is for readers to read (Is AI learning the same or different?)

## Slide 8: Incorporating engineer knowledge into Train data
Landslide topographic distribution map
Landslide topographic distribution map GIS polygons
Train data
Moving only As notation It was used as training data
There is a sliding cliff at the back, and the outline of the moving object is clear and can be judged
The sliding cliff behind is clear, but it is difficult to determine the outline of the moving object
Most of the cliffs have been opened, but some of the moving bodies of the past remain
NIED(Japan) 1:50,000 Partial addition to landslide topographic distribution map legend
Focusing on the clarity of the contours and boundaries of moving objects

## Slide 9: Creation of multiple types of topographic representation maps
originality
Contour Map
Inclination Map
CS 3D Map
500ｍ
500ｍ
500ｍ
500ｍ
500ｍ
500ｍ
◆Differences in the amount of information and landslide representation for each topographic map
(Top: topographic map, bottom: image with landslide topographic distribution map superimposed on the topographic map)
◆The more color information there is, the easier it is for readers to read (Is AI learning the same or different?)
Contour map
Image B
Image A
Landslide moving body
Image B
Image A
CS 3D map
Contour map
CS Sharpening
Train・Correct data image example
color’s information | 1bit | 2bit | 24bit
legibility | △ | ○ | ◎

## Slide 10: Data used for learning
Train data and number of verification data
◆Engineers look at the images to be trained and select only the necessary images.
★The “feature acquisition” mentioned in the AI ​​overview is from “a large amount of messy data”
★Deep learning is possible with "quality over quantity" for targets where the amount of data is limited, such as disaster phenomena.
topographic map | Train Data |  |  |  | Test Data
 | original | data expansion | After expansion | Number of data after sorting | 
Contour Map | 600 | slides | 2000 | 1000 | 80
Inclination Map |  |  |  |  | 
CS 3D Map |  |  |  |  | 
CS Sharpening |  |  |  |  | 

## Slide 11
Chapter2
Evaluation of landslide topography interpretation AI

## Slide 12: Key points of the results of landslide topography interpretation using AI
■Learn landslide topography displayed in color. Expert knowledge required.
originality
input
output
target
input
output
target
input
output
target
1. No Train data selection, no image processing
2. Train data selection/image sharpening
3. Train data selection and sharpening processing
Output is several tens of seconds to several minutes
Topography to focus on when sorting
Landslide area is out of frame
Image does not contain landslides
Sliding Cliff
Landslide moving body
Landslide moving body
DELETE
Sliding Cliff
Landslide Body
Head gentle slope
[Number of teacher data]
◆Before sorting: Approx. 2300*1
◆After sorting: Approximately 1000
Improved accuracy even with less data
⇒ Expert knowledge is required to create Train data
[When writing the paper in *1]
Hirokazu Furuki, Yutaka Inagaki, Masayuki Hitoto, Dai Fujihira, Tomomi Sakuramoto: Automatic extraction of landslide topography using deep learning - Relationship between accuracy and training data, Journal of the Japanese Society of Geotechnical Engineering, Vol. 67, No. 6, p. 20-23, 2019
Example of landslide topography on CS3Dmap

## Slide 13: Sorting Train data (before sorting)
■Before sorting: 150 out of about 2000. There are many blank areas in image B. Images deleted during sorting

## Slide 14: AI generate Landslide areas movie

## Slide 15: [Implementation results] Input image
1km

## Slide 16: [Implementation results] Correct answer example - Landslide topography distribution map
1km

## Slide 17: [Implementation results] AI interpretation diagram
1km
Inference
Size of one image
It takes about 5 minutes to output and synthesize
It would take an engineer about 1 to 2 hours to decipher this area.

## Slide 18: Evaluation indicators for implementation results
matching part
Parts that AI overlooks
Parts that AI extracts excessively
Input
AI generated image
Landslide topographic distribution map
(Correct answer data)
Recall rate = matched area / (matched area + unreadable area)……(1)
Precision rate = matching area / (matching area + misinterpretation area)…………(2)
◆How well does the AI ​​extract (match) the correct answers without omission?
◆The higher the value (closer to 1), the less leakage.
◆How much does AI overreact to correct answers?
◆The higher the value (closer to 1), the less excessive image generation occurs.
Match
Match
Leak
Recall Rate =
Excess
Match
Match
Precision rate=

## Slide 19: Examination result example 1
Input
Contour Map
AI generated image
Inclination Map
CS 3D Map
CS Sharpening
Landslide topographic distribution map
(Correct answer data)
Example of an image with a high extraction rate of landslide moving objects (1)
Example of an image with a high extraction rate of landslide moving objects (2)
Input
Contour Map
AI generated image
Inclination Map
CS 3D Map
CS Sharpening
Landslide topographic distribution map
(Correct answer data)

## Slide 20: Examination result example 2
Contour Map
AI generated image
Input
Inclination Map
CS 3D Map
CS Sharpening
Landslide topographic distribution map
(Correct answer data)
Input
Contour Map
AI generated image
Inclination Map
CS 3D Map
CS Sharpening
Landslide topographic distribution map
(Correct answer data)
Example of an image with a low extraction rate (Landslide terrain included in the correct answer)
Example of an image with a low extraction rate (no landslide image in the correct answer)

## Slide 21: Example of matching correct data and AI extracted image for evaluation
Input
Input
AI generated image
AI generated image
Landslide topographic distribution map (correct data)
Landslide topographic distribution map (correct data)

## Slide 22: Verification result list ~ Performance of landslide topography interpretation AI
AI landslide extraction rate calculated on a part-by-point basis |  |  |  |  |  |  |  | 
Type of topographic map | Matches the engineer's prior interpretation of the location |  |  | AI over-detected |  | AI Landslide Number of extracted area (2)＋(3) | Total number of AI extraction area (2)＋(3)＋(4) | Probability that the AI extraction site is a landslide ((2)＋(3)) / ((2)＋(3)＋(4))
 | (1)Total number of landslides | (2)Number of matches between engineer's decipherment and AI extraction | Extraction rate（％） | (3)Polygons that engineers can determine to be landslides | (4)Determined not to be a landslide |  |  | 
contour map | 228 | 98 | 43.0% | 40 | 56 | 138 | 194 | 71.1%
Inclination map | 228 | 94 | 41.2% | 47 | 34 | 141 | 175 | 80.6%
CS map | 228 | 119 | 52.2% | 77 | 87 | 196 | 283 | 69.3%
Sharpening CS map | 228 | 125 | 54.8% | 84 | 51 | 209 | 260 | 80.4%
Match, recall, and precision calculated per pixel |  |  | 
Type of topographic map | Match rate | Recall rate | Precision rate
contour map | 0.08 | 0.11 | 0.24
Inclination map | 0.19 | 0.26 | 0.43
CS map | 0.15 | 0.27 | 0.22
Sharpening CS map | 0.20 | 0.33 | 0.26
■What you want is the location of the landslide
◆Pixel-by-pixel evaluation → No need to reproduce the shape
◆Evaluate by location → know the general landslide area
⇒70-80% of the locations identified by AI are landslide terrain

## Slide 23
Chapter3
Recommendations regarding landslide topograpic interpretation AI
◆Landslide moving object extraction using deep learning using 3D topographic information
Journal of the Japan Landslide Society (2021), Volume 58, Issue 2, p. 65-72.
◆Automatic extraction of landslide topography using deep learning - Relationship between accuracy and training data
Journal of Japan Geotechnical Engineering Society (2019), 67(6), pp.20-23.
◆Examination of annotation methods targeting a small number of phenomena in deep learning
Japan Society of Civil Engineers, Proceedings of AI and Data Science (2021), Volume 2, No. J2, pp.856-862.
◆Deep generation of landslide moving bodies by normalization processing regarding spatial heterogeneity and continuity
Japan Photogrammetry Society (2022), Vol. 61, No. 1, pp. 14-31.
◆Proposal of uncertainty evaluation and performance improvement method for image generation of landslide moving objects using deep learning model
Japan Photogrammetry Society (2022), Vol. 61, No. 6, pp. 368-386.

## Slide 24: Interpretation of matching results
◆Extraction rate improves in the order of contour line → slope map → CS 3D map
◆In other words, it is easy to read ⇒ Engineers and AI are the same in terms of being able to read accurately
◆The probability that the location extracted by AI is landslide terrain is approximately 80%
Chart: Number of AI extraction points and extraction rate for landslide topographic distribution map
| contour map | Inclination map | CS map | Sharpening CS map
②Number of matches between engineer's decipherment and AI extraction | 98 | 94 | 119 | 125
Extraction rate（％） | 0.42982 | 0.41228 | 0.52193 | 0.54825
(2)Number of matches between engineer’s decipherment and AI extraction
Chart: Number of landslide terrain locations extracted by AI and extraction probability
| contour map | Inclination map | CS map | Sharpening CS map
AI Landslide Number of extracted area ②＋③ | 138 | 141 | 196 | 209
Probability that the AI extraction site is a landslide （②＋③）／ （②＋③＋④） | 0.71134 | 0.80571 | 0.69258 | 0.80385
AI Landslide Number of extracted area (2) + (3)
Probability that the AI extraction site is a landslide ((2) + (3)) ／ ((2) + (3) + (4))

## Slide 25: Characteristics of misinterpreted images - problem extraction
Contour Map
Inclination Map
CS 3D Map
CS Sharpening
▲：Missing part of reading
★：Misreading part
Input
AI generated image
Landslide topographic distribution map
(Correct answer data)
[★Misinterpretation points]... Locations where the positional relationship and color tone of the top of an alluvial fan, a meandering river, and a slope between a sliding cliff and a gentle slope in a landslide topography are similar, such as the surface of a terrace.
[▲Characteristics of poorly readable areas]...Topography that even engineers are confused about ⇒Landslide topography that is unclear in the legend of the landslide topography distribution map
Example: A falling cliff is clear, but a gentle slope, slope line, slope line is not clear, etc.

## Slide 26: Proposed measures to solve problems
■Solutions to reduce misinterpretation
(1) Expand the variety of interpretation data
◆The topographical patterns to be interpreted tend to have similar morphological characteristics depending on the region and geology.
◆If we can accumulate and learn from the knowledge of civil engineering engineers who make a living by interpreting, it is possible to improve accuracy and reduce misinterpretation.
(2) Let AI learn the features of the terrain that were misinterpreted
◆Let AI learn terrain that is not landslide terrain
◆However, future verification is required in order to apply it to regions and topographical elements where it is difficult to determine the true correct answer due to natural phenomena.
(3) Use detailed topographical information
◆Use more detailed terrain information. It is necessary to specify the landslide range more clearly.
◆Example of high-resolution topographic data: 0.5-1m mesh topographic data is released by local governments.
The Geospatial Information Authority of Japan also announced that it will release 1m mesh resolution topographical data nationwide on October 28, 2020.
(4) Add processing such as emphasizing the features (color tone) that engineers focus on

## Slide 27: Improving terrain interpretation technology through deep learning: Improving efficiency, awareness, and passing on technology
Conventional method
Terrain interpretation AI construction
wide area terrain
Interpretation diagram completed
Preliminary learning
Information acquired by sensors (SAR, etc.)
Area monitoring
Wide area and high precision
Interpretation work possible
Automatic reading
Creating and checking topographical
interpretation maps
Field survey
Acquisition of terrain data
period
technical
results
Check by technician
(On The Desk/Field)
High Quality Train Data
Teaching materials for technology inheritance
◆Application to other regions
◆Feedback to teacher data/topographic interpretation AI
Judgment assistance in combination with monitoring technology
Terrain interpretation AI
Ex. : satellite information
Terrain interpretation AI + α
Completed topographical interpretation map
Interpretation engineers spend several months interpreting and plotting
◆Improving the efficiency of interpretation
◆Preventing oversight
◆Engineer's awareness
Contents of interpretation technology
improved by AI
◆Speed ​​up
◆Reducing risks such as individuality and
human error
◆Supports high-resolution terrain data
◆Flexibility in updating terrain/teacher data
◆Versatility to other regions
◆Explanability by visualizing tacit knowledge
◆Use as a technology inheritance tool

## Slide 28: Example of deployment of terrain interpretation AI
Combining traditional Japanese technology (interpretation) with AI technology to pass on technology
Examples of overseas expansion
Seminar on terrain interpretation technology and terrain interpretation AI overseas
in Ecuador
June 2022-June 2023
in El Salvador
June 2023

## Slide 29: Recommendations regarding landslide topography interpretation AI
■Improve excellent conventional interpretation techniques with deep learning
◆Use of open source
◆Extract macro-scale “locations” of landslide terrain risk areas
◆pix2pix: Intuitive and versatile AI algorithm
◆Expert knowledge (tacit knowledge) can be deep learned
◆Technical knowledge is essential for teacher data
◆Landslide location extraction rate in target area: approximately 80%
◆Improvement in interpretation technology brought about by AI
1．Speed ​​up
2．Reduce risks such as individuality and human error
3．Supports high-resolution topographic data
4．Flexibility in updating terrain/teacher data
5．Versatility to other regions
6．Explainability by visualizing tacit knowledge
7．Utilization as a technology inheritance tool
Previously
Not 100%, but highly accurate
It takes about 10 days to interpret 100m2
Higher terrain resolution requires more time
Landslide topography interpretation AI
interpretation expertise
objectivity
Reduces misreading
Regional versatility
(Customization required)
Checked and added by someone
Focus on risk assessment
Can be output in a short time
Supports various terrain resolutions
Depends on each individual's ability, there is a risk of oversight, and updates require a lot of effort

## Slide 30: Recommendations regarding landslide topography interpretation AI
■Points to keep in mind and issues in utilizing AI
◆ This study utilizes the data accumulated so far and integrates the advantages of AI
◆AI is a tool and will always give an answer if data is input.
⇒Check function is required
◆ Sometimes there is no absolute right answer in Geoscience. ⇒Only experts can do it.
◆ Even so, the results predicted by AI are appealing (e.g., Risk assessment of ground interior).
◆Time saved by deep learning
Shouldn't the time saved by deep learning be used for further discussion?
existing methods
Desk Research
Field
Analysis/Tes
Result
What kind of output method?
What kind oあf data?
What about the procedures and format?
【Assignment】
◆Weaknesses of deep learning: black box remains ⇒ Control by quality of training data
◆ Verification of stability of inference accuracy and generalization performance
Combined use of sensor technology (e.g., satellites)